## Slide 1: On MinCR
JCTVC-P0044
Sony Corp.

## Slide 2: Overview
There are two aspects to this proposal:
  Potentially modify version 1 to increase MinCR for High Tier
  Change values in Annex A so that the indicated MinCR values are relevant at a given level for the RExt profiles.

## Slide 3: Change version 1 High Tier MinCr
For large pictures, e.g. 4K video, higher value of MinCR is used to reduce the worst case complexity of CABAC.
  For example, the value of MinCR is 8 for level 5.1 (4K@60p).
However MinCR=8 is too high for high end applications.
  When 4K@60p video is encoded at 160Mbps, this MinCR > 8 is often occurirng for the I picture.
Would it be possible to change the definition of the high tier so that the MinCR values are reduced?

## Slide 4: Changes to RExt profiles and levels
In the current text for RExt, intra profiles are defined and the MinCR can be reduced to 25% of the stated value in the level.
However, the MinCR is academic for intra profiles at a particular level as the bit rate is too low to allow the format targeted by the profile and levels to be compressed at MinCR.
  Eg Level 5.1, 4:2:0 8-bit 4K@60P high tier,
      maxLumaSampleRate = 534,773,760 samples/second
      maxBitRate = 160,000,000 bits/second
      baseBandBitRate = 534,773,760 * 1.5 [4:2:0] * 8 (bits/sample) = 6,417,285,120
    Sequence average compression ratio is (baseband bit rate / maximum bit rate) = 40:1
  For intra, it is likely that all frames will be compressed by the same amount.

## Slide 5: Changes to RExt profiles and levels
In addition, the CPB size defined for a level is no longer related to bit-rate.
  This means that for some profile and level combinations, the CPB cannot hold one frame of dimensions targeted by the level with the minimum compression ratio.
    Eg HD@30P 4:4:4 12-bit level 4.
Level 6.1 would have to be used to code HD@30P 4:4:4 12-bit at MinCR for all frames.

## Slide 6: Changes to RExt profiles and levels
Add a new super tier
  Selected by a flag in the profile_tier_level() syntax element.
  Super tier specifies higher MaxBR and MaxCPB values.
    4 times that of High tier, following a similar trend from Main to High.
    Note that even a factor of 4 is not always adequate to reach the target MinCRs, and therefore it is recommended that the binarization of the main/high/super tiers allow for extension of a super-high tier in the future.
Modify base values of CbpBrVclFactor and CbpNalVclFactor for RExt profiles to take maximum bit depth into account (not just chroma format)
  Though it is recommended that there is discussion on whether just the highest bit-depth profiles are altered.

## Slide 7: Notes for syntax change
Maximum bit rate is derived as follows:
  VCL HRD parameter: Max bit rate = CpbBrVclFactor * MaxBR
  NAL HRD parameter: Max bit rate = CpbBrNalFactor * MaxBR
MinCR is derived as follows:
  MinCR = MinCrBase * MinCrScaleFactor
HbrFactor is derived as follows:
  HbrFactor = 2 − general_lower_bit_rate_constraint_flag
where MaxBR and MinCrBase are defined in Table A-2, CpbBrVclFactor, CpbBrNalFactor, FormatCapabilityFactor and MinCrScaleFactor are defined in Table A-3.

## Slide 8: Syntax changes (1/4)
profile_tier_level( maxNumSubLayersMinus1 ) { | Descriptor
general_profile_space | u(2)
general_tier_flag | u(1)
general_profile_idc | u(5)
for( j = 0; j < 32; j++ ) | 
general_profile_compatibility_flag[ j ] | u(1)
general_progressive_source_flag | u(1)
general_interlaced_source_flag | u(1)
general_non_packed_constraint_flag | u(1)
general_frame_only_constraint_flag | u(1)
general_max_12bit_constraint_flag | u(1)
general_max_10bit_constraint_flag | u(1)
general_max_8bit_constraint_flag | u(1)
general_max_422chroma_constraint_flag | u(1)
general_max_420chroma_constraint_flag | u(1)
general_max_monochrome_constraint_flag | u(1)
general_intra_constraint_flag | u(1)
general_lower_bit_rate_constraint_flag | u(1)
general_super_tier_flag | u(1)
general_reserved_zero_35bits | u(35)
general_level_idc | u(8)
The value of general_super_tier_flag shall be 0 except when the value of general_tier_flag is 0. The value 1 of general_super_tier_flag when general_tier_flag is 1 is reserved for future use.

## Slide 9: Syntax changes (2/4)
Level | Max luma picture size MaxLumaPs (samples) | Max CPB size MaxCPB (1000 or 1100 bits) |  |  | Max slice segments per picture MaxSliceSegmentsPerPicture | Max # of tile rows MaxTileRows | Max # of tile columns MaxTileCols
 |  | Main tier | High tier | Super tier |  |  | 
1 | 36 864 | 350 | - | - | 16 | 1 | 1
2 | 122 880 | 1 500 | - | - | 16 | 1 | 1
2.1 | 245 760 | 3 000 | - | - | 20 | 1 | 1
3 | 552 960 | 6 000 | - | - | 30 | 2 | 2
3.1 | 983 040 | 10 000 | - | - | 40 | 3 | 3
4 | 2 228 224 | 12 000 | 30 000 | 120 000 | 75 | 5 | 5
4.1 | 2 228 224 | 20 000 | 50 000 | 200 000 | 75 | 5 | 5
5 | 8 912 896 | 25 000 | 100 000 | 400 000 | 200 | 11 | 10
5.1 | 8 912 896 | 40 000 | 160 000 | 640 000 | 200 | 11 | 10
5.2 | 8 912 896 | 60 000 | 240 000 | 960 000 | 200 | 11 | 10
6 | 35 651 584 | 60 000 | 240 000 | 960 000 | 600 | 22 | 20
6.1 | 35 651 584 | 120 000 | 480 000 | 1 920 000 | 600 | 22 | 20
6.2 | 35 651 584 | 240 000 | 800 000 | 3 200 000 | 600 | 22 | 20

## Slide 10: Syntax changes (3/4)
Level | Max luma sample rate MaxLumaSr (samples/sec) | Max bit rate MaxBR (CpbBrVclFactor or CpbBrNalFactor bits/s) |  |  | Min compression ratio base MinCrBase
 |  | Main tier | High tier | Super tier | 
1 | 552 960 | 128 | - | - | 2
2 | 3 686 400 | 1 500 | - | - | 2
2.1 | 7 372 800 | 3 000 | - | - | 2
3 | 16 588 800 | 6 000 | - | - | 2
3.1 | 33 177 600 | 10 000 | - | - | 2
4 | 66 846 720 | 12 000 | 30 000 | 120 000 | 4
4.1 | 133 693 440 | 20 000 | 50 000 | 200 000 | 4
5 | 267 386 880 | 25 000 | 100 000 | 400 000 | 6
5.1 | 534 773 760 | 40 000 | 160 000 | 640 000 | 8
5.2 | 1 069 547 520 | 60 000 | 240 000 | 960 000 | 8
6 | 1 069 547 520 | 60 000 | 240 000 | 960 000 | 8
6.1 | 2 139 095 040 | 120 000 | 480 000 | 1 920 000 | 8
6.2 | 4 278 190 080 | 240 000 | 800 000 | 3 200 000 | 6

## Slide 11: Syntax changes (4/4)
Profile | CpbBrVclFactor | CpbBrNalFactor | FormatCapabilityFactor | MinCrScaleFactor
Monochrome 12 | 1000 | 1100 | 1.500 | 1.0
Monochrome 16 | 1330 | 1470 | 2.000 | 1.0
Main | 1000 | 1100 | 1.500 | 1.0
Main 10 | 1000 | 1100 | 1.875 | 1.0
Main 12 | 1500 | 1650 | 2.250 | 1.0
Main 4:2:2 10 | 1670 | 1830 | 2.500 | 0.5
Main 4:2:2 12 | 2000 | 2200 | 3.000 | 0.5
Main 4:4:4 | 2000 | 2200 | 3.000 | 0.5
Main 4:4:4 10 | 2500 | 2750 | 3.750 | 0.5
Main 4:4:4 12 | 3000 | 3300 | 4.500 | 0.5
Main Intra | 1000 * HbrFactor | 1100 * HbrFactor | 1.500 | 1.0 ÷ HbrFactor
Main 10 Intra | 1250 * HbrFactor | 1375 * HbrFactor | 1.875 | 1.0 ÷ HbrFactor
Main 12 Intra | 1500 * HbrFactor | 1650 * HbrFactor | 2.250 | 1.0 ÷ HbrFactor
Main 4:2:2 10 Intra | 1670 * HbrFactor | 1830 * HbrFactor | 2.500 | 0.5 ÷ HbrFactor
Main 4:2:2 12 Intra | 2000 * HbrFactor | 2200 * HbrFactor | 3.000 | 0.5 ÷ HbrFactor
Main 4:4:4 Intra | 2000 * HbrFactor | 2200 * HbrFactor | 3.000 | 0.5 ÷ HbrFactor
Main 4:4:4 10 Intra | 2500 * HbrFactor | 2750 * HbrFactor | 3.750 | 0.5 ÷ HbrFactor
Main 4:4:4 12 Intra | 3000 * HbrFactor | 3300 * HbrFactor | 4.500 | 0.5 ÷ HbrFactor
[Ed. the CpbBrVclFactor have been scaled by bit-depth over previous definition in O1005_v4 where 8-bit was assumed. 16-bit profiles would follow the same rules as defined here (P0057,P0058). Note also that which profiles are changed is open to debate and are just indicating a potential conflict.]

## Slide 12: Notes
Tier | general_tier_flag | general_super_tier_flag | general_intra_constraint_flag | general_lower_bit_rate_constraint_flag | HbrFactor
Main | 0 | 0 | 0 or 1 | 1 | 1
High | 1 | 0 | 0 or 1 | 1 | 1
Super | 0 | 1 | 0 or 1 | 1 | 1
Tier | general_tier_flag | general_super_tier_flag | general_intra_constraint_flag | general_lower_bit_rate_constraint_flag | HbrFactor
Main | 0 | 0 | 1 | 0 or 1 | 2 or 1
High | 1 | 0 | 1 | 0 or 1 | 2 or 1
Super | 0 | 1 | 1 | 0 or 1 | 2 or 1
Long-Gop profiles
All-intra profiles