## Slide 1: MV-HEVC/SHVC HLS: On layer set definition (JCTVC-P0045/JCT3V-G0037)
JCT-VC 16th Meeting: San José, US, 9–17 Jan. 2014
JCT-3V 7th Meeting: San José, US, 11–17 Jan. 2014
Tomohiro Ikai, Takeshi Tsukuba, Tomoyuki Yamamoto
SHARP Corporation

## Slide 2: Summary
Proposal:
  Specify “Any layer shall be included in at least one layer set” (Proposal 1)
  Add a flag “complete flag” to indicate whether the layer set can be extracted into a conforming bitstream, thus includes all dependent information (Proposal 2)
Benefits:
  Answer market confusions on the layer set usage
  Avoid stray layer problem in which profile and level is unknown
  Allow flexible layer set usage

## Slide 3: Introduction
Layer set / Output layer set
  has profile and level
  can be safely extracted (implicitly anticipated)
  has output layer flag and may have HRD param ...
Layer set / Output layer set is just defined and used but not adequately restricted
There are QUESTIONS on usage

## Slide 4: Question 1?
  Q1: “Which layer sets should be defined?
A
B
AUX
C
Layer set should be defined for any layers?
(Can we skip it by assuming SHVC as the same as A&B)
Layer set should be defined for auxiliary layers?
Bitstream has number of layers, A, B, C and AUX
SHVC layer set

## Slide 5: Solution for the question 1
  Q1: “Which layer sets should be defined?
Layer set should be defined for any layers?
Yes! (auxiliary layers too)
A1: Layer set should be mandatory for any layers
Every layers should be defined in terms of profile and level to know how to decode and how much decoder capability is needed
Profile and level can limit which kind of auxiliary is allowed (not yet decided).

## Slide 6: Proposal 1
“Any layer shall be included in at least one layer set.”
Text
It is a requirement of bitstream conformance that any layers, which exist in the coded video sequence and are specified in the active VPS, shall be included in at least one layer set specified in the same VPS.

## Slide 7: Question2
  Q2: “Which layer sets can be defined?
BL
EL
But It seems that usage is not allowed since it breaks results of bitstream extraction
We want to define a layer set which has EL only to indicate EL only bitstream
EL only layer set

## Slide 8: Solution for Question2
  Q2: “Which layer sets can be defined?
EL only layer set is useful to indicate EL only bitstream
A2: Incomplete layer set (missing some dependent layer) is allowed but extraction problem should be addressed.

## Slide 9: Proposal2
Add a flag “complete_layer_set_flag” to each layer set to avoid bitstream extraction problem
for( i = 1; i < numOutputLayerSets; i++ ) { | 
if( i > vps_number_layer_sets_minus1 ) { | 
output_layer_set_idx_minus1[ i ] | u(v)
lsIdx = output_layer_set_idx_minus1[ i ] + 1 | 
for( j = 0 ; j < NumLayersInIdList[ lsIdx ] − 1; j++) | 
output_layer_flag[ i ][ j ] | u(1)
} | 
else | 
complete_layer_set_flag[ i ] | u(1)
profile_level_tier_idx[ i ] | u(v)
} | 

## Slide 10: Proposal 2 (continue)
complete_layer_set_flag[ i ] specifies whether the corresponding layer set can be extracted into conforming bitstream by the process specified in subclause F.10.X Sub-bitstream extraction process.
complete_layer_set_flag[ i ] equal to 1 specifies the corresponding layer set can be extracted into conforming bitstream and complete_layer_set_flag equal to 0 specifies the corresponding layer set may or may not be extracted into the conforming bitstream. When complete_layer_set_flag[ i ] is not present and i is equal to 0, it is inferred to be equal to 1. When complete_layer_set_flag[ i ] is not present and index i is greater than vps_number_layer_sets_minus1, it is inferred to be equal to the value of complete_layer_set_flag[ output_layer_set_idx_minus1[ i ] + 1 ].
F.10.X Sub-bitstream extraction process.
It is a requirement of bitstream conformance for the input bitstream that any output sub-bitstream of the process specified in this clause with tIdTarget equal to any value in the range of 0 to 6, inclusive, and layerIdListTarget equal to the layer identifier list associated with a layer set specified in the active video parameter set shall be a conforming bitstream and complete_layer_set_flag of the layer set shall be equal to 1.

## Slide 11: Conclusion
Proposal
  Specify “Any layer shall be included in at least one layer set.” (Proposal 1)
  Add a flag “complete flag” to indicate whether the layer set can be extracted into a conforming bitstream, thus includes all dependent information (Proposal 2)
Questions for layer set usage are resolved
  Layer set is to be mandatory for any layers (auxiliary picture also is included in a layer set)
  EL only layer set (missing some dependent layer) can be used