## Slide 1: AHG 13: Scale and reference position derivation for sub-region extraction (JCTVC-P0049)
JCT-VC 16th Meeting: San José, US, 9–17 Jan. 2014
Tomoyuki Yamamoto, Tomohiro Ikai, Takeshi Tsukuba (SHARP) Elena Alshina (Samsung)

## Slide 2: Summary
Proposal:
  modifications on scale and reference position derivation to help sub-region extraction
    SPS syntax to signal “reference layer offsets”
    change semantics of “scaled reference layer offsets”
    scale and reference position derivation using “reference layer offsets” and “scaled reference layer offsets”
Benefits:
  achieves functionality to keep the same reconstructed pixel values before and after sub-region extraction

## Slide 3: Introduction
sub-region extraction in SHVC
  create bitstream corresponding to sub-region (ROI) by
    extracting VCL NAL Unit relating the sub-region
    rewriting PS and header information
Problem
  cannot keep the same pixel value before and after extraction
    derived scale value could be different
    derived phase between EL and BL pixels could be different
    it causes drift when decoding the extracted bitstream
    slice data re-encoding will be required to avoid the drift

## Slide 4: Sub region extraction example
extraction
EL
BL
ELW0 = SRLW0
BLW0
EL
BL
ELW1
SRLW1
BLW1
A
B
C
D
Phase could be different from “A and B” to “C and D”
Scale could be different (cf. “BLW0 / SRLW0” and “BLW1 / SRLW1”)

## Slide 5: Reference layer offsets
extraction
EL
BL
ELW0 = SRLW0
BLW0
EL
BL
ELW1
AltBLW1
SRLW1
BLW1
RefLayerLeft/TopOffset (negative value)
RefLayerRight/BottomOffset (negative value)
ScaledRefLayerTop/LeftOffset
ScaledRefLayerBottom/RightOffset
EL picture
SRL picture
BL picture
Alt BL picture

## Slide 6: RefLayerOffset syntax in SPS extension
sps_multilayer_extension( ) { | Descriptor
inter_view_mv_vert_constraint_flag | u(1)
num_scaled_ref_layer_offsets | ue(v)
for( i = 0; i < num_scaled_ref_layer_offsets; i++) { | 
scaled_ref_layer_id[ i ] | u(6)
scaled_ref_layer_left_offset[ scaled_ref_layer_id[ i ] ] | se(v)
scaled_ref_layer_top_offset[ scaled_ref_layer_id[ i ] ] | se(v)
scaled_ref_layer_right_offset[ scaled_ref_layer_id[ i ] ] | se(v)
scaled_ref_layer_bottom_offset[ scaled_ref_layer_id[ i ] ] | se(v)
} | 
num_ref_layer_offsets | ue(v)
for( i = 0; i < num_ref_layer_offsets; i++) { | 
ref_layer_id[ i ] | u(6)
ref_layer_left_offset[ ref_layer_id[ i ] ] | se(v)
ref_layer_top_offset[ ref_layer_id[ i ] ] | se(v)
ref_layer_right_offset[ ref_layer_id[ i ] ] | se(v)
ref_layer_bottom_offset[ ref_layer_id[ i ] ] | se(v)
} | 
} | 
reference layer offset variables are derived as follows
RefLayerLeftOffset = (ref_layer_left_offset [ref_layer_id[i]] << 1)

## Slide 7: Scale and reference position derivation
AltRefLayerPicWidthInSamplesY = RefLayerPicWidthInSamplesY – RefLayerLeftOffset – RefLayerRightOffset
ScaleFactorX = ( ( AltRefLayerPicWidthInSamplesY << 16 ) + ( ScaledRefLayerPicWidthInSamplesY >> 1 ) ) / ScaledRefLayerPicWidthInSamplesY
BL
ELW1
AltBLW1
SRLW1
BLW1
(RefLayerLeftOffset, RefLayerTopOffset)
(RefLayerRightOffset, RefLayerBottomOffset)
ScaledRefLayerTop/LeftOffset
ScaledRefLayerBottom/RightOffset
offsetXRef = ( RefLayerLeftOffset << 4 )/ ( ( cIdx = = 0) ? 1 : SubWidthC)
xRef16 = ( ( ( xP – offsetX ) * ScaleFactorX + addX + ( 1 << 11 ) ) >> 12 ) – ( phaseX << 2 ) + offsetXRef
Scale
Reference position

## Slide 8: Conclusion
This contribution proposes:
  new “reference layer offset” syntax
  modified scale and reference position derivation
The proposed changes helps to keep reconstructed pixel values after sub-region extraction  light sub-region extraction process can be supported
It is recommended to adopt the proposed changes in SHVC

## Slide 10: positive reference layer offsets
extraction
EL
BL
ELW0 = SRLW0
BLW0
EL
BL
ELW1
BLW1
SRLW1
AltBLW1
(RefLayerLeftOffset, RefLayerTopOffset)
(RefLayerRightOffset, RefLayerBottomOffset)
ScaledRefLayerTop/LeftOffset
ScaledRefLayerBottom/RightOffset
EL picture
SRL picture
BL picture
Alt BL picture

## Slide 11: negative reference layer offsets
extraction
EL
BL
ELW0 = SRLW0
BLW0
EL
BL
ELW1
AltBLW1
SRLW1
BLW1
(RefLayerLeftOffset, RefLayerTopOffset)
(RefLayerRightOffset, RefLayerBottomOffset)
ScaledRefLayerTop/LeftOffset
ScaledRefLayerBottom/RightOffset
EL picture
SRL picture
BL picture
Alt BL picture

## Slide 12: zero reference layer offsets
extraction
EL
BL
ELW0 = SRLW0
BLW0
EL
BL
ELW1
BLW1 = AltBLW1
SRLW1
(RefLayerLeftOffset, RefLayerTopOffset)
(RefLayerRightOffset, RefLayerBottomOffset)
ScaledRefLayerTop/LeftOffset
ScaledRefLayerBottom/RightOffset
EL picture
SRL picture
BL picture
Alt BL picture