## Slide 1: AHG18: Worst-Case Escape Code Length Mitigation
JCTVC-P0061
Broadcast & Professional Research Labs
Sony Europe Ltd.
Karl Sharman
Sony Corp.

## Slide 2: Background
In HEVC, escape codes are used to signal any part of a coefficient’s magnitude that is not described by a CABAC syntax element.
  The escape code syntax element is named “coeff_abs_level_remaining”.
coeff_abs_level_remaining is bypass-coded using a mixed Golomb‑Rice and exponential‑Golomb‑order‑k binarisation.
When using extended‑precision processing to code 16-bit video, the worst-case escape code length is 46.
  The largest possible coefficient magnitude is 222 = 4194304.
    Hence, the largest possible escape code is 4194303 (after deducting 1 for the significance map).
    If the Rice parameter rParam is 0, a further 3 is deducted and the value 4194300 is coded using exponential‑Golomb coding.
    The final code will require 21 prefix bits, 21 suffix bits, 1 separator bit and 3 extra prefix bits to signify that golomb-Rice coding is not in use. 21 + 21 + 1 + 3 = 46.
  In HEVC version 1, the worst-case escape code length is 32 (see JCTVC-J0142).

## Slide 3: Proposed Scheme
In exponential‑Golomb coding, the suffix length is equal to the prefix length. It is proposed that, instead, when extended‑precision processing is in use, a different mapping between prefix and suffix length is used.
  The proposed mapping is shown in the following table:
In addition, since the maximum prefix length would be fixed at 7, it is proposed that the prefix be coded using truncated‑unary coding rather than simple unary coding.
Using this scheme, the worst-case escape code length would be:
  7 (prefix) + 22 (maximum suffix) + 3 (not-a-Golomb-Rice-code bits) = 32.
  The worst-case is thus reduced by 14 bits.
  This is the same worst case as in HEVC version 1, which would have to be supported by a Range Extensions codec.

## Slide 4: Results
The proposed scheme was tested under AHG18 test conditions as defined in RCE1.
  Since the proposed scheme is only in use when extended-precision processing is enabled, no change in BD-rate occurs for other test conditions.
  The results are shown below:

## Slide 5: Conclusion
A modification to the current HEVC escape coding scheme for use with extended‑precision processing has been presented.
  Through use of this scheme, the worst-case escape code length can be reduced from 46 to 32, bringing it in line with that of HEVC version 1.
The proposed scheme has been shown not to have significant impact on coding efficiency or run-time.
  BD-rate changes of 0.1% or less are observed for AHG18 test conditions, with the overall changes being 0.0%.