## Slide 1: Redundant frames for SHVC/HEVC
Sychev Maxim

## Slide 2: Abstract
This contribution presents the support for redundant frames in SHVC/MV-HEVC (/HEVC if possible).
The proposed solution describes the syntax and semantics of how to support redundant frames (in the enhancement layers) by enabling more then one frame in the same layer to have the same POC, and propose the HRD behaviour when processing the frame with duplicated POC.
This contribution has two solutions for usage of redundant frames for error resilience and one solution for performing interlayer prediction for redundant frames.

## Slide 3: Introduction
The current specification of SHVC/MV-HEVC and HEVC does not allow having redundant frames in bitstream. This proposal describes introducing redundant frames into SHVC/MV-HEVC/HEVC and several applications and examples of how they can be used. Usage of redundant frames makes no sense for non-reference pictures.
Proposed solutions allow to separate the primary coded picture and the redundant coded pictures, which can increase the error resilience of bitstream in case of bursts (grouped packet loss).

## Slide 4: Description
primary coded picture: The coded representation of a picture to be used by the decoding process for a bitstream conforming to this Recommendation | International Standard. The primary coded picture contains all coding tree units of the picture. The only pictures that have a normative effect on the decoding process are primary coded pictures. See also redundant coded picture.
redundant coded picture: A coded representation of a picture or a part of a picture. The content of a redundant coded picture shall not be used by the decoding process for a bitstream conforming to this Recommendation | International Standard. A redundant coded picture is not required to contain all coding tree units in the primary coded picture. Redundant coded pictures have no normative effect on the decoding process. See also primary coded picture.

## Slide 5: Enabling redundant frames
The value of PicOrderCntVal shall be in the range of −231 to 231 − 1, inclusive. In one CVS, the PicOrderCntVal values for any two coded pictures in the same layer shall not be the same.
In one CVS, the same values of PicOrderCntVal for any two coded pictures in the same layer (exclude base layer) means that the first picture with this value of POC in decoding order is a primary coded picture and the following pictures with the same POC are redundant coded pictures.

## Slide 6: Solution A
If any received frame has the same POC number as any frame in DPB, then this frame is discarded. If there is no frame with the same POC number in DPB then this frame is decoded.
Before any RPS list construction perform the following:
If( there is a picture in the DPB that has the same PicOrderCntVal as the current picture )
Stop the current picture decoding process and proceed to the following access units

## Slide 7: Solution B
The slice header parsing process is required for solution A. It makes impossible early detection of redundant slices in CVS for discarding from decoding process in case of absence of errors in previously decoded frames.
The solution A has some restriction on protection IRAP frames.
For early detection it is proposed to include new NAL unit type RDN_NUT instead of RSV_VCL24.
nal_unit_type | Name of nal_unit_type | Content of NAL unit and RBSP syntax structure NAL unit | type class
24 | RDN_NUT | Coded slice segment of a redundant picture slice_segment_layer_rbsp( ) | VCL

## Slide 8: Different losses are covered by redundant frame

## Slide 9: Redundant frames for IRAP frames (Solution B)
There are no recovering problem with IRAP frames with NoRaslOutputFlag equal to 0
In case of IRAP frames with NoRaslOutputFlag equal to 1 the POCprimary based on nal_unit_type_primary used for matching with POCs in DPB

## Slide 10: Redundant P frames in MDC

## Slide 11: Redundant B frames in MDC

## Slide 12: Recovering base layer with redundant frames

## Slide 13: Reduced size redundant frames
Redundant frames make sense especially for error resilience those of frames which marked as “used for reference”.
Proposed to code only those areas of picture which are used for temporal inter prediction. In that case it is need to mark redundant frame PicOutputFlag equal to 0 and use it only for decoder state recovery.

## Slide 14: Results of simulations

## Slide 15: Conclusion
Redundant frames are very useful in different error protection scenarios such as the interactive scenario using the feedback channel to signal lost data and non-interactive scenarios based on forward error correction approach.
The proposed technique allows to separate the protected primary coded picture and the associated redundant frame for better error resilience in case of bursts.
The proposed solution B allows to protect the large sized IRAP frames which are more sensitive to transmission errors.
The new redundant frames are constructed in a manner which allows to add such functionality to HEVC version 1 because the redundant frames will be discarded by already implemented decoders and can be used in future versions with little modifications in HLS.

## Slide 16
Thank You
www.huawei.com