## Slide 1: Non-SCE1: Asymmetric 3D LUT for Color Gamut Scalability (JCTVC-P0063)
X. Li, J. Chen, and M. Karczewicz (Qualcomm Inc.)

## Slide 2: Motivation
In Nov. 2013, Qualcomm announced Snapdragon 805 for mobile devices
  System-level 4K/Ultra HD support
  4K video capture and playback
4K video becomes an important application for mobile devices such as tablet
Hardware cost for color gamut scalability has to be considered
  Non-fixed large lookup table is very expensive for hardware

## Slide 3: Review of 3D Lookup Table based Color Gamut Scalability
JCTVC-P0128 (Technicolor) and JCTVC-P0186 (InterDigital)
  Y-U-V space is evenly split into 8x8x8 partitions (with 9x9x9 vertexes)
  For each partition
  Coefficients are converted to vertexes of a cubic partition
  The vertexes of neighboring cubic partition are merged so that neighboring partitions share vertexes
  Vertexes are signaled
  The lookup table has 9x9x9x3=2187 entries

## Slide 4: Asymmetric 3D Lookup Table based Color Gamut Scalability
To reduce the table size, asymmetric 3D lookup table is proposed
  The Y-U-V space is split into up to 8x2x2 cuboid partitions
    More partitions along Y direction
  For each partition
  Coefficients are converted to four vertexes according to tetrahedral interpolation.
  Vertexes are signaled. Neighboring partitions do not share vertexes
  The lookup table size is 8x2x2x4x3=384 entries

## Slide 5: Lookup Table Derivation and Signaling
Lookup table derivation
  The partition number is first determined based on previously coded frames
  The table is derived by minimizing the distortion between converted samples and original input samples of enhancement layer
Signaling
  The table is signaled in PPS
  The table is updated in slice header when necessary

## Slide 6: Simulation Results (SpsPpsPeriod=0)

## Slide 7: Simulation Results (SpsPpsPeriod=1)

## Slide 8: Conclusions
4K video is an important application for mobile devices. However, non-fixed large lookup table in color gamut scalability is very expensive for mobile hardware
Asymmetric 3D lookup table based method is proposed for color gamut scalability.
  Up to 8x2x2 partitions are used. At most, the table has 8x2x2x4x3=384 entries
Significant coding efficiency improvement is observed
  No worse or even better than methods with larger table.
    On average, 6.3% and 6.2% luma BD-rate reduction over UC1 anchor for RA cases
    On average, 6.6% and 6.4% luma BD-rate reduction over UC2 anchor for RA cases
Thanks Technicolor for crosschecking!
  Crosschecking report JCTVC-P0129

## Slide 9: Syntax Table (I)
pic_parameter_set_rbsp( ) { | Descriptor
… | 
slice_segment_header_extension_present_flag | u(1)
if(nuh_layer_id > 0) { | 
pps_cgs_idc | ue(v)
if(pps_cgs_idc==1 ¦¦ pps_cgs_idc==3) | 
3D_LUT_color_data() | 
} | 
… | 
} | 
slice_segment_header( ) { | Descriptor
… | 
if(nul_layer_id > 0) { | 
if(pps_cgs_idc==3) | 
slice_cgs_overwrite_pps_flag | u(1)
if(pps_cgs_idc==2 ¦¦ slice_cgs_overwrite_pps) | 
3D_ LUT_ color_data() | 
} | 
byte_alignment( ) | 
} | 

## Slide 10: Syntax Table (II)
3D_ LUT_ color_data ( ) { | Descriptor
cur_octant_depth | u(3)
cur_y_part_num_log2 | u(2)
input_bit_depth_minus8 | u(3)
output_bit_depth_minus8 | u(3)
res_quant_bit | u(2)
coding_octant( 0, 0, 0, 0, 1 << InputBitDepth) | 
} | 
coding_octant (depth, y,u,v,length) { | Descriptor
if ( depth < cur_octant_depth ) | 
split_octant_flag | u(1)
if ( split_octant_flag ) { | 
for( l = 0 ; l < 2 ; l++ ) | 
for( m = 0 ; m < 2 ; m++ ) | 
for( n = 0 ; n < 2 ; n++ ) | 
coding_octant ( depth+1, y+l*length/2, u+m*length/2,v+n*length/2, length/2) | 
} | 
else { | 
for( i = 0 ; i < YPartNum ; i++ ) | 
for( vertex = 0 ; vertex < 4 ; vertex++ ) { | 
encoded_vertex_flag | u(1)
if( encoded_vertex_flag ) { | 
resY[yIdx][uIdx][vIdx][vertex] | se(v)
resU[yIdx][uIdx][vIdx][vertex] | se(v)
resV[yIdx][uIdx][vIdx][vertex] | se(v)
} | 
} | 
} | 
} | 

## Slide 11: Results of Use Case 1
 | AI-10bit |  |  | AI-8bit |  |  | RA-10bit |  |  | RA-8bit |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
JCTVC-P0128 (9x9x9x3=2187) | -0.9% | -4.1% | -3.3% | -2.2% | -5.1% | -4.1% | -2.6% | -4.2% | -5.8% | -3.3% | -4.6% | -5.8%
JCTVC-P0186 (9x9x9x3=2187) With additional filtering | -2.9% | -5.5% | -5.0% | -3.4% | -5.8% | -5.1% | -3.8% | -5.1% | -7.3% | -4.0% | -5.2% | -6.9%
JCTVC-P0186 (9x9x9x3=2187) No additional filtering |  |  |  |  |  |  |  |  |  |  |  | 
JCTVC-P0063 (8x2x2x4x3=384) No picture update | -1.0% | -5.0% | -5.5% | -1.5% | -5.3% | -5.6% | -3.3% | -7.3% | -9.4% | -3.4% | -7.4% | -9.0%
JCTVC-P0063 (8x2x2x4x3=384) With picture update | -8.2% | -11.4% | -15.0% | -8.2% | -11.4% | -14.9% | -6.3% | -10.3% | -13.9% | -6.2% | -10.3% | -13.5%
JCTVC-P0128 (8x8x8x4x3=6144) Update for each intra period |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 12: Results of Use Case 2
 | AI-10bit |  |  | AI-8bit |  |  | RA-10bit |  |  | RA-8bit |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
JCTVC-P0128 (9x9x9x3=2187) | -5.6% | -7.8% | -9.9% | -5.9% | -8.0% | -10.0% | -5.1% | -6.1% | -9.7% | -5.1% | -6.1% | -9.3%
JCTVC-P0186 (9x9x9x3=2187) With additional filtering | -7.8% | -8.9% | -11.6% | -7.8% | -8.9% | -11.5% | -6.3% | -6.5% | -11.0% | -6.2% | -6.5% | -10.6%
JCTVC-P0186 (9x9x9x3=2187) No additional filtering | -7.1% | -8.5% | -11.1% | -7.1% | -8.5% | -11.0% | -5.9% | -6.5% | -10.9% | -5.7% | -6.4% | -10.4%
JCTVC-P0063 (8x2x2x4x3=384) No picture update | -6.0% | -9.1% | -12.3% | -6.1% | -9.3% | -12.2% | -5.9% | -9.2% | -13.2% | -5.8% | -9.2% | -12.9%
JCTVC-P0063 (8x2x2x4x3=384) With picture update | -8.4% | -11.5% | -15.2% | -8.4% | -11.5% | -15.1% | -6.6% | -9.8% | -14.2% | -6.4% | -9.8% | -13.9%
JCTVC-P0124 (8x8x8x4x3=6144) Update for each intra period | -8.6% | -12.3% | -16.8% | -8.5% | -12.3% | -16.7% | -6.4% | -10.0% | -14.3% | -6.3% | -10.0% | -14.1%
JCTVC-P0197 (8x2x2x4x3=384) |  |  |  |  |  |  |  |  |  |  |  |