## Slide 1: JCTVC-P0066 AHG5: Luma-chroma prediction for different bitdepth
Ohji Nakagami
Teruhiko Suzuki
Sony corporation

## Slide 2: Introduction
In JCTVC-O1005, the residual modification process for transform blocks using luma-chroma prediction (a.k.a. Cross Component Prediction) was introduced.
It is pointed that the current process is not optimal when BitDepthY and BitDepthC are different because the ranges of input and output variables are not same in eq. (8-298).
r[ x ][ y ] += ( ResScaleVal[ cIdx ][ xTbY ][ yTbY ] * rY[ x ][ y ] ) >> 3 (8‑298)
8.6.6 Residual modification process for transform blocks using luma-chroma prediction

## Slide 3: Proposal
To fix the issue, two alternative solutions are proposed.
Solution1: Scale the luma residual to align the chroma bitdepth by right or left shift operation
Solution2: Prohibit the luma-chroma prediction when the bitdepth are different

## Slide 4: Experiment
 | Used software | Configuration parameters |  |  |  | Corresponding proposal
 |  | CrossComponentDecorrelation | InternalBit Depth | InternalBit DepthC | SAO | 
Anchor | RExt5.1 | 1 | Same as TestX | Same as TestX | Same as TestX | -
Test1 | RExt5.1+change | 1 | 12 | 8 | 1 | Solution1
Test2 | RExt5.1+change | 1 | 8 | 12 | 0* | Solution1
Test3 | RExt5.1 | 0 | 12 | 8 | 1 | Solution2
Test4 | RExt5.1 | 0 | 8 | 12 | 0* | Solution2
The proposed two solutions are studied under RExt CTC with the modified settings shown in Table1 for YUV444 test set.
Table1 Test conditions
* It is due to the base software issue reported in the ticket #1219.

## Slide 5: Results of Solution1
 | Y (12bit) | U (8bit) | V (8bit)
AI-MT | -1.4% | -5.7% | -5.8%
RA-MT | -0.6% | -7.1% | -6.1%
LB-MT | -0.4% | -4.6% | -3.9%
 | Y (8bit) | U (12bit) | V (12bit)
AI-MT | -1.3% | -3.6% | -4.4%
RA-MT | -0.6% | -5.3% | -5.2%
LB-MT | -0.5% | -4.2% | -4.5%
Test1 results
Test2 results
It is confirmed that the expected performance by CCP is obtained with the proposed shift operation.

## Slide 6: Results of Solution2
 | Y (12bit) | U (8bit) | V (8bit)
AI-MT | -0.1% | 0.0% | 0.1%
RA-MT | -0.2% | -0.1% | 0.0%
LB-MT | -0.3% | 0.0% | -0.1%
 | Y (8bit) | U (12bit) | V (12bit)
AI-MT | 0.1% | 3.4% | 2.8%
RA-MT | -0.2% | 3.9% | 2.4%
LB-MT | -0.4% | 2.1% | 0.9%
Test3 results
Test4 results
It is noted that the positive value means the coding gain in Test3&4 since CCP is enabled in the anchor.
By disabling CCP, small (0.x%) luma loss is observed in Test3.
The chroma gain in Test4 is due to the maximum ResScaleVal (e.g. 8 or -8), which works as a scaling factor for the tested bitdepth difference ( 1<<4 = 1<<(C12-Y8)).

## Slide 7: Conclusion
From the experimental results, it is encouraged to modify the current luma-chroma residual prediction process to fix the issue.
As a straightforward approach, Solution1 is recommended.
Thanks to KDDI for the crosscheck (JCTVC-P0100).