## Slide 1: On VPS extension and VPS VUI (JCTVC-P0076/JCT3V-G0090)
Hahyun Lee
Jan., 2014

## Slide 2: Introduction
“vps_extension_offset” and “vps_vui_offset” would help some network entities to locate and access fixed-length coded information that is essential information in the VPS for session negotiation and, or capability changes
For accessing output layer sets and video signal information without entropy decoding for session negotiation and, or capability exchange, VPS extension and VPS VUI changes are proposed
On VPS extension
  Layer sets information are added into VPS extension for accessing output layer sets without entropy decoding.
On VPS VUI
  The signalling of video signal information is moved up to be accessible without entropy decoding.

## Slide 3: On VPS extension
Problem
  In the current MV-HEVC/SHVC draft text, the syntax element “vps_number_layer_sets_minus1” is u(10) coded in the VPS extension to access output layer sets without entropy decoding.
    Specify the layer sets specified in the VPS.
    Has an identical semantics with “vps_num_layer_sets_minus1” coded as ue(v) in the VPS.
  Due to the variable NumLayersInIdList[i] in the VPS extension, accessing output layer sets still needs entropy decoding.
    NumberLayerInIdList is derived as

## Slide 4: On VPS extension
Proposal
  layer sets information are also signalled in the VPS extension

## Slide 5: On VPS VUI
Problem
  Because there are syntax elements coded as ue(v) before video signal information, accessing video signal information needs entropy decoding.
    min_spatial_segment_offset_plus1[ i ][ j ]
    min_horizontal_ctu_offset_plus1[ i ][ j ]

## Slide 6: On VPS VUI
Proposal
  The signalling of video signal information is moved up to be accessible without entropy decoding.

## Slide 7: Conclusion
This contribution proposed VPS extension and VPS VUI changes to access output layer sets and video signal information without entropy decoding for session negotiation and, or capability changes
  The layer sets information are also signalled in the VPS extension
  The signalling of video signal information in the VPS VUI is moved up to be accessible without entropy decoding