## Slide 1
Non-RCE4 : On palette update for palette coding (JCTVC-O0091)
Chanyul Park, Sunil Lee, Chanyul Kim
Samsung Electronics Co., Ltd

## Slide 2: Problem Statement
No memory constraints on palette update in RCE4
  No constraints on palette size per each CU, CTU, slice
  No constraints on maximum memory size required for palette update
Unclear comparison between two RCE4 tests
  Palette size for Test 1 is smaller than that for Test 2
  Related with the maximum memory constraints, we need a guidance to compare two test results such as
    No palette update condition,
    Limited palette update condition,
    Unlimited palette update condition

## Slide 3: Descriptions
No palette update vs palette update
  RCE4 T1 : 0.1% / 0.8% / 0.4% for class F / SC (444) RGB / YUV
  RCE4 T2 : 0.1% / 2.7% / 2.0% for class F / SC (444) RGB / YUV
Palette update from left CU only
  RCE4 T1 : average 0.0% loss
  RCE4 T2 : no loss
Palette update from left and current LCU
  RCE4 T1 : not confirmed but almost zero loss is expected.
  RCE4 T2 : no loss
Palette update within current slice
  RCE4 T1 : no loss
  RCE4 T2 : no loss

## Slide 4: Proposals
A picture layer flag to disable the palette update.
More specific description for palette update enabled tests is required
  Palette update from left CU only
  Palette update from neighboring left CU only
  Palette update within left and current LCUs

## Slide 5: RCE4 T1 : No above pred.
 | Average bit-rate increase |  | 
 | AI | RA | LB
Class F | 0.0% | 0.1% | 0.0%
Class B | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | 0.1% | 0.0% | 0.2%
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | 0.1% | 0.1% | 0.0%
YCbCr 4:4:4 Animation | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | 0.3% | 0.2% | 0.1%
YCbCr 4:4:4 SC (Optional) | 0.3% | 0.8% | 2.1%
Enc Time[%] | 100% | 100% | 100%
Dec Time[%] | 100% | 100% | 100%

## Slide 6: RCE4 T1 : No above pred.
 | All Intra Main-tier |  |  | All Intra High-tier |  |  | All Intra Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1%
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | 0.0% | 0.0% | 0.1% | 0.1% | 0.0% | 0.1% | 0.1% | 0.1% | 0.1%
YCbCr 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | 0.3% | 0.2% | 0.2% | 0.3% | 0.3% | 0.3% | 0.3% | 0.3% | 0.3%
YCbCr 4:4:4 SC (Optional) | 0.3% | 0.2% | 0.2% | 0.3% | 0.3% | 0.2% | 0.4% | 0.4% | 0.3%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
 | Random Access Main-tier |  |  | Random Access High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RGB 4:4:4 SC | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% |  |  | 
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
YCbCr 4:4:4 SC | 0.0% | 0.0% | 0.1% | 0.2% | 0.1% | 0.2% |  |  | 
YCbCr 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RGB 4:4:4 SC (Optional) | 0.1% | 0.2% | 0.2% | 0.2% | 0.1% | 0.2% |  |  | 
YCbCr 4:4:4 SC (Optional) | 0.5% | 0.3% | 0.4% | 0.4% | 0.2% | 0.3% |  |  | 
Enc Time[%] | 100% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 102% |  |  | 102% |  |  |  |  | 
 | Low delay B Main-tier |  |  | Low delay B High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.1% | -0.2% | -0.1% | 0.0% | -0.1% | -0.2% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RGB 4:4:4 SC | 0.0% | 0.1% | 0.1% | 0.1% | 0.1% | 0.2% |  |  | 
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
YCbCr 4:4:4 SC | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% |  |  | 
YCbCr 4:4:4 Animation | 0.0% | 0.0% | -0.1% | 0.0% | -0.1% | -0.1% |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RGB 4:4:4 SC (Optional) | 0.4% | 0.4% | 0.4% | 0.3% | 0.2% | 0.2% |  |  | 
YCbCr 4:4:4 SC (Optional) | -0.1% | -0.6% | -0.3% | 0.3% | -0.2% | 0.1% |  |  | 
Enc Time[%] | 100% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 101% |  |  | 100% |  |  |  |  | 

## Slide 7: RCE4 T1 : No update
 | Average bit-rate increase |  | 
 | AI | RA | LB
Class F | 0.0% | 0.1% | 0.0%
Class B | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | 0.7% | 0.6% | 0.6%
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | 0.4% | 0.3% | 0.3%
YCbCr 4:4:4 Animation | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | 3.4% | 3.4% | 1.0%
YCbCr 4:4:4 SC (Optional) | 1.7% | 1.9% | 1.8%
Enc Time[%] | 100% | 100% | 100%
Dec Time[%] | 100% | 101% | 100%

## Slide 8: RCE4 T1 : No update
 | All Intra Main-tier |  |  | All Intra High-tier |  |  | All Intra Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | 0.1% | 0.2% | 0.2% | 0.1% | 0.1% | 0.2% | 0.1% | 0.1% | 0.1%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | 0.8% | 0.8% | 0.9% | 0.9% | 0.8% | 0.9% | 0.9% | 0.8% | 0.8%
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | 0.4% | 0.5% | 0.4% | 0.5% | 0.5% | 0.5% | 0.6% | 0.5% | 0.5%
YCbCr 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | 3.6% | 3.5% | 3.4% | 3.7% | 3.6% | 3.6% | 3.9% | 3.8% | 3.8%
YCbCr 4:4:4 SC (Optional) | 1.5% | 1.6% | 1.5% | 1.9% | 1.8% | 1.6% | 2.2% | 1.9% | 1.9%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 101% |  |  | 100% |  | 
 | Random Access Main-tier |  |  | Random Access High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | 0.1% | 0.0% | 0.2% | 0.1% | 0.0% | 0.1% |  |  | 
Class B | 0.0% | -0.1% | 0.2% | 0.0% | 0.0% | 0.0% |  |  | 
RGB 4:4:4 SC | 0.8% | 0.8% | 0.8% | 0.9% | 0.9% | 0.8% |  |  | 
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% |  |  | 
YCbCr 4:4:4 SC | 0.2% | 0.2% | 0.3% | 0.4% | 0.4% | 0.4% |  |  | 
YCbCr 4:4:4 Animation | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1% |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RGB 4:4:4 SC (Optional) | 3.2% | 3.1% | 3.0% | 3.5% | 3.3% | 3.3% |  |  | 
YCbCr 4:4:4 SC (Optional) | 1.5% | 1.4% | 1.3% | 1.7% | 1.6% | 1.5% |  |  | 
Enc Time[%] | 100% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 100% |  |  | 100% |  |  |  |  | 
 | Low delay B Main-tier |  |  | Low delay B High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.1% | 0.0% | -0.2% | 0.0% | -0.1% | -0.3% |  |  | 
Class B | 0.0% | 0.3% | -0.1% | 0.0% | 0.2% | 0.0% |  |  | 
RGB 4:4:4 SC | 0.5% | 0.5% | 0.6% | 0.6% | 0.6% | 0.6% |  |  | 
RGB 4:4:4 Animation | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% |  |  | 
YCbCr 4:4:4 SC | 0.2% | 0.3% | 0.3% | 0.3% | 0.3% | 0.3% |  |  | 
YCbCr 4:4:4 Animation | -0.1% | -0.2% | -0.2% | 0.0% | -0.1% | -0.1% |  |  | 
RangeExt | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% |  |  | 
RGB 4:4:4 SC (Optional) | 3.6% | 3.4% | 3.4% | 4.2% | 3.9% | 3.8% |  |  | 
YCbCr 4:4:4 SC (Optional) | 0.5% | 0.0% | 0.4% | 1.2% | 0.7% | 0.9% |  |  | 
Enc Time[%] | 100% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 100% |  |  | 99% |  |  |  |  | 

## Slide 9: RCE4 T2 : No update
 | Average bit-rate increase |  | 
 | AI | RA | LB
Class F | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | 3.6% | 2.2% | 1.4%
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | 3.6% | 2.3% | 1.4%
YCbCr 4:4:4 Animation | 0.3% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | 8.3% | 4.5% | 2.0%
YCbCr 4:4:4 SC (Optional) | 7.2% | 4.9% | 2.5%
Enc Time[%] | 100% | 100% | 100%
Dec Time[%] | 101% | 100% | 100%

## Slide 10: RCE4 T2 : No update
 | All Intra Main-tier |  |  | All Intra High-tier |  |  | All Intra Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | 2.7% | 2.7% | 2.7% | 3.2% | 3.2% | 3.1% | 3.5% | 3.5% | 3.5%
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | 2.0% | 2.2% | 2.2% | 2.9% | 2.9% | 2.8% | 3.4% | 3.3% | 3.4%
YCbCr 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | 5.8% | 5.7% | 5.8% | 6.7% | 6.5% | 6.5% | 7.3% | 7.3% | 7.4%
YCbCr 4:4:4 SC (Optional) | 5.3% | 5.6% | 5.6% | 6.5% | 6.5% | 6.4% | 7.2% | 7.3% | 7.3%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 99% |  | 
 | Random Access Main-tier |  |  | Random Access High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RGB 4:4:4 SC | 2.3% | 2.3% | 2.3% | 2.4% | 2.4% | 2.4% |  |  | 
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
YCbCr 4:4:4 SC | 1.9% | 1.9% | 2.0% | 2.3% | 2.2% | 2.2% |  |  | 
YCbCr 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RGB 4:4:4 SC (Optional) | 3.7% | 3.6% | 3.7% | 4.4% | 4.1% | 4.2% |  |  | 
YCbCr 4:4:4 SC (Optional) | 3.9% | 4.2% | 4.2% | 4.5% | 4.5% | 4.5% |  |  | 
Enc Time[%] | 100% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 99% |  |  | 99% |  |  |  |  | 
 | Low delay B Main-tier |  |  | Low delay B High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RGB 4:4:4 SC | 1.0% | 1.0% | 1.0% | 1.1% | 1.1% | 1.0% |  |  | 
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
YCbCr 4:4:4 SC | 0.7% | 0.9% | 0.8% | 1.0% | 1.0% | 1.0% |  |  | 
YCbCr 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RGB 4:4:4 SC (Optional) | 2.1% | 2.0% | 2.0% | 2.1% | 2.2% | 2.3% |  |  | 
YCbCr 4:4:4 SC (Optional) | 0.5% | 0.8% | 1.0% | 1.0% | 1.0% | 1.2% |  |  | 
Enc Time[%] | 100% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 98% |  |  | 98% |  |  |  |  | 

## Slide 11: RCE4 T2 : One LCU update
 | Average bit-rate increase |  | 
 | AI | RA | LB
Class F | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | 2.7% | 1.7% | 1.1%
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | 2.8% | 1.8% | 1.2%
YCbCr 4:4:4 Animation | 0.1% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | 5.8% | 3.2% | 1.6%
YCbCr 4:4:4 SC (Optional) | 4.6% | 3.4% | 1.9%
Enc Time[%] | 100% | 100% | 100%
Dec Time[%] | 100% | 98% | 99%

## Slide 12: RCE4 T2 : One LCU update
 | All Intra Main-tier |  |  | All Intra High-tier |  |  | All Intra Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | 2.3% | 2.3% | 2.3% | 2.7% | 2.7% | 2.6% | 2.8% | 2.8% | 2.7%
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | 1.7% | 1.9% | 1.9% | 2.4% | 2.5% | 2.4% | 2.8% | 2.7% | 2.8%
YCbCr 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | 4.0% | 3.9% | 3.9% | 4.4% | 4.3% | 4.3% | 4.7% | 4.7% | 4.7%
YCbCr 4:4:4 SC (Optional) | 3.6% | 3.8% | 3.9% | 4.3% | 4.3% | 4.3% | 4.7% | 4.7% | 4.7%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
 | Random Access Main-tier |  |  | Random Access High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RGB 4:4:4 SC | 1.9% | 1.9% | 1.9% | 2.0% | 1.9% | 2.0% |  |  | 
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
YCbCr 4:4:4 SC | 1.6% | 1.5% | 1.6% | 1.9% | 1.8% | 1.8% |  |  | 
YCbCr 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RGB 4:4:4 SC (Optional) | 2.7% | 2.6% | 2.7% | 3.3% | 3.0% | 3.1% |  |  | 
YCbCr 4:4:4 SC (Optional) | 2.8% | 3.1% | 3.2% | 3.3% | 3.3% | 3.3% |  |  | 
Enc Time[%] | 100% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 98% |  |  | 98% |  |  |  |  | 
 | Low delay B Main-tier |  |  | Low delay B High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RGB 4:4:4 SC | 0.8% | 0.9% | 0.8% | 0.9% | 0.9% | 0.9% |  |  | 
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
YCbCr 4:4:4 SC | 0.6% | 0.7% | 0.7% | 0.8% | 0.8% | 0.8% |  |  | 
YCbCr 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RGB 4:4:4 SC (Optional) | 1.8% | 1.7% | 1.8% | 1.8% | 1.9% | 2.0% |  |  | 
YCbCr 4:4:4 SC (Optional) | 0.3% | 0.5% | 0.6% | 0.7% | 0.7% | 0.8% |  |  | 
Enc Time[%] | 100% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 98% |  |  | 98% |  |  |  |  | 

## Slide 13: Conclusioins
A picture layer flag to disable the palette update is proposed
More specific description for palette update enabled tests is presented.
  Palette update from left CU only
  Palette update from neighboring left CU only
  Palette update within left and current LCUs