## Slide 1: Non-RCE4: Combined coding of run and index for RCE4 Test2 JCTVC-P0117
C. Gisquet, P. Onno, G. Laroche,
16th JCTVC Meeting, San Jose, January 2014

## Slide 2: Current RCE4 Test 2
RCE4 Test2 contains up to 32 palette elements.
The number P (P≤32= of palette elements used in a CU is signaled for each CU
P is used to determine the length (⌈log2(P)⌉) of the fixed length code for coding the index/level values.
Consequently, if P is not a power of 2, unused values ≥P of the code exist.

## Slide 3: Proposal: Level and Run coding combination
Given a FLC of length R = log2(P), there are L = 2R-P values above P that are unused.
We have chosen to repurpose these L unused values by having them represent instances of “run” for the palette index level=0, such that:
  For decoded index values level ≥ P, the run length is computed as (level-P), while the level is set to 0;
  Otherwise, because runs of length < L for level=0 have been encoded following the previous point, the decoded run is incremented by L.

## Slide 4: Experiments results: Lossy configuration
Anchor: RCE4 Test 2
Test: Mix of « level » and « run » coding
Results AI/RA/LB:
-0.5%/-0.5%/-0.3% on SC
-1.3%/-1.0%/-0.7% on opt. SC
 | All Intra Main-tier |  |  | All Intra High-tier |  |  | All Intra Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.1% | -0.2% | -0.1% | -0.2% | -0.2% | -0.1% | -0.2% | -0.2% | -0.2%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | -0.5% | -0.5% | -0.5% | -0.6% | -0.6% | -0.6% | -0.6% | -0.6% | -0.5%
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | -0.4% | -0.5% | -0.4% | -0.5% | -0.5% | -0.5% | -0.5% | -0.6% | -0.6%
YCbCr 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | -1.2% | -1.1% | -1.2% | -1.2% | -1.2% | -1.2% | -1.2% | -1.3% | -1.2%
YCbCr 4:4:4 SC (Optional) | -1.3% | -1.4% | -1.3% | -1.4% | -1.4% | -1.4% | -1.6% | -1.6% | -1.6%
Enc Time[%] | 99.6% |  |  | 99.5% |  |  | 99.5% |  | 
Dec Time[%] | 99.6% |  |  | 99.7% |  |  | 99.5% |  | 
 | Random Access Main-tier |  |  | Random Access High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.1% | -0.2% | -0.1% | -0.1% | -0.2% | -0.1% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RGB 4:4:4 SC | -0.5% | -0.5% | -0.5% | -0.6% | -0.6% | -0.6% |  |  | 
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
YCbCr 4:4:4 SC | -0.3% | -0.4% | -0.3% | -0.5% | -0.6% | -0.5% |  |  | 
YCbCr 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RGB 4:4:4 SC (Optional) | -1.1% | -1.1% | -1.1% | -1.2% | -1.1% | -1.2% |  |  | 
YCbCr 4:4:4 SC (Optional) | -0.9% | -1.3% | -1.2% | -0.9% | -1.0% | -1.0% |  |  | 
Enc Time[%] | 100.0% |  |  | 100.0% |  |  |  |  | 
Dec Time[%] | 99.1% |  |  | 98.8% |  |  |  |  | 
 | Low delay B Main-tier |  |  | Low delay B High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.1% | -0.8% | 0.4% | 0.0% | -0.3% | 0.0% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RGB 4:4:4 SC | -0.3% | -0.2% | -0.3% | -0.4% | -0.3% | -0.4% |  |  | 
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
YCbCr 4:4:4 SC | -0.3% | -0.2% | -0.2% | -0.3% | -0.2% | -0.1% |  |  | 
YCbCr 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RGB 4:4:4 SC (Optional) | 0.0% | 0.0% | 0.1% | -0.6% | -0.5% | -0.5% |  |  | 
YCbCr 4:4:4 SC (Optional) | -1.0% | -1.3% | -1.3% | -1.0% | -1.1% | -1.2% |  |  | 
Enc Time[%] | 99.6% |  |  | 99.4% |  |  |  |  | 
Dec Time[%] | 99.4% |  |  | 99.5% |  |  |  |  | 

## Slide 5: Experiments results: lossless configuration
Anchor: RCE4 Test 2
Test: CU transition mode
Results AI/RA/LB:
-0.4%/-0.4%/-0.4% on SC
-1.5%/-1.8%/-1.3% on opt. SC
 | Average bit-rate increase |  | 
 | AI | RA | LB
Class F | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | -0.4% | -0.3% | -0.4%
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | -0.4% | -0.4% | -0.4%
YCbCr 4:4:4 Animation | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | -1.5% | -2.0% | -1.4%
YCbCr 4:4:4 SC (Optional) | -1.4% | -1.6% | -1.1%
Enc Time[%] | 100% | 100% | 100%
Dec Time[%] | 101% | 100% | 101%

## Slide 6: Conclusion
Recommend to consider this combination of run and level coding for Palette mode on top of RCE4 Test 2 due to the coding efficiency gain reported for the Screen Content sequences.