## Slide 1: RExt HLS (AHG5 and 9): SEI message for alpha channel information JCTVC-P0123
R&D
© BBC MMXIV
Matteo Naccari and Marta Mrak
BBC Research and Development

## Slide 2: Outline
Introduction
Alpha channel parameters and associated processing
Proposed SEI message for alpha channel information

## Slide 3: Introduction
Alpha channel specifies for each pixel its degree of transparency or opacity
HEVC supports transmission of alpha channel using auxiliary pictures
  Do not have normative effects
  Transmitted as an additional scalability dimension in the bitstream (O0041)
Accordingly, each signal dependent parameter can be transmitted using specific SEI messages
This contribution therefore proposes an SEI message to signal parameters related to the alpha channel and its use in frame composition

## Slide 4: Alpha channel parameters and associated processing
For alpha channel signals, it is desirable to transmit the following information:
  Values for opaque and transparent samples
  Bit depth associated to alpha channel pixels
  Whether sample values should be clipped, filtered, etc.
  Whether the received primary picture is a pre-multiplied alpha
  Whether the received alpha channel should be up-sampled
The proposed SEI message for alpha channel information includes all these features

## Slide 5: Proposed SEI message for alpha channel information
Indicates the use of alpha channel
Multiply with primary picture
Do nothing
Unspecified
Avoids division during frame composition
Indicates alpha channel values clipping
Binary clipping
Linear clipping
Indicates whether alpha channel up-sampling is required