## Slide 1: Non-SCE1: Color gamut scalability using modified weighted prediction
JCTVC-P0124
A. Aminlou, K. Ugur, M. M. Hannuksela

## Slide 2: Introduction
Aim: Improving coding efficiency for Color Gamut Scalability by modifying the existing Weighted Prediction (WP) process.
Three modifications to existing WP:
  Region based WP: YUV region is divided into NxNxN regions and separate parameters are signaled separately for each region.
  Matrix based mapping: WP is modified so enhancement layer YUV values are calculated using linear matrix equations (i.e. Y of EL depends on YUV of BL, etc.)
  Polynomial WP: Instead of linear equations, second order polynomial equations are used.

## Slide 3: Region based WP
Based on the observations in JCTVC-L0334 and JCTVC-M0197:
  Dividing the YUV colorspace into regions and using different color space mapping function for each region improves the coding efficiency.
This technique was also used in SCE1 responses and also included in our proposal.
  YUV region is divided into an NxNxN region and separate parameters are signaled separately for each region.

## Slide 4: Matrix based mapping
As analyzed in JCTVC-L0334, utilizing a matrix based mapping more accurately reflects the BT.2020 to BT.709 mapping.
Gain(Y, Cb, Cr) is a 3x3 matrix and Offset(Y, Cb, Cr) is a 1x3 matrix.
Encoder uses simple linear regression to derive the parameters of the matrices (using more complicated algorithms could further improve coding efficiency)

## Slide 5: Polynomial WP
In order to better capture the non-linear relationship between two color spaces, as an alternative to Equation 1, we use a second order polynomial equation as follows:
Gain1(Y, Cb, Cr) and Gain2(Y, Cb, Cr) are 3x3 matrices and Offset(Y, Cb, Cr) is a 1x3 matrix.
(Y0, Cb0, Cr0) is the central point of the corresponding region to reduce the dynamic range.
The benefit of using polynomial equations is that one could reduce the number of regions as non-linear characteristics can already be captured with the polynomial equation.

## Slide 6: Results
Results for 4 different configurations are provided:
Configuration 1: N=8, linear matrix mapping (YUV colorspace is divided into 8x8x8 regions)
Configuration 2: N=1, linear matrix mapping (only difference to HEVC WP is linear matrix based equations)
Configuration 3: N=8, no matrix based WP (only difference to HEVC WP is signaling different WP parameters for different regions)
Configuration 4: N=1, polynomial matrix mapping enabled (only difference to HEVC WP is polynomial matrix based equations)

## Slide 7: Results - Summary
Comparison against best performing SCE results:
Chart: 
| Config1 | Config2 | Config3 | Config4 | UseCase2 Test1 | UseCase2 Test2
All Intra - BL 8 bits | -8.5 | -3.2 | -5.2 | -6.7 | -5.9 | -7.8

## Slide 8: Results
Configuration 1: N=8, linear matrix mapping (YUV colorspace is divided into 8x8x8 regions)

## Slide 9: Results
Configuration 2: N=1, linear matrix mapping (only difference to HEVC WP is linear matrix based equations)

## Slide 10: Results
Configuration 3: N=8, no matrix based WP (only difference to HEVC WP is signaling different WP parameters for different regions)

## Slide 11: Results
Configuration 4: N=1, polynomial matrix mapping enabled (only difference to HEVC WP is polynomial matrix based equations)

## Slide 12: Conclusions
Higher coding efficiency for CoGS is achieved by modifying the WP process.
Advantages:
Performs better than the best performing SCE1 response.
Modification to existing WP, asserted to be a smaller modification.
Various coding efficiency / complexity trade-offs possible.