## Slide 1: JCTVC-P0126 SEI message for Colour Mapping Information
P. Andrivon, P. Bordes, E. François
16th JCT-VC Meeting: San José, 9 – 17 Jan. 2014

## Slide 2: Colour Mapping Info SEI
  Context
    Migrating to WCG: Rec.2020/XYZ-based colorspaces
        Rec.2020/XYZ future-proof colour encoding systems
    Different gamut, different grades
      Rec.601, Rec.709, Rec.2020…
  Rationales
    Smooth colour space transition
    Preserving artistic intent for movies
      Bring quality from the Studios to the Home
      But… keeping TV sets differentiation (if required)
        mapping between Rec.2020 and Rec.709 legacy (not TV set primaries)
        optional rendering
    Transmit metadata with bitstreams: SEI
      To avoid data pruning during distribution
      To avoid sync issues

## Slide 3: Colour Mapping Info SEI
  Application
    UHDTV forward compatibility scenario
      e.g. UHD-1 Rec.2020 phase 2 signal with UHD-1 phase 1 Rec.709 devices
      Help rendering if Rec.2020 signal rendering is optional for UHD-1 phase 1 devices
Production
Rec.709 grade
WCG grade
WCG to Rec.709
gamut mapped
WCG to Rec.709
colour mapping SEI
colour
metadata
Displays
WCG display
Rec.709 legacy
display
HEVC STB
WCG to Rec.709
Colour mapping SEI
Rec.709 display
Wide CG display
Legacy
display
HEVC
distribution
WCG + metadata
Home
Distribution

## Slide 4: Colour Mapping Info SEI
  Other applications
    HD/UHD Rec.709 streams with WCG support
      Leverage legacy workflow while deploying new displays with new formats
    High quality stored content (Blu-ray…)
      Preserving colorist intent
    Colour mapping for specific applications
      Highlight content in content
      Non destructive content personalization
      …

## Slide 5: Colour Mapping Info SEI
  Proposition
    Syntax inspired from SEI tone mapping information
    Output format parameters: same as VUI
    Simplification of 3D LUT model
      1D LUT + 3x3 matrix + 1D LUT
        Leverage displays existing resources

## Slide 6: Colour Mapping Info SEI
  Proposition: 1D LUT + 3x3 matrix + 1D LUT
    Configurable model
    1D LUT: Piecewise linear (same as tone_map_model_id 3)

## Slide 7: Colour Mapping Info SEI
  Conclusion
    Demo showing benefits (last meeting)
    Preserving content creator intent
    Simplified model: 1D LUT + 3x3 matrix + 1D LUT
      address complexity concerns
      use limited resources from display