## Slide 1: Non-RCE4 Major Color Table (Palette) Merge from Above and Left CU
PoLin Lai, Shan Lu, Tzu-Der (Peter) Chuang, Yu-Wen Huang, Shawmin Lei
Presented by PoLin Lai
16th JCT-VC Meeting in San José
9–17 Jan. 2014
JCTVC-P0152
Notes: <number>

## Slide 2: Currently in RCE4 Major Color Table (Palette) Prediction
In RCE4, major color tables (palettes) of neighboring CUs can be used to predict the major color table of the current CU
  In RCE4 Test1, the major color tables of the left / above CUs are used
  In RCE4 Test2, the major color tables of the left CUs are used
Element-wise copy
  An major color element in the table, i.e. MCtable_current [n]
  MCtable_current [n] can copy from corresponding MCtable_above/left [n]
  For each element MCtable_current [n] :
  Flag to indicate copy, and copy direction (above/left), or code color value
<number>
JCTVC-P0152

## Slide 3: Proposed: MC Table (Palette) Merge
For current CU
  Copy entire major color table from the left CU
  Copy entire major color table from the above CU
  Transmit it’s own major color table
For a. and b.(merge), save syntax for major color table
  One flag major_color_merge = 1 to indicate merge
  One flag major_color_merge_dir to indicate left/above
  No further syntax for MC table
For c.(major_color_merge = 0), two options tested
  Allow element-wise copy (as in RCE4)
  Each MCtable_current [n]: Copy flag, copy direction flag, or color value
  Remove element-wise copy
  Each MCtable_current [n]: Always code color value
Encoder evaluates a. b. and c. based on RD
<number>
JCTVC-P0152

## Slide 4: Method 1: Non-merge has Element-wise Copy
Anchor: RCE4 Test1 (P0108)
2.2%, 1.6%, and 1.0% BD-rate savings for SC YUV 444 sequences under AI-MT, RA-MT, and LB-MT, respectively
<number>
BD-rate Y | AI-MT | AI-HT | AI-SHT | RA-MT | RA-HT | LB-MT | LB-HT
Class F | -0.6% | -0.6% | -0.5% | -0.4% | -0.3% | -0.3% | -0.2%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -2.3% | -2.3% | -2.2% | -1.9% | -1.9% | -1.2% | -1.3%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -2.2% | -2.5% | -2.4% | -1.6% | -1.5% | -1.0% | -1.1%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Opt. | -4.4% | -4.5% | -4.4% | -3.8% | -3.9% | -2.3% | -2.5%
SC(444) YUV Opt. | -4.0% | -4.6% | -4.9% | -3.2% | -3.7% | -2.2% | -2.0%
JCTVC-P0152
Notes: <number>

## Slide 5: Method 1: Non-merge has Element-wise Copy
Anchor: RCE4 Test1 (P0108)
1.7%, 1.2%, and 1.1% BD-rate savings for SC YUV 444 sequences under AI, RA, and LB, respectively
<number>
 | Average bit-rate increase |  | 
 | AI | RA | LB
Class F | -0.1% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | -1.6% | -1.6% | -1.1%
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | -1.7% | -1.2% | -1.1%
YCbCr 4:4:4 Animation | -0.1% | -0.1% | -0.1%
RangeExt | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | -3.9% | -3.8% | -3.2%
YCbCr 4:4:4 SC (Optional) | -3.8% | -3.2% | -2.8%
JCTVC-P0152
Notes: <number>

## Slide 6: Method 2: Non-merge code all color values
Anchor: RCE4 Test1 (P0108)
2.2%, 1.6%, and 1.0% BD-rate savings for SC YUV 444 sequences under AI-MT, RA-MT, and LB-MT, respectively
<number>
BD-rate Y | AI-MT | AI-HT | AI-SHT | RA-MT | RA-HT | LB-MT | LB-HT
Class F | -0.6% | -0.5% | -0.5% | -0.4% | -0.3% | -0.2% | -0.1%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -2.1% | -2.0% | -1.9% | -1.8% | -1.7% | -1.0% | -1.1%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -2.2% | -2.4% | -2.3% | -1.7% | -1.5% | -1.0% | -1.0%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | -0.1% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Opt. | -2.7% | -2.8% | -2.6% | -2.3% | -2.2% | -1.2% | -0.9%
SC(444) YUV Opt. | -3.6% | -4.1% | -4.2% | -2.8% | -3.2% | -1.5% | -2.0%
JCTVC-P0152
Notes: <number>

## Slide 7: Method 2: Non-merge code all color values
Anchor: RCE4 Test1 (P0108)
1.6%, 1.1%, and 1.0% BD-rate savings for SC YUV 444 sequences under AI, RA, and LB, respectively
<number>
 | Average bit-rate increase |  | 
 | AI | RA | LB
Class F | -0.1% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | -1.4% | -1.3% | -0.9%
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | -1.6% | -1.1% | -1.0%
YCbCr 4:4:4 Animation | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | -2.6% | -2.4% | -1.6%
YCbCr 4:4:4 SC (Optional) | -3.4% | -2.7% | -2.5%
JCTVC-P0152
Notes: <number>

## Slide 8: Conclusions
Major color table (palette) merge, select among:
  Copy entire MC table from the left CU  Just 2 flags
  Copy entire MC table from the above CU  Just 2 flags
  Transmit it’s own MC table
For c.(non-merge), two options tested
  Allow element-wise copy (as in RCE4)
  Simply code all the color values
<number>
JCTVC-P0152
Y-BD rate, on top of RCE4 Test1 (P0108) SC YUV 444 Class | AI | RA | LB
Test 1: Non-merge has element-wise, Lossy-MT | -2.2% | -1.6% | -1.0%
Test 1: Non-merge has element-wise, Lossless | -1.7% | -1.2% | -1.1%
Test 2: Non-merge codes all colors, Lossy-MT | -2.2% | -1.7% | -1.0%
Test 2: Non-merge codes all colors, Lossless | -1.6% | -1.1% | -1.0%
Notes: <number>

## Slide 9: Non-RCE4: Major color table propagation through non-palette CUs
Tzu-Der (Peter) Chuang, PoLin Lai, Yu-Chen Sun, Yi-Wen Chen,
Yu-Wen Huang, Shan Lu, Shawmin Lei
Presented by PoLin Lai
16th JCT-VC Meeting in San José
9–17 Jan. 2014
JCTVC-P0096
Notes: <number>

## Slide 10: Major Color Table (Palette) Prediction
In RCE4, major color tables of neighboring CUs can be used to predict the major color table of the current CU
  In RCE4 Test1, the major color tables of the left / above CUs are used
  In RCE4 Test2, the major color tables of the left CUs are used
In P0152, copy entire table from left / above CU
However……
If a neighboring CU is not coded in palette mode
  Major color table of the neighboring CU is set to all zero
  The prior major color table cannot be propagated to following CUs
<number>
JCTVC-P0096

## Slide 11: Proposed Methods
For a non-palette CU, the major color table of its left CU is used as its major color table
This major color table can be a reference major color table for following CUs
The prior major color table can be propagated through non-palette CUs
For current CU, even neighbors are non-palette CU, there are still major color tables (propagated from left palette-coded CU) to be used for the element-wise copy
<number>
JCTVC-P0096

## Slide 12: Results on Top of RCE4 Test1 - Lossy
Anchor: RCE4 Test1
2.7%, 2.3%, and 1.5% BD-rate savings for SC YUV 444 sequences under AI-MT, RA-MT, and LB-MT, respectively
Thank Microsoft for cross-verification (JCTVC-P0267)
<number>
BD-rate Y | AI-MT | AI-HT | AI-SHT | RA-MT | RA-HT | LB-MT | LB-HT
Class F | -0.7% | -0.7% | -0.7% | -0.5% | -0.5% | -0.4% | -0.3%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -2.5% | -2.5% | -2.3% | -2.0% | -2.0% | -1.8% | -1.9%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -2.7% | -3.1% | -3.1% | -2.3% | -2.1% | -1.5% | -1.8%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Opt. | -3.7% | -3.8% | -3.7% | -3.4% | -3.4% | -2.6% | -2.6%
SC(444) YUV Opt. | -5.2% | -6.1% | -6.4% | -3.9% | -4.8% | -3.5% | -3.9%
JCTVC-P0096
Notes: <number>

## Slide 13: Results on Top of RCE4 Test1 - Lossless
Anchor: RCE4 Test1
1.9%, 1.6%, and 1.5% BD-rate savings for SC YUV 444 sequences under AI, RA, and LB, respectively
<number>
 | Average bit-rate increase |  | 
 | AI | RA | LB
Class F | -0.2% | -0.1% | -0.1%
Class B | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | -1.6% | -1.6% | -1.4%
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | -1.9% | -1.6% | -1.5%
YCbCr 4:4:4 Animation | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | -3.5% | -3.3% | -3.1%
YCbCr 4:4:4 SC (Optional) | -5.2% | -4.5% | -4.2%
JCTVC-P0096
Notes: <number>

## Slide 14: Results on Top of RCE4 Test2 - Lossy
Anchor: RCE4 Test2
1.4%, 1.3%, and 0.6% BD-rate savings for SC YUV 444 sequences under AI-MT, RA-MT, and LB-MT, respectively
Thank Qualcomm for cross-verification (JCTVC-P0243)
<number>
BD-rate Y | AI-MT | AI-HT | AI-SHT | RA-MT | RA-HT | LB-MT | LB-HT
Class F | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -1.5% | -1.6% | -1.6% | -1.3% | -1.3% | -0.5% | -0.8%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -1.4% | -1.6% | -1.6% | -1.3% | -1.3% | -0.6% | -0.6%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Opt. | -4.5% | -4.6% | -4.9% | -3.6% | -4.0% | -1.9% | -2.5%
SC(444) YUV Opt. | -4.9% | -5.2% | -5.6% | -3.8% | -4.2% | -3.2% | -3.8%
JCTVC-P0096
Notes: <number>

## Slide 15: Results on Top of RCE4 Test2 - Lossless
Anchor: RCE4 Test2
1.1%, 1.2%, and 1.6% BD-rate savings for SC YUV 444 sequences under AI, RA, and LB, respectively
<number>
 | Average bit-rate increase |  | 
 | AI | RA | LB
Class F | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | -1.1% | -1.1% | -1.3%
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | -1.1% | -1.2% | -1.6%
YCbCr 4:4:4 Animation | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | -4.9% | -4.5% | -3.6%
YCbCr 4:4:4 SC (Optional) | -5.4% | -5.4% | -4.8%
JCTVC-P0096
Notes: <number>

## Slide 16: Conclusions
Propagate the major color table through non-palette CUs
  For a non-palette CU
  The major color table of its left CU is used as its major color table
  This table can be a reference major color table for following CUs
  The prior major color table can be propagated through non-palette CUs
<number>
JCTVC-P0096
Y-BD rates SC YUV 444 Class | AI | RA | LB
On top of RCE4 Test1, Lossy-MT | -2.7% | -2.3% | -1.5%
On top of RCE4 Test1, Lossless | -1.9% | -1.6% | -1.5%
On top of RCE4 Test2, Lossy-MT | -1.4% | -1.3% | -0.6%
On top of RCE4 Test2, Lossless | -1.1% | -1.2% | -1.6%
Notes: <number>

## Slide 17: P0152 Major Color Table Merge + P0096 Major Color Table Propagation
Presented by PoLin Lai
16th JCT-VC Meeting in San José
9–17 Jan. 2014
JCTVC-P0152
+ JCTVC-P0096
Notes: <number>

## Slide 18: Summary
P0152 Major color table (palette) merge, select among:
  Copy entire MC table from the left CU  Just 2 flags
  Copy entire MC table from the above CU  Just 2 flags
  Transmit it’s own MC table
P0096 Major color table (palette) propagation
  For a non-palette CU
  The major color table of its left CU is used as its major color table
  This table can be a reference major color table for following CUs
Combined methods
  Propagate coded-palette from the left CU for non-palette CU
  “Merge above / left” now could actually be merging with a previously-coded-palette that is not from a CU adjacent to the current CU
<number>
JCTVC-P0152
+ JCTVC-P0096
Notes: <number>

## Slide 19: Results Summary
<number>
Y-BD rates, lossy SC YUV 444 Class | AI-MT | RA-MT | LB-MT
P0152 Method 1 | -2.2% | -1.6% | -1.0%
P0096 | -2.7% | -2.3% | -1.5%
P0152,M1 + P0096 | -4.6% | -3.7% | -2.4%
JCTVC-P0152
+ JCTVC-P0096
Y-BD rates, lossless SC YUV 444 Class | AI | RA | LB
P0152 Method 1 | -1.7% | -1.2% | -1.1%
P0096 | -1.9% | -1.6% | -1.5%
P0152,M1 + P0096 | -2.8% | -2.3% | -2.3%
Notes: <number>

## Slide 20: Combined Results - Lossy
Anchor: RCE4 Test1
4.6%, 3.7%, and 2.4% BD-rate savings for SC YUV 444 sequences under AI-MT, RA-MT, and LB-MT
<number>
BD-rate Y | AI-MT | AI-HT | AI-SHT | RA-MT | RA-HT | LB-MT | LB-HT
Class F | -1.6% | -1.5% | -1.3% | -1.2% | -1.0% | -0.7% | -0.6%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -4.0% | -3.9% | -3.6% | -3.3% | -3.1% | -2.7% | -2.8%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -4.6% | -4.8% | -4.6% | -3.7% | -3.4% | -2.4% | -2.8%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.1%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Opt. | -7.7% | -7.7% | -7.4% | -6.7% | -6.8% | -5.3% | -5.6%
SC(444) YUV Opt. | -8.9% | -9.9% | -10.3% | -7.1% | -8.0% | -5.5% | -6.3%
JCTVC-P0152
+ JCTVC-P0096
Notes: <number>

## Slide 21: Combined Results - Lossless
Anchor: RCE4 Test1
2.8%, 2.3%, and 2.3% BD-rate savings for SC YUV 444 sequences under AI, RA, and LB, respectively
<number>
 | Average bit-rate increase |  | 
 | AI | RA | LB
Class F | -0.4% | -0.1% | -0.1%
Class B | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | -2.5% | -2.3% | -2.1%
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | -2.8% | -2.3% | -2.3%
YCbCr 4:4:4 Animation | -0.1% | -0.1% | -0.1%
RangeExt | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | -6.6% | -6.5% | -6.2%
YCbCr 4:4:4 SC (Optional) | -8.4% | -7.5% | -7.4%
JCTVC-P0152
+ JCTVC-P0096
Notes: <number>