## Slide 1: Non-RCE4 Major Color Table (Palette) Sharing
PoLin Lai, Shan Lu, Tzu-Der (Peter) Chuang, Yu-Wen Huang, Shawmin Lei
Presented by PoLin Lai
16th JCT-VC Meeting in San José
9–17 Jan. 2014
JCTVC-P0153
Notes: <number>

## Slide 2: Currently in RCE4 Major Color Table (Palette) Prediction
In RCE4, major color tables (palettes) of neighboring CUs can be used to predict the major color table of the current CU
  In RCE4 Test1, the major color tables of the left / above CUs are used
  In RCE4 Test2, the major color tables of the left CUs are used
Element-wise copy
  An major color element in the table, i.e. MCtable_current [n]
  MCtable_current [n] can copy from corresponding MCtable_above/left [n]
  For each element MCtable_current [n] :
  Flag to indicate copy, and copy direction (above/left), or code color value
If a neighboring CU is not “major-color-mode”
  Major color table of the neighboring CU is set to all zero
  The prior major color table cannot be propagated to following CUs
<number>
JCTVC-P0153

## Slide 3: Proposed: MC Table (Palette) Sharing
  Store the most-recently decoded major color table (palette)
For current CU
  Copy entire major color table from the most-recent-palette-CU
  Transmit it’s own major color table
For a.(sharing), save syntax for major color table
  One flag major_color_share = 1 to indicate sharing
  No further syntax for major color table
For b.(major_color_share = 0), two options tested
  Allow element-wise copy
  Each MCtable_current [n]: Copy MCtable_last [n], or code color value
  Remove element-wise copy
  Each MCtable_current [n]: Always code color value
Encoder evaluates a. b. based on RD
<number>
JCTVC-P0153

## Slide 4: Method 1: Non-share has Element-wise Copy
Anchor: RCE4 Test1 (P0108)
4.0%, 3.4%, and 2.2% BD-rate savings for SC YUV 444 sequences under AI-MT, RA-MT, and LB-MT, respectively
<number>
BD-rate Y | AI-MT | AI-HT | AI-SHT | RA-MT | RA-HT | LB-MT | LB-HT
Class F | -1.4% | -1.2% | -1.1% | -1.1% | -0.9% | -0.6% | -0.6%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -3.6% | -3.4% | -3.1% | -3.0% | -2.7% | -2.5% | -2.6%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -4.0% | -4.1% | -3.9% | -3.4% | -3.1% | -2.2% | -2.5%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Opt. | -6.1% | -6.1% | -5.9% | -5.7% | -5.7% | -4.8% | -4.6%
SC(444) YUV Opt. | -7.8% | -8.6% | -8.7% | -6.5% | -7.3% | -6.4% | -7.3%
JCTVC-P0153
Notes: <number>

## Slide 5: Method 1: Non-share has Element-wise Copy
Anchor: RCE4 Test1 (P0108)
2.4%, 1.8%, and 2.0% BD-rate savings for SC YUV 444 sequences under AI, RA, and LB, respectively
<number>
 | Average bit-rate increase |  | 
 | AI | RA | LB
Class F | -0.4% | -0.1% | -0.1%
Class B | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | -2.0% | -2.0% | -1.9%
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | -2.4% | -1.8% | -2.0%
YCbCr 4:4:4 Animation | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | -5.4% | -5.5% | -5.6%
YCbCr 4:4:4 SC (Optional) | -7.0% | -6.2% | -7.8%
JCTVC-P0153
Notes: <number>

## Slide 6: Method 2: Non-share code all color values
Anchor: RCE4 Test1 (P0108)
3.9%, 3.1%, and 2.2% BD-rate savings for SC YUV 444 sequences under AI-MT, RA-MT, and LB-MT, respectively
<number>
BD-rate Y | AI-MT | AI-HT | AI-SHT | RA-MT | RA-HT | LB-MT | LB-HT
Class F | -1.3% | -1.2% | -1.0% | -1.1% | -0.8% | -0.7% | -0.5%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -3.4% | -3.2% | -2.9% | -2.8% | -2.7% | -2.3% | -2.5%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -3.9% | -3.9% | -3.7% | -3.1% | -2.9% | -2.2% | -2.5%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Opt. | -5.2% | -5.1% | -4.9% | -5.0% | -5.0% | -4.0% | -3.6%
SC(444) YUV Opt. | -6.8% | -7.5% | -7.6% | -6.0% | -6.7% | -5.4% | -6.6%
JCTVC-P0153
Notes: <number>

## Slide 7: Method 2: Non-share code all color values
Anchor: RCE4 Test1 (P0108)
2.3%, 1.7%, and 2.0% BD-rate savings for SC YUV 444 sequences under AI, RA, and LB, respectively
<number>
 | Average bit-rate increase |  | 
 | AI | RA | LB
Class F | -0.4% | -0.1% | -0.1%
Class B | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | -1.9% | -1.8% | -1.8%
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | -2.3% | -1.7% | -2.0%
YCbCr 4:4:4 Animation | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | -4.7% | -4.8% | -4.8%
YCbCr 4:4:4 SC (Optional) | -6.4% | -6.1% | -7.3%
JCTVC-P0153
Notes: <number>

## Slide 8: Conclusions
Major color table (palette) sharing
  Storage of the most-recently decoded major color table (palette)
  For current CU, select between:
  Copy entire MC table from the most-recent-palette-CU  1 flag
  Transmit it’s own MC table
For b.(non-share), two options tested
  Allow element-wise copy from most-recent, or code color values
  Simply code all the color values
<number>
JCTVC-P0153
Lossy Y-BD rate, on top of RCE4 Test1 (P0108) SC YUV 444 Class | AI | RA | LB
Test 1: Non-share has element-wise, Lossy-MT | -4.0% | -3.4% | -2.2%
Test 1: Non-share has element-wise, Lossless | -2.4% | -1.8% | -2.0%
Test 2: Non-share codes all colors, Lossy-MT | -3.9% | -3.1% | -2.2%
Test 2: Non-share codes all colors, Lossless | -2.3% | -1.7% | -2.0%
Notes: <number>

## Slide 9: Suggestions
CE study of major color table (palette) sharing
  Only the most-recent-table for sharing, this contribution tested
  More than one set of recently decoded tables for sharing
  Reset mechanism: Reset the stored table for parallelism / error resilience
With sharing that copies entire table
  Benefit of allowing element-wise copy for non-share?
<number>
JCTVC-P0153
Notes: <number>