## Slide 1: JCTVC-P0154 AHG 8 and AHG5: New Alpha Parameter Coding Methods for Inter-component Residual Prediction in HEVC-RExt
Xianguo Zhang, Kai Zhang, Jicheng An, Shawmin Lei

## Slide 2: Outline
Background of Alpha Parameter Coding
Problems
Methods
Results

## Slide 3: Background of Alpha Parameter Coding
Alpha: res_scale_sign_flag and log2_res_scale_abs_plus1
log2_res_scale_abs_plus1: The absolute values of alpha
Binarization
Context Models, 3 context:
1 ctx for the 1st bin, 1 ctx for the 2nd bin, 1 ctx for the last two bins
Abosulte of ResScaleVal | log2_res_scale_abs_plus1 [ c ]
0 | 0(0)
1 | 1(10)
2 | 2(110)
4 | 3(1110)
8 | 4(1111)
Syntax element | ctxTable | InitType=0 | InitType=1 | InitType=2
log2_res_scale_abs_plus1[0][1] | Table 9‑37 | 0..5 | 6..11 | 12..17
res_scale_sign_flag[0][1] | Table 9‑38 | 0..1 | 2..3 | 4..5

## Slide 4: Problems
Problem 1
  Lots of videos select 8,4 as alpha values more often
  However, the current alpha mapping makes the 2 bits used to indentify latter values of 4,8 share one context model
    log2_res_scale_abs_plus1 utilizes 3 context models in total.
    Two context models are used by the first two bins separately, while one context model is shared by the last two bins.
Problem 2
  RGB videos are typically different from YUV videos
  JCTVC-P0066: Large value works as a scaling factor which is corresponding to the bitdepth difference equal to 4 (=C12-Y8).
  The proportion relationship among alphas is
    P(8)>P(4)>P(2)>P(1)> any of { P(-8), P(-4), P(-2), P(-1)}
  The current sign flag produces problems!

## Slide 5: Methods for alpha representation
Method 1
  Add a context model to encode absolute value of alpha
  Make the 2 bits used to indentify 4,8 have their separate context model.
Method 2 (Further Improvement for RGB)
  Alpha-parameter Predictive coding
    Pred value,
      5 bins used to identify 0, 8, 4, 2,1 and error, with 5 context model
    Remaining value
      ( -8,-4,-2,-1) is fixed encoded with equal proportion in 2 bins.
      Method 1+2
  A flag in PPS extension to select method 1 or 2
    Encode RGB videos with Method 2, YUV videos with Method 1

## Slide 6: Methods
Method 2
  Syntax
  Binarization
log2_res_scale_pred_4minus[ c ]
if( log2_res_scale_pred_plus1[ c ] != 5 )
log2_res_scale_neg[ c ]
Alpha | log2_res_scale_pred_4minus[ c ] | log2_res_scale_neg [ c ]
0 | 0(0) | Na
8 | 1(10) | Na
4 | 2(110) | Na
2 | 3(1110) | Na
1 | 4(11110) | Na
-1 | 5(11111) | 0(00)
-2 | 5(11111) | 1(01)
-4 | 5(11111) | 2(10)
-8 | 5(11111) | 3(11)

## Slide 7: Results
Method 1
  Average gains for groups of AHG8 videos, for Y, U, V or G, B, R
    0.1%~0.3% at AI and RA,0.1%~1.2% in LDB for YUV
    0.2%~0.4% at AI, -0.1%~0.4% at RA, 0.1%~1.0% in LDB for RGB
  Average gains for groups AHG 5 videos, for Y, U, V or G, B, R
    0.02%~0.05% at AI, -0.08%~0.12% at RA, -0.04%~0.25% in LDB for YUV
    0.1%~0.5% at AI, 0.2%~0.6% at RA, 0.3%~0.9% in LDB for RGB

## Slide 8: Results
Method 1+2
  Average gains for groups of AHG8 videos, for Y, U, V or G, B, R
    0.1%~0.3% at AI and RA,0.1%~1.2% in LDB for YUV
    0.1%~0.8% at AI, 0.3%~0.7% at RA, 0.1%~1.8% in LDB for RGB;
  Average gains for groups AHG 5 videos, for Y, U, V or G, B, R
    0.02%~0.05% at AI, -0.08%~0.12% at RA, -0.04%~0.25% in LDB for YUV
    0.1%~0.5% at AI, 0.3%~0.8% at RA, 0.4%~1.1% in LDB for RGB.

## Slide 9: Results
AHG 8 results for Method 1

## Slide 10: Results
AHG 8 results for Method 1+2

## Slide 11: Results
AHG 5 results for Method 1

## Slide 12: Results
AHG 5 results for Method 1+2

## Slide 13: Thank you for your attention!