## Slide 1
M. Horowitz, F. Kossentini and H. Tmar
JCT-VC 16th Meeting: San José, CA
9–17 Jan. 2014
Informal Subjective
Video Quality Comparison Between the
eBrisk-UHD HEVC and x264 AVC Encoders

## Slide 2: Objective
Compare the eBrisk-UHD (HEVC) encoder to the x264 (AVC) encoder in terms of subjective video quality and encoding speed
Employ encoder configurations consistent with 4K video streaming applications
Compare the eBrisk-UHD encoder to the HM 12 encoder for some of the 4K content

## Slide 3: Encoder Configuration
HEVC
  eBrisk-UHD encoder
  Main profile
AVC
  x264 version core 135 r2345 default configuration
  High profile
eBrisk-UHD configured to use ~60% fewer bits than x264

## Slide 4: Experimental Settings
Equipment and room conditions:
  55”, 4K Sony Bravia LED monitor
  1 subject at a time sat 1.5 meters from the monitor (centered)
  Darkened room
Video sequences were:
  Presented side-by-side
  Presented in a randomized double-blind fashion
  Displayed at native size
Five-degree evaluation scale:
  Left better, left slightly better, no preference, right slightly better and right better

## Slide 5: Test Sequences (YCrCb 4:2:0 8-bit)

## Slide 6: Subjective Test Results
No preference or eBrisk-UHD preferred in 69.4% of trials
Results suggest eBrisk-UHD achieved higher subjective video quality at ~60% lower bit rate compared with x264
Comparing eBrisk-UHD and HM 12 at the same average bit rate, approximately 40% preferred eBrisk-UHD encoder or had no preference

## Slide 7: Encoding Speed Comparison
Dual-Xeon-E5-2697-v2-based server
Speed measured using encoder configurations that produced subjective test sequences
Average 4K encoding speed
  eBrisk-UHD: >35 fps
  x264: 31 fps
  HM 12: 0.002 fps

## Slide 8: Demonstration
Sequences used in the viewing trials
Real-time encoding demonstration
  eBrisk-UHD encoder
  Dual Xeon E5-2690
  4K encoding at 30 fps