## Slide 1
Non-RCE4:
Palette prediction for palette coding
JCTVC-P0160
Guoxin Jin, Ankur Saxena and Felix Fernandes
Samsung Electronics, Co. Ltd.
Dallas R & D Research Center

## Slide 2: Motivation
Screen content video has similar colors in local areas
It will be good to re-use previous coded palettes to prevent transmitting colors in current palettes
Similar to Mediatek’s proposal JCTVC-P0096.
y
x
For example, CU x can re-use palette in y

## Slide 3: Motivation
However, there may exist ‘gap’ between two palette coded CUs.
y: Previous palette coded CU
z: Not palette coded
x: Current CU
Can benefit by using palette from the last CU on left coded using palette coding.
y
x
z

## Slide 4: Proposed Palette Prediction Schemes
Three schemes for palette prediction proposed:
Scheme A.1 : Search palette from CU’s located to the left of current CU. Search range constrained in current LCU
Scheme A.2 : Search palette from CU’s located to the left of current CU. Search range is constrained in one left LCU and current LCU
A.2 with no constraint: Search palette from CU’s located to the left of current CU. Search range is un-constrained

## Slide 5: Scheme A.1 Search Left within current LCU
Search to the left until it finds the first palette coded CU
If no palette until the left of LCU, terminate search.
Rate-Distortion (on top of O-0218)
  Palette of x
  Choose palette of y for x (prediction)
No additional R-D on top of P-0198.
y
x

## Slide 6: Scheme A.2 Search Left in LCU+Left LCU
Search to the left until it finds the first palette coded CU
If no palette until the left of LCU, terminate search.
Rate-Distortion (on top of O-0218)
  Palette of x
  Choose palette of y for x (prediction)
No additional R-D on top of P-0198.
y
x

## Slide 7: Scheme A.2 Unconstrained
Search to the left until it finds the first palette coded CU
No additional R-D on top of P-0198.
y
x

## Slide 8: Proposal highlights
Part 1: Anchor : RExt5.1 + JCTVC-O0218
  Bit-rate savings of:
  2.5 % for Lossy coding SC YUV 444
  3 % for Lossless coding SC YUV 444
Part 2 : Anchor: RExt5.1 + JCTVC-P0198 (RCE 4 test 2)
  1.4 % for Lossy coding SC YUV 444
  1.1 % for Lossless coding SC YUV 444

## Slide 9: Scheme A.1 Lossless Results on O-0218
Anchor: HM 12.1+RExt5.1 + O-0218
Proposal : HM 12.1+RExt5.1 + O-0218 + Scheme A.1 (Palette prediction in current LCU only)

## Slide 10: Scheme A.1 : Lossy results on O-0218
Anchor: HM 12.1+RExt5.1 + O-0218
Proposal : HM 12.1+RExt5.1 + O-0218 + Scheme A.1 (Palette prediction in current LCU only)

## Slide 11: Scheme A.2 Lossless Results on O-0218
Anchor: HM 12.1+RExt5.1 + O-0218
Proposal : HM 12.1+RExt5.1 + O-0218 + Scheme A.2 (Palette prediction in current + one left LCU only)

## Slide 12: Scheme A.2 : Lossy results on O-0218
Anchor: HM 12.1+RExt5.1 + O-0218
Proposal : HM 12.1+RExt5.1 + O-0218 + Scheme A.1 (Palette prediction in current + one left LCU only)

## Slide 13: Scheme A.2 Lossless Results on P-0198
Anchor: HM 12.1+RExt5.1 + P-0218
Proposal : HM 12.1+RExt5.1 + P-0218 + Scheme A.2 (Palette prediction in current + one left LCU only)

## Slide 14: Scheme A.2 : Lossy results on P-0198
Anchor: HM 12.1+RExt5.1 + P-0218
Proposal : HM 12.1+RExt5.1 + P-0218 + Scheme A.2 (Palette prediction in current + one left LCU only)

## Slide 15: Un-constrained Scheme A.2: Lossless Results on P-0198
Anchor: HM 12.1+RExt5.1 + P-0218
Proposal : Un-constrained Scheme A.2 (Palette prediction)

## Slide 16: Un-constrained Scheme A.2 : Lossy results on P-0198
Anchor: HM 12.1+RExt5.1 + P-0218
Proposal Un-constrained Scheme A.2 (Palette prediction)

## Slide 17: Conclusions
Proposed palette prediction schemes.
  Scheme A.1 :Search palette from CUs located in current LCU
  Scheme A.2: Search palette from all CUs in current+one left LCU
  Un-constrained scheme A.2
2.5 % gain for Lossy; and 3 % gain for lossless over
O-0218.
1.4 % gain for Lossy ; 1.1 % for Lossless over P-0198.
Recommend to test in AhG/CE.