## Slide 1: On 16-bit coding
A. Aminlou, K. Ugur
JCTVC-P0162

## Slide 2: Overview
Proposal: Seperate the 16-bit source into two 8-bit sources and code each 8-bit source with 8-bit HEVC.

## Slide 3: Results
Lossless coding, Intra configuration, number of frames = 50
Lossless coding, Low-delay configuration, number of frames = 50
 | bitrate (kbps) |  |  |  | Rate savings
Sequence | 16bit | MSB 8bit | LSB 8bit | MSB+LSB | 
CrowdRun | 5170146 | 1679605 | 2700102 | 4379706 | -15.3%
DucksTakeOff | 5280572 | 1734432 | 2700147 | 4434579 | -16.0%
InToTree | 4980271 | 1584147 | 2699054 | 4283200 | -14.0%
OldTownCross | 5219718 | 1701319 | 2699015 | 4400334 | -15.7%
ParkJoy | 4939025 | 1575163 | 2702194 | 4277357 | -13.4%
Average |  |  |  |  | -14.9%
 | bitrate (kbps) |  |  |  | Rate savings
Sequence | 16bit | MSB 8bit | LSB 8bit | MSB+LSB | 
CrowdRun | 4902434 | 1563738 | 2699941 | 4263680 | -13.0%
DucksTakeOff | 5203950 | 1699171 | 2700041 | 4399213 | -15.5%
InToTree | 4777475 | 1492226 | 2698961 | 4191187 | -12.3%
OldTownCross | 5075446 | 1623213 | 2698879 | 4322092 | -14.8%
ParkJoy | 4717655 | 1479947 | 2702016 | 4181962 | -11.4%
Average |  |  |  |  | -13.4%

## Slide 4: Update
Code the 16-bit original with two 12-bit low bit-depth sources
  MSB part is coded lossy
  LSB part is generated by taking the residual between original MSB and the reconstructed MSB
  LSB part is coded in a lossless manner
Additional coding efficiency is achieved as transform coding is utilized in coding MSB part.

## Slide 5: Results
MSB10bit (QP=13), LSB12bit (lossless) ,All Intra configuration, number of frames = 50
MSB10bit (QP=12), LSB12bit (lossless) , Low-delay configuration, number of frames = 50
 | bitrate (kbps) |  |  |  | Rate savings
Sequence | 16bit | MSB | LSB | MSB+LSB | 
CrowdRun | 5170146 | 1100126 | 3120699 | 4220825 | -18.4%
DucksTakeOff | 5280572 | 1178481 | 3116777 | 4295258 | -18.7%
InToTree | 4980271 | 1008456 | 3124676 | 4133132 | -17.0%
OldTownCross | 5219718 | 1147577 | 3117242 | 4264819 | -18.3%
ParkJoy | 4939025 | 1000396 | 3121820 | 4122216 | -16.5%
Average |  |  |  |  | -17.8%
 | bitrate (kbps) |  |  |  | Rate savings
Sequence | 16bit | MSB | LSB | MSB+LSB | 
CrowdRun | 4902434 | 918960.1 | 3213495 | 4132455 | -15.7%
DucksTakeOff | 5203950 | 1074202 | 3205133 | 4279335 | -17.8%
InToTree | 4777475 | 861407.6 | 3219510 | 4080918 | -14.6%
OldTownCross | 5075446 | 1020216 | 3205216 | 4225432 | -16.7%
ParkJoy | 4717655 | 826333.2 | 3223275 | 4049608 | -14.2%
Average |  |  |  |  | -15.8%

## Slide 6: Conclusions
The proposal could be implemented in two ways:
  The MSB and LSB part could be packed into and frame packing arrangement SEI message could be used.
  The LSB part could be signaled as an auxiliary picture layer and MSB picture could be the base picture.
Conclusion: 16-bit lossless coding is seen as an important area (e.g. Coding of medical content).
Benefits of this proposal:
  Improved coding efficiency for 16-bit lossless coding
  Backwards compatibility to HEVC low bit depth coders