## Slide 1: JCTVC-P0164: Chroma phase offset for SHVC resampling process
K. Rapaka, Jianle Chen, Marta Karczewicz (Qualcomm)

## Slide 2: Chroma samples location relatively to luma samples
SHVC : position ‘b’ (half luma sample shift vertically, no shift horizontally)
4:2:0 sampling from 4:4:4 information is not specified as mandatory information in decoding process, though it is needed to accurately derive reference layer sample location in resampling process.

## Slide 3: Test Method
This topic has been extensively discussed in the past JCTVC meetings. However no concrete decision was made due to the lack of appropriate test results and coding impact analysis.
Five 4:4:4 sequences are used located @ ftp.tnt.uni-hannover.de /testsequences/FrExt-candidate-sequences - BirdsInCage_1920x1080_60_10bit_444.zip - CrowdRun_1920x1080_50_10bit_444.zip - Kimono1_1920x1080_24_10bit_444.zip - EBURainFruits_1920x1080_50_10bit_444_ebu.zip - BigBuck_1920x1080_60p_8b444.zip
4:4:4 10-bit to 4:2:0 8 bit conversion using 2D separable 12-tap filters used in SHVC downsampler for all the 6 chroma positions {0, 2, -3, -9, 6, 39, 58, 39, 6, -9, -3, 2, 0}, {0, 1, 0, -7, -5, 22, 53, 53, 22, -5, -7, 0, 1},
The 4:2:0 generated sequences are down-sampled using SHM4.0_dev downsampler (considering the accurate chroma sample position )

## Slide 4: Coding efficiency results
The coding gain by considering the actual chroma sample position in resampling process, compared to SHM4.0, provides –0.1% to –0.4% BD rate saving.

## Slide 5: Coding efficiency results

## Slide 6: Coding efficiency results Contd…

## Slide 7: Additional Results
The coding gain by considering the actual chroma sample position in resampling process, compared to using chroma position ‘a’, provides –0.1% to –0.9% BD rate saving.

## Slide 8: Additional Results Contd…

## Slide 9: Additional Results Contd…

## Slide 10: Proposal
Based on the results we recommend a schemes to be used in SHVC to solve chroma sample location issue.
  Signal chroma sampling position information in VPS and consider the actual chroma sample position in resampling process.
H.6.2 Derivation process for reference layer sample location used in resampling
phaseX = ( cIdx = = 0 ) ? ( cross_layer_phase_alignment_flag << 1 ) : cross_layer_phase_alignment_flag + chroma_phase_X (H‑5) phaseY = ( cIdx = = 0 ) ? ( cross_layer_phase_alignment_flag << 1 ) : cross_layer_phase_alignment_flag + chroma_phase_Y (H‑6)

## Slide 11: Conclusion
We prefer a scheme in SHVC that considers the actual chroma sample position in resampling process
We would like to thank Interdigital for cross-checking the proposal.