## Slide 1: Some Syntax Modifications for HEVC Range Extension JCTVC-P0166
Yue Yu and Limin Wang Arris Group Inc.

## Slide 2: Conditionally Parsing PPS extension Syntax
Problem: 1. pps_extension2_flag is conditionally parsed by checking the value of pps_extension1_flag. However, pps_extension2_flag is always checked no matter it is present or not.
2. The later standardized extension must include syntax elements related to the previous standardized extension, even if those extensions are not related.
.......... | 
pps_extension1_flag | u(1)
if( pps_extension1_flag ) { | 
if( transform_skip_enabled_flag ) | 
log2_max_transform_skip_block_size_minus2 | ue(v)
luma_chroma_prediction_enabled_flag | u(1)
chroma_qp_adjustment_enabled_flag | u(1)
if( chroma_qp_adjustment_enabled_flag ) { | 
diff_cu_chroma_qp_adjustment_depth | ue(v)
chroma_qp_adjustment_table_size_minus1 | ue(v)
for( i = 0; i <= chroma_qp_adjustment_table_size_minus1; i++ ) { | 
cb_qp_adjustment[ i ] | se(v)
cr_qp_adjustment[ i ] | se(v)
} | 
} | 
pps_extension2_flag | u(1)
} | 
if( pps_extension2_flag ) | 
while( more_rbsp_data( ) ) | 
pps_extension_data_flag | u(1)
rbsp_trailing_bits( ) | 
} | 

## Slide 3
Proposal :
1. add additional flags to indicate further extension syntax elements if pps_extension_present_flag is equal to 1. Each individual flag controls whether the specific extension syntax are present.
2. A 7-bit syntax is used to indicate further extension.
3. Harmonize PPS level extension syntax with SPS level design (JCTVC-O0142).

## Slide 5: Modifications of Transform Skip Related Syntax
Three transform skip related syntax, transform_skip_rotation_enabled_flag , transform_skip_context_enabled_flag and log2_max_transform_skip_block_size_minus2, are added for range extension.
Two of them are present at SPS and one is present at PPS in the current spec.
Current spec. : transform_skip_rotation_enabled_flag equal to 1 specifies that a rotation is applied to the residual data block for intra 4x4 blocks, with the exception of blocks using intra block copying prediction, coded using a transform skip operation. transform_skip_rotation_enabled_flag equal to 0 specifies that this rotation is not applied. When not present, the value of transform_skip_rotation_enabled_flag is inferred to be equal to 0.

## Slide 6
Two SPS syntax will be used if either transform_skip_rotation_enabled_flag or transquant_bypass_enabled_flag is equal to 1.
Proposal
1. Present all transform skip related syntax at PPS level.
2. transform_skip_rotation_enabled_flag , transform_skip_context_enabled_flag should be conditionally parsed if transform_skip_enabled_flag or transquant_bypass_enabled_flag is equal to 1.

## Slide 9: Simplification of Intra Block Copy Syntax
If intra_block_copy_enabled_flag is equal to 1, a one-bit intra_bc_flag is always coded except the current CU is inter skip mode. The status of intra_bc_flag indicates whether intra block copy is used or not. It may check the status of intra_bc_flag up to three times.
Proposal 1: only one time check of the status of intra_bc_flag without any performance change. The spec. is more clean.
When intra_bc_flag is 1, CuPredMode[ x ][ y ] is inferred to be equal to MODE_INTRA. Therefore, the check of CuPredMode[ x0 ][ y0 ] = = MODE_INTRA && intra_bc_flag[ x0 ][ y0 ] is equivalent to the check of intra_bc_flag[ x0 ][ y0 ]
Proposal 2: simplify (CuPredMode[ x0 ][ y0 ] = = MODE_INTRA && intra_bc_flag[ x0 ][ y0 ]) to intra_bc_flag[ x0 ][ y0 ]