## Slide 1: AHG14: Extension of SNR scalability with bit-depth scalability
Cheung Auyeung, Ohji Nakagmi, Kazushi Sato
Sony Electronics Inc. and Sony Corporation
Jan 9, 2014

## Slide 2: HEVC Scalable Extension Draft 4
Input
BT.709
Input
BT.2020
Base Layer
Encoding Loop
Enhancement Layer
Encoding Loop
(Weighted Prediction)
Base Layer
Reference
Bitstream
Multiplex
Enhancement Layer
Reference
Joint
Upsampling
and bit-shift
4K 10 bits
1080P 8 bits
SHVC Draft 4 support joint
spatial & color space Scalability
Color
Space 2
Color
Space 1
Base Layer
Encoding Loop
Enhancement Layer
Encoding Loop (Weighted Prediction)
Base Layer
Reference
Bitstream
Multiplex
Enhancement Layer
Reference
bit-shift
1080P 10 bits
1080P 8 bits
SHVC Draft 4 does not support
bit-depth and color space scalability
when BL and EL have same picture size
and zero offset.

## Slide 3: Use Cases
Pro choice for the user
  In this internet age, the user may decide to use the same picture size in the BL and EL especially when those contents are available.
    For example, SCE1 distribute BT.709 videos in both 8 bits and 10 bits.
High dynamic range (HDR) and low dynamic range (LDR) video coding
  LDR in BL
  HDR in EL
  Same picture size in BL and EL.

## Slide 4: Application of SHVC for HDR Coding
LDR
HDR
Base Layer
Encoding Loop
Enhancement Layer
Encoding Loop with
Weighted Prediction
Base Layer
Reference
Bitstream
Multiplex
Enhancement Layer
Reference
Inverse
Tone Mapping
Propose to support joint bit-depth and color space scalability when picture size of BL and EL are the same.
A use case is to encode high dynamic range (HDR) video and the corresponding low dynamic range (LDR) video.
  Both HDR and LDR video have the same picture size.
Tone Mapping
12 bits
8 bits
Same Picture Size
Different Bit-Depth
Different Color

## Slide 5: Results
Implemented in SCE1 anchor
Tested with SCE1 BT.709 videos
  8 bits for BL input
  10 bits for EL input
 | AI HEVC 1x 8-bit base |  | 
 | Y | U | V
Overall (Test vs single layer) | 13.5% | 13.9% | 13.2%
Overall (Test EL+BL vs single EL+BL) | -27.9% | -28.7% | -28.7%
 | RA HEVC 1x 8-bit base |  | 
 | Y | U | V
Overall (Test vs single layer) | 24.2% | 28.7% | 25.6%
Overall (Test EL+BL vs single EL+BL) | -18.9% | -16.5% | -17.8%

## Slide 6: Conclusion
Propose to add SNR scalability to the CGS studies.
Propose to add bit-shift with SNR scalability to SHM WD.