## Slide 1: JCTVC-P0205_Non-RCE3: Intra block copy syntax clean up
Xiaozhong Xu, Kai Zhang, Xianguo Zhang, Shan Liu, Shawmin Lei

## Slide 2: On CU level IntraBC Signaling
Binary tree of CU prediction modes in current Rext.
Binary tree of CU prediction modes in this contribution.

## Slide 3: Syntax Change
coding_unit( x0, y0, log2CbSize ) { | Descriptor
if( transquant_bypass_enabled_flag ) | 
cu_transquant_bypass_flag | ae(v)
if( slice_type != I ) | 
cu_skip_flag[ x0 ][ y0 ] | ae(v)
nCbS = ( 1 << log2CbSize ) | 
if( cu_skip_flag[ x0 ][ y0 ] ) | 
prediction_unit( x0, y0, nCbS, nCbS ) | 
else { | 
if( intra_block_copy_enabled_flag ) | 
intra_bc_flag[ x0 ][ y0 ] | ae(v)
if( !intra_bc_flag[ x0 ][ y0 ] ) { | 
if( slice_type != I ) | 
pred_mode_flag | ae(v)
if( intra_block_copy_enabled_flag && pred_mode_flag) | 
intra_bc_flag[ x0 ][ y0 ] | ae(v)
if( !intra_bc_flag[ x0 ][ y0 ] ¦ ¦ (CuPredMode[ x0 ][ y0 ] != MODE_INTRA ¦ ¦ log2CbSize = = MinCbLog2SizeY) ) | 
part_mode | ae(v)
} | 
...... | 
pred_mode_flag is inferred to 1 when not present.

## Slide 4: Summary of the simulation results:
Identical results as anchor in All-Intra configurations
For lossless simulation in RA and LD,
  Delta BD-rate range for this change is
    0.0% for mandatory sequences.
    -0.4% to 0.1% for optional sequences.
For lossy simulation in RA and LD,
  Delta BD-rate range for this change is
    -0.2% to 0.2% for mandatory sequences.
    -1.1% to 0.2% for optional sequences.

## Slide 5: Conclusion
Propose to enable intra_bc_flag signaling when pred_mode_flag is 1 (intra coded CU)
Syntax wise, better classify IntraBC as an intra-picture coding tools
Performance wise, on average no impact on mandatory sequences, some small gain (~1%) observed for screen content optional sequences.

## Slide 6: Thank you for your attention!