## Slide 1
Tile Based Resampling for SHVC
JCTVC-P0215
Robert Skupin, Karsten Sühring, Yago Sanchez, Thomas Schierl

## Slide 2: Problem Statement
Tile- and layer-parallelization for SHVC
EL tile processing can commence only after corresponding BL area is resampled
Inter-Layer constrained Tile Sets (ILCTS) signal related encoder-constraint
Reference layer
Current layer

## Slide 3: ILCTS coding penalty
Anchor:
SHM4.0, CTC, uniformly spaced aligend tiles structure
no ILCTS
Test:
Implementation of ILCTS on PU level
Tile structures: 2x2 and 3x2

## Slide 4: ILCTS coding penalty
ILCTS implemenation on PU level
2x2 tile structure
3x2 tile structure
 | HEVC 2x |  |  | HEVC 1.5x |  | 
AI Overall (Test vs Ref) | 1.7% | 2.2% | 2.2% | 2.4% | 3.3% | 3.3%
RA Overall (Test vs Ref) | 1.1% | 0.9% | 0.8% | 1.8% | 1.9% | 1.8%
LD-B Overall (Test vs Ref) | 0.6% | 0.5% | 0.5% | 1.4% | 1.4% | 1.4%
 | HEVC 2x |  |  | HEVC 1.5x |  | 
AI Overall (Test vs Ref) | 2.2% | 2.9% | 2.9% | 3.1% | 4.3% | 4.3%
RA Overall (Test vs Ref) | 1.4% | 1.2% | 1.1% | 2.3% | 2.5% | 2.2%
LD-B Overall (Test vs Ref) | 0.8% | 0.6% | 0.7% | 1.8% | 1.8% | 1.7%

## Slide 5: Proposal
Tile Based Resampling:
Obey tile structure of current layer for reference resampling
Superior coding performance wrt ILCTS
2x2 tile structure
3x2 tile structure
 | HEVC 2x |  |  | HEVC 1.5x |  | 
AI Overall (Test vs Ref) | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1%
RA Overall (Test vs Ref) | 0.1% | 0.0% | 0.1% | 0.0% | 0.0% | 0.1%
LD-B Overall (Test vs Ref) | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1%
 | HEVC 2x |  |  | HEVC 1.5x |  | 
AI Overall (Test vs Ref) | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.2%
RA Overall (Test vs Ref) | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1%
LD-B Overall (Test vs Ref) | 0.1% | 0.0% | 0.1% | 0.1% | 0.1% | 0.0%

## Slide 6: Proposal
Tile Based Resampling:
Syntax element in SPS multilayer extension resampling_across_tiles_enabled_flag
Modifications to H.8.1.4.1.X
Luma|Chroma sample interpolation process
Introduce derivation process for boundary sample positions
Specification text available

## Slide 7: Summary
SHVC tile- and layer-parallelization
ILCTS scheme impacts coding performance significantly
Proposal: Tile Based Resampling
Specification text, software and results available
Superior coding performace wrt ILCTS scheme
TBR vs ILCTS for 3x2 tile structure
 | HEVC 2x |  |  | HEVC 1.5x |  | 
AI Overall (Test vs Ref) | -2.0% | -2.7% | -2.7% | -3.0% | -4.0% | -4.0%
RA Overall (Test vs Ref) | -1.3% | -1.1% | -1.0% | -2.2% | -2.3% | -2.1%
LD-B Overall (Test vs Ref) | -0.8% | -0.6% | -0.6% | -1.7% | -1.7% | -1.7%