## Slide 1: Additional content interpretation type and experiments for frame packing arrangement SEI message for 4:4:4 content in 4:2:0 bitstreams JCTVC-P0216
S. Reddy, S. Kanumuri, Y. Wu, S. Sadhwani, G. J. Sullivan, and H. S. Malvar
16th Meeting: San Jose, USA 9 January–17 January, 2014

## Slide 2
Motivation
Variety of emerging applications that operate on screen content (4:4:4 YUV format)
Most of current video codec deployments utilize 4:2:0 format i.e. do not support the 4:4:4 format currently
The ability to convey 4:4:4 YUV content through conventional 4:2:0 decoders is highly desirable, for quicker and wide-spread deployment of 4:4:4 content.
Y444
U444
V444
B1
B2
B3
B6
B7
B8
B9
B4
B5
Main view
(YUV 4:2:0 frame)
Auxiliary view
(YUV 4:2:0 frame)
YUV 4:4:4
Frame Packing

## Slide 3: Different approaches
Three approaches are proposed
  Direct mode with/without anti-alias filtering
  Band-separation filtering
  Lifting-based band separation filtering
Can be added as simple pre-post processing stages to the encoder/decoder.
Discussion and mathematical equations are detailed in the contribution draft

## Slide 4: Evaluation
Lifting-based band separation has generally superior performance
Frame packing (Lifting/non-lifting band separation) becomes more competitive to HM444 at lower bitrates where quantization error dominates
Chart: sc_word_editing_1280x720
| 8345.1551999999992 | 5788.1472000000003 | 3617.9135999999999 | 2191.6992 | 1360.752
Direct | 43.3884 | 39.7871 | 36.3839 | 34.7773 | 33.6962
BandSeparation | 46.1762 | 42.3806 | 38.5558 | 37.1496 | 36.0834
HM444 | 51.8546 | 47.9459 | 43.7038 | 40.1069 | 37.7002
Lifted Band-sep | 48.4368 | 44.5621 | 40.3775 | 37.8533 | 36.5024
Figure 1: Sample BD-plot (Chroma) for different packing approaches

## Slide 5: Discussion
A few sequences are operating in the “flat” part of the BD-graph (slight changes in chroma psnr need many bits).
Varying the Chroma QP-delta affects both the BDrate-Y and Bdrate-U/V curves
Hence, manual inspection of the BD-plots (both Y and U/V) is encouraged to understand the performance
Chart: BirdsInCage_10bit_1920x1080
| 104206.40640000001 | 23990.774399999998 | 2923.5360000000001 | 565.30560000000003 | 308.0256
Direct | 40.5862 | 39.1551 | 38.1679 | 37.263 | 36.3004
BandSeparation | 41.8687 | 40.4398 | 39.6576 | 39.0619 | 38.3939
HM444 | 44.071 | 41.9039 | 40.535 | 39.9851 | 39.2544
Lifted Band-sep | 43.7187 | 41.4531 | 39.9763 | 39.2405 | 38.6583

## Slide 6: Conclusion
Proposed frame packing approaches provide the ability to transmit 4:4:4 content over 4:2:0 channels
Simple architecture – only pre-processing and post-processing steps required. No decoder functionality changes are required.
Other approaches for transmitting 4:4:4 content (single-layer 4:4:4 codec, auxiliary pictures: JCTVC-P0122) are complementary to current contribution.
  They also require decoder capability beyond that of an ordinary 4:2:0 decoder