## Slide 1: AhG 18: On SAO performance at high bit-depth and high bit-rate
Samsung Electronics, Ltd., Qualcomm Inc,
Apple Inc, MediaTek Inc.

## Slide 2: AhG 8 Lossy test
Code base:
Rext s/w 5.0.1
Anchor:
SAO ON
Test:
SAO OFF
 | All Intra Main-tier |  |  | All Intra High-tier |  |  | All Intra Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | 1,3% | 3,4% | 4,6% | 1,2% | 2,4% | 3,3% | 0,8% | 1,4% | 1,9%
Class B | 0,6% | 0,1% | 0,4% | 0,4% | 0,2% | 0,4% | 0,1% | 0,1% | 0,3%
RGB 4:4:4 SC | 2,8% | 1,6% | 2,0% | 2,7% | 1,6% | 1,9% | 2,3% | 1,3% | 1,4%
RGB 4:4:4 Animation | 0,7% | 1,4% | 1,4% | 0,7% | 1,4% | 1,3% | 0,4% | 0,9% | 0,8%
YCbCr 4:4:4 SC | 3,4% | 2,7% | 3,2% | 2,9% | 2,3% | 2,7% | 2,2% | 1,7% | 2,0%
YCbCr 4:4:4 Animation | 0,6% | 2,0% | 1,8% | 0,6% | 1,9% | 1,8% | 0,4% | 1,7% | 1,5%
RangeExt | 0,4% | 0,3% | 0,7% | 0,5% | 0,5% | 0,7% | 0,4% | 0,4% | 0,7%
RGB 4:4:4 SC (Optional) | 3,4% | 2,3% | 2,3% | 3,4% | 2,8% | 2,9% | 2,9% | 2,5% | 2,6%
YCbCr 4:4:4 SC (Optional) | 3,6% | 3,8% | 2,5% | 3,6% | 3,7% | 2,5% | 3,2% | 3,4% | 2,1%
 | Random Access Main-tier |  |  | Random Access High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | 2,5% | 4,7% | 6,7% | 2,5% | 3,6% | 4,8% |  |  | 
Class B | 0,7% | 0,8% | 0,7% | 1,2% | 1,1% | 0,4% |  |  | 
RGB 4:4:4 SC | 5,1% | 3,2% | 3,7% | 4,8% | 3,3% | 3,7% |  |  | 
RGB 4:4:4 Animation | 0,7% | 1,0% | 0,9% | 0,8% | 0,9% | 0,8% |  |  | 
YCbCr 4:4:4 SC | 6,4% | 4,4% | 5,1% | 5,7% | 3,8% | 4,5% |  |  | 
YCbCr 4:4:4 Animation | 0,6% | 2,1% | 1,9% | 0,7% | 2,0% | 1,9% |  |  | 
RangeExt | 0,8% | 3,8% | 1,9% | 1,4% | 7,3% | 3,3% |  |  | 
RGB 4:4:4 SC (Optional) | 4,1% | 3,1% | 3,2% | 4,3% | 3,7% | 4,0% |  |  | 
YCbCr 4:4:4 SC (Optional) | 3,9% | 5,9% | 4,2% | 4,3% | 5,2% | 3,8% |  |  | 
 | Low delay B Main-tier |  |  | Low delay B High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | 5,3% | 8,5% | 11,8% | 4,9% | 7,0% | 9,1% |  |  | 
Class B | 1,1% | 1,8% | 2,4% | 1,5% | 3,1% | 2,7% |  |  | 
RGB 4:4:4 SC | 7,0% | 5,5% | 6,0% | 6,3% | 5,1% | 5,5% |  |  | 
RGB 4:4:4 Animation | 1,5% | 2,3% | 1,9% | 1,9% | 2,4% | 2,0% |  |  | 
YCbCr 4:4:4 SC | 10,4% | 6,4% | 7,0% | 8,9% | 5,5% | 6,2% |  |  | 
YCbCr 4:4:4 Animation | 1,0% | 5,4% | 5,0% | 1,1% | 5,6% | 5,3% |  |  | 
RangeExt | 0,9% | 3,4% | 2,5% | 1,3% | 5,0% | 4,0% |  |  | 
RGB 4:4:4 SC (Optional) | 7,6% | 7,3% | 8,4% | 9,0% | 8,2% | 8,5% |  |  | 
YCbCr 4:4:4 SC (Optional) | 5,6% | 7,7% | 5,4% | 6,0% | 8,2% | 6,1% |  |  | 
Screen content | 4,9% |  |  | 4,4% |  |  |  |  | 
Camera captured 8 b | 0,8% |  |  | 1,0% |  |  |  |  | 
Camera captured 10 b | 0,7% |  |  | 1,1% |  |  |  |  | 

## Slide 3: AhG18 test
Code base:
  Rext s/w 5.0.1
Anchor:
  SAO ON
Test:
  SAO OFF
In majority of cases SAO off is selected by encoder
 |  |  | Average BD-rate Change (%) - All Tiers |  |  |  |  |  |  |  |  |  |  | 
 |  |  | Intra 16-bit (internal bit depth) |  |  | Intra 12-bit (internal bit depth) |  |  | Lowdelay 16-bit (internal bit depth) |  |  | Lowdelay 12-bit (internal bit depth) |  | 
 |  |  | Y/G | Cb/B | Cr/R | Y/G | Cb/B | Cr/R | Y/G | Cb/B | Cr/R | Y/G | Cb/B | Cr/R
SVT |  |  | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0%
RExt RGB |  |  | 0,0% | 0,0% | 0,0% | 0,0% | 0,1% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,1% | 0,0%
HDR |  |  | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,1% | 0,0% | 0,0%
4K from HDR |  |  | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% |  |  |  |  |  | 
HDR 4:0:0 Medical |  |  | 0,0% |  |  | 0,0% |  |  | 0,0% |  |  | 0,1% |  | 
4:0:0 Medical |  |  | 0,0% |  |  | 0,0% |  |  | 0,0% |  |  | 0,0% |  | 
Synthetic RGB HDR (+2 MSBs) |  |  | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,1% | 0,0% | 0,0% | 0,0% | 0,2% | 0,1% | 0,1%
Synthetic RGB HDR (+4 MSBs) |  |  | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,1% | 0,0% | 0,0% | 0,0% | 0,4% | 0,1% | 0,1%
Synthetic RGB HDR (+6 MSBs) |  |  | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | -0,1% | -0,1%
All Classes |  |  | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,1% | 0,0% | 0,0%

## Slide 4: Summary of tests
AhG | Internal bitDepth | QP | PSNR, dB | SAO gain non- SC | SAO gain SC
8 | 8 | 37…12 | 32…53 | 0.9% | 4.7%
8 | 10 | 37…12 | 30…43 | 0.9% | NA
18 | 12 | 8…–12 | 55...75 | <0.1% | NA
18 | 16 | –16…–37 | 78…99 | 0.0% | NA
8 bits
10 bits
12 bits
16 bits
PSNR
32..53 dB
55...75 dB
78...99 dB
Additional tests
12 & 16 bits
27..61 dB

## Slide 5: SAO parameters derivation at encoder side
SAO encoder
  collects following statistics for each SAO class
    diff– accumulated difference between Orig and Rec
    count - total amount of samples of this class
  Offsets value calculation:
    Ratio  rounding  clipping
    quantOffsets =Clip3(-Th, Th, [ diff/count ] >> ( bitDepth − 10) )
    Th = (1<<( bitDepth − 10))-1
Under AhG18 test conditions
    PSNR is high  error to be corrected by SAO is very small
      |diff| ~ count
    After quantization resulting
      quantOffsets= 0 (almost always)
    Encoder turns SAO off

## Slide 6: Solution 1
Quantization removal for SAO magnitude
  SaoOffset = offsetSign * saoOffsetAbs << ( bitDepth − Min( bitDepth, 10 ) ),
Effect:
  No samples processing chance
  One shift removed during SaoOffset calculation
  quantOffsets become non-zero

## Slide 7: Solution 2
EO classification modification
  Current:
    z1 = px − px-1; z2 = px − px+1
    edgeIdx = 2 + Sign(z1) + Sign( z2)
  Proposed #1:
    edgeIdx = 2+ Sign( (z1+roundOffset)>>N + Sign( (z2+roundOffset)>>N )
  Proposed #2:
    edgeIdx = 2 + Sign( ((px )>>N ) − ((px-1 )>>N ))
    + Sign( ((px )>>N ) − ((px+1 )>>N ))
  N = ( bitDepth − Min( bitDepth, 10 ) ),
  roundOffset = (1<<(N-1)).
Effects:
  |diff| > count  increases the magnitude of SAO values
  Sample processing has to be modified compare to HEVC

## Slide 8: Quantization removal for SAO magnitude
Code base:
  Rext s/w 5.0.1
Anchor:
  SAO ON
Test:
  SAO ON, no quantization, magnitude range -31….31 (decoded) / -5….5 (actual)
 |  |  | Average BD-rate Change (%) - All Tiers |  |  |  |  |  |  |  |  |  |  | 
 |  |  | Intra 16-bit (internal bit depth) |  |  | Intra 12-bit (internal bit depth) |  |  | Lowdelay 16-bit (internal bit depth) |  |  | Lowdelay 12-bit (internal bit depth) |  | 
 |  |  | Y/G | Cb/B | Cr/R | Y/G | Cb/B | Cr/R | Y/G | Cb/B | Cr/R | Y/G | Cb/B | Cr/R
SVT |  |  | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0%
RExt RGB |  |  | 0,0% | -0,1% | 0,0% | -0,1% | -0,1% | -0,1% | 0,0% | 0,0% | 0,0% | -0,2% | -0,1% | -0,1%
HDR |  |  | 0,0% | 0,0% | 0,0% | -0,2% | -0,3% | -0,3% | 0,0% | 0,0% | 0,0% | -0,7% | -0,8% | -0,7%
4K from HDR |  |  | 0,0% | 0,0% | 0,0% | 0,0% | -0,1% | 0,0% |  |  |  |  |  | 
HDR 4:0:0 Medical |  |  | 0,0% |  |  | -0,5% |  |  | -0,1% |  |  | -2,3% |  | 
4:0:0 Medical |  |  | 0,0% |  |  | -0,2% |  |  | 0,0% |  |  | -0,4% |  | 
Synthetic RGB HDR (+2 MSBs) |  |  | 0,0% | 0,0% | 0,0% | -0,3% | -0,1% | -0,6% | 0,0% | 0,0% | 0,0% | -1,2% | -1,0% | -1,1%
Synthetic RGB HDR (+4 MSBs) |  |  | 0,0% | 0,0% | -0,1% | -1,1% | -0,7% | -1,8% | -0,1% | -0,1% | -0,2% | -4,8% | -2,8% | -3,3%
Synthetic RGB HDR (+6 MSBs) |  |  | -0,3% | -0,1% | -0,7% | -2,6% | -1,8% | -4,4% | -1,3% | -1,1% | -1,2% | -6,7% | -3,4% | -4,6%
All Classes |  |  | 0,0% | 0,0% | -0,1% | -0,5% | -0,4% | -1,0% | -0,2% | -0,2% | -0,2% | -2,1% | -1,4% | -1,6%

## Slide 9: EO classification change #1
Code base:
  Rext s/w 5.0.1
Anchor:
  SAO ON
Test:
  SAO ON, no quantization, magnitude range -31….31, EO classification is modified (method #1)
 |  |  | Average BD-rate Change (%) - All Tiers |  |  |  |  |  |  |  |  |  |  | 
 |  |  | Intra 16-bit (internal bit depth) |  |  | Intra 12-bit (internal bit depth) |  |  | Lowdelay 16-bit (internal bit depth) |  |  | Lowdelay 12-bit (internal bit depth) |  | 
 |  |  | Y/G | Cb/B | Cr/R | Y/G | Cb/B | Cr/R | Y/G | Cb/B | Cr/R | Y/G | Cb/B | Cr/R
SVT |  |  | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0%
RExt RGB |  |  | 0,0% | -0,1% | 0,0% | -0,1% | 0,0% | -0,1% | 0,0% | 0,0% | 0,0% | -0,2% | -0,1% | -0,1%
HDR |  |  | 0,0% | 0,0% | 0,0% | -0,2% | -0,3% | -0,3% | 0,0% | 0,0% | 0,0% | -0,6% | -0,7% | -0,7%
4K from HDR |  |  | 0,0% | 0,0% | 0,0% | 0,0% | -0,1% | 0,0% |  |  |  |  |  | 
HDR 4:0:0 Medical |  |  | 0,0% |  |  | -0,5% |  |  | 0,0% |  |  | -2,1% |  | 
4:0:0 Medical |  |  | 0,0% |  |  | -0,2% |  |  | 0,0% |  |  | -0,6% |  | 
Synthetic RGB HDR (+2 MSBs) |  |  | 0,0% | 0,0% | 0,0% | -0,3% | -0,2% | -0,8% | 0,0% | 0,0% | 0,0% | -1,3% | -1,2% | -1,2%
Synthetic RGB HDR (+4 MSBs) |  |  | 0,0% | 0,0% | 0,0% | -0,8% | -0,7% | -1,4% | 0,0% | 0,0% | 0,0% | -2,6% | -0,8% | -1,4%
Synthetic RGB HDR (+6 MSBs) |  |  | 0,0% | 0,0% | 0,0% | -0,5% | -0,5% | -1,3% | 0,0% | 0,0% | 0,0% | -1,0% | -0,4% | -0,4%
All Classes |  |  | 0,0% | 0,0% | 0,0% | -0,3% | -0,2% | -0,6% | 0,0% | 0,0% | 0,0% | -1,0% | -0,5% | -0,6%

## Slide 10: EO classification change #2
Code base:
  Rext s/w 5.0.1
Anchor:
  SAO ON
Test:
  SAO ON, no quantization, magnitude range -31….31, EO classification is modified (method #2)
 |  |  | Average BD-rate Change (%) - All Tiers |  |  |  |  |  |  |  |  |  |  | 
 |  |  | Intra 16-bit (internal bit depth) |  |  | Intra 12-bit (internal bit depth) |  |  | Lowdelay 16-bit (internal bit depth) |  |  | Lowdelay 12-bit (internal bit depth) |  | 
 |  |  | Y/G | Cb/B | Cr/R | Y/G | Cb/B | Cr/R | Y/G | Cb/B | Cr/R | Y/G | Cb/B | Cr/R
SVT |  |  | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0%
RExt RGB |  |  | 0,0% | -0,1% | 0,0% | -0,1% | -0,1% | -0,1% | 0,0% | 0,0% | 0,0% | -0,2% | -0,1% | -0,1%
HDR |  |  | 0,0% | 0,0% | 0,0% | -0,1% | -0,3% | -0,3% | 0,0% | 0,0% | 0,0% | -0,7% | -0,7% | -0,7%
4K from HDR |  |  | 0,0% | 0,0% | 0,0% | 0,0% | -0,1% | 0,0% |  |  |  |  |  | 
HDR 4:0:0 Medical |  |  | 0,0% |  |  | -0,3% |  |  | 0,0% |  |  | -1,9% |  | 
4:0:0 Medical |  |  | 0,0% |  |  | -0,2% |  |  | 0,0% |  |  | -0,5% |  | 
Synthetic RGB HDR (+2 MSBs) |  |  | 0,0% | 0,0% | 0,0% | -0,3% | -0,1% | -0,7% | 0,0% | 0,0% | 0,0% | -1,2% | -1,1% | -1,1%
Synthetic RGB HDR (+4 MSBs) |  |  | 0,0% | 0,0% | -0,1% | -0,6% | -0,6% | -1,2% | -0,1% | 0,0% | -0,1% | -3,6% | -1,6% | -2,0%
Synthetic RGB HDR (+6 MSBs) |  |  | 0,0% | 0,0% | -0,2% | -0,6% | -0,7% | -1,6% | -0,2% | -0,1% | -0,1% | -3,1% | -1,0% | -1,2%
All Classes |  |  | 0,0% | 0,0% | 0,0% | -0,2% | -0,3% | -0,6% | 0,0% | 0,0% | 0,0% | -1,4% | -0,8% | -0,8%

## Slide 11: Brief summary
Removal of quantization for SAO magnitudes improves BD-rate performance
  1,3% (avg 12 bits test, PSNR 55..75 dB)
  0,2% (avg 16 bits test, PSNR 78..99 dB)
EO classification change gives no additional gain on top of quantization removal
Test | AI-16 | AI-12 | LD-16 | LD-12
SAO disabled | 0.0% | 0.0% | 0.0% | 0.0%
no SAO parameters quantization | 0.0% | -0.5% | -0.2% | -2.1%
no SAO parameters quantization + EO classification modified #1 | 0.0% | -0.3% | 0.0% | -1,0%
no SAO parameters quantization + EO classification modified #2 | 0.0% | -0.2% | -XX% | -1,4%

## Slide 12: Conclusion
Based on tests data provided (1,3% average BD-rate gain in 12 bits AhG18 test) it is proposed
  to optionally (e.g. with a PPS switch) or always (based on bitdepth) remove the quantization step of the SAO magnitude value for higher bitdepth content.
  Continue investigating the quantization process for the Edge Classification method using different quantization values and adaptation mechanisms.

## Slide 13: Additional test requested
Test | AI-16 | AI-12 | LD-16 | LD-12
AhG 18 QPs (-16…-37 16b, 8…-12 12b) |  |  |  | 
Rext 5.0.1 vs Rext 5.0.1 bf | 0.0% | 0.0% | 0.0% | 0.0%
Rext 5.0.1 bf vs SAO no Quant | 0.0% | -0.5% | -0.2% | -2.1%
QP = 17…38 (PSNR 27…61 dB) |  |  |  | 
Rext 5.0.1 vs Rext 5.0.1 bf | 0%…-60% | 0,0% | 0%…-60% | 0,0%
Rext 5.0.1 bf vs SAO noQ | 0,3% | 0,1% | 1,2% | 0,6%
Rext 5.0.1 bf vs SAO Adapt.Q (both PicRdoSAO ) | 0.0% | 0.0% | -0,7% | -0,6%
#if SH_RD_COST_64_FIX
dRdCost = (Double)(Int64)uiDistortion + (Double)((Int64)(uiBits * dLambda+.5)>>16);
#else
dRdCost = ((Double)(Int64)uiDistortion + (Double)((Int)((Int64)uiBits * dLambda+.5)>>16));
#endif

## Slide 14: Conclusion based on additional test results
Based on the test data provided it is proposed
  fix s/w bug which leads to overflow in RDCost calculation
  to remove the quantization step of the SAO magnitude value for higher bitDepth content (AhG18).
  to add the control quantization step of the SAO magnitude value on slice level.
  to continue investigating the quantization process for the Edge Classification method using different quantization values and adaptation mechanisms.

## Slide 15: SAO Quant removal w/o condition
Sample adaptive offset semantics
…
The variable bitDepth is derived as follows:
If cIdx is equal to 0, bitDepth is set equal to BitDepthY.
Otherwise (cIdx is equal to 1 or 2), bitDepth is set equal to BitDepthC.
The list SaoOffsetVal[ cIdx ][ rx ][ ry ][ i ] for i ranging from 0 to 4, inclusive, is derived as follows:
SaoOffsetVal[ cIdx ][ rx ][ ry ][ 0 ] = 0 for( i = 0; i < 4; i++ ) SaoOffsetVal[ cIdx ][ rx ][ ry ][ i + 1 ] = (7‑64) offsetSign * sao_offset_abs[ cIdx ][ rx ][ ry ][ i ] << ( bitDepth − Min( bitDepth, 10 ) )

## Slide 16: SPS control
if( sps_extension_flag[ 0 ] ) { | 
… | 
if (sample_adaptive_offset_enabled_flag) | 
sao_quant _enabled_flag | u(1)
} | 
Sample adaptive offset semantics
…
The variable saoOffsetBitShift is derived as follows
if (sao_quant _enabled_flag)
saoOffsetBitShift = ( bitDepth − Min( bitDepth, 10 ) )
else
saoOffsetBitShift = 0.
The list SaoOffsetVal[ cIdx ][ rx ][ ry ][ i ] for i ranging from 0 to 4, inclusive, is derived as follows:
SaoOffsetVal[ cIdx ][ rx ][ ry ][ 0 ] = 0 for( i = 0; i < 4; i++ ) SaoOffsetVal[ cIdx ][ rx ][ ry ][ i + 1 ] = (7‑64) offsetSign * sao_offset_abs[ cIdx ][ rx ][ ry ][ i ] << saoOffsetBitShift ( bitDepth − Min( bitDepth, 10 ) )

## Slide 17: Slice level control for SAO quant bits
if( sps_extension_flag[ 0 ] ) { | 
… | 
if (sample_adaptive_offset_enabled_flag) | 
adaptive_sao_bit_shift_active_flag | u(1)
} | 
slice_segment_header( ) { | Descriptor
……. | 
if( sample_adaptive_offset_enabled_flag ) { | 
slice_sao_luma_flag | u(1)
if( ChromaArrayType > 0 ) | 
slice_sao_chroma_flag | u(1)
} | 
if( slice_sao_luma_flag && adaptive_sao_bit_shift_active_flag ) | 
sao_luma_bit_shift | ue(v)
if( slice_sao_chroma_flag && adaptive_sao_bit_shift_active_flag ) | 
sao_chroma_bit_shift | ue(v)
……. | 
} | 
Sample adaptive offset semantics
…
The variable saoOffsetBitShift is derived as follows:
If cIdx is equal to 0, saoOffsetBitShift is set equal to sao_luma_bit_shift.
Otherwise (cIdx is equal to 1 or 2), saoOffsetBitShift is set equal to sao_chmora_bit_shift
The list SaoOffsetVal[ cIdx ][ rx ][ ry ][ i ] for i ranging from 0 to 4, inclusive, is derived as follows:
SaoOffsetVal[ cIdx ][ rx ][ ry ][ 0 ] = 0 for( i = 0; i < 4; i++ ) SaoOffsetVal[ cIdx ][ rx ][ ry ][ i + 1 ] = (7‑64) offsetSign * sao_offset_abs[ cIdx ][ rx ][ ry ][ i ] << saoOffsetBitShift ( bitDepth − Min( bitDepth, 10 ) )