## Slide 1: JCTVC-P0237 Non-RCE3 Major Color Padding Algorithm for Intra Block Copy
Chao-Hsiung Hung, Erh-Chung Ke, Hsin-Ta Chiao (ITRI)
Wen-Hsiao Peng, Hsueh-Ming Hang (NCTU)

## Slide 2: Contents
Introduction
  Intra Block Copy
  Overlapping of Intra Block Copy
Proposed Algorithms
Experimental Results
Conclusion

## Slide 3: Intra Block Copy
left LCU
(LCU, largest coding unit)
current LCU
current CU
reference CU
JCT VC N0256
Reference CU and current CU are located on the same frame
Yellow region is available reconstructed pixels
block vector

## Slide 4: Overlapping of Intra Block Copy
left LCU
(LCU, largest coding unit)
current LCU
current CU
overlapping region
Reference block and current block overlap together
Reference block must contain just reconstructed pixels
reference CU

## Slide 5: Contents
Introduction
Proposed Algorithms
Experimental Results
Conclusion

## Slide 6: Proposed Algorithm (1)
Considering the reconstructed pixels in the left 1 column, top 1 row, left-up 1×1 square around current CU
Calculating histograms of these reconstructed pixels
current CU
considered
reconstructed
pixels

## Slide 7: Proposed Algorithm (2)
Total number of considered reconstructed pixels is N.
Classifying them into M color indexes, P1 , P2 , …, PM . Index order is P1 < P2 < … < PM .
Each color index Pi has its corresponding accumulated histogram frequency Hi , 1 ≤ i ≤ M.
The sum of these Hi is N.
Hmax = max(H1 , H2 , …, HM) and the corresponding color index is Pmax .
The center color index of the histogram is PC .
color index
P1
P2
P3
P4
PM-1
PM
H1
H2
H3
H4
HM-1
HM
……
……

## Slide 8
If M ≤ 4 or Hmax ≥ N/4, we choose Pmax as padding pixel.
Otherwise, we choose PC instead.
Padding the overlapping region between this current CU and reference CU by selected padding pixel above.
Proposed Algorithm (3)

## Slide 9: Contents
Introduction
Proposed Algorithms
Experimental Results
Conclusion

## Slide 10: Experimental Results
HM-12.1+Rext-5.1
RCE3 test conditions

## Slide 11: Experimental Results, Lossless
 | AI |  |  |  | RA |  |  |  | LB |  |  | 
 | Total | Avg | Min | Max | Total | Avg | Min | Max | Total | Avg | Min | Max
Class F | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | -0.2% | -0.3% | -0.7% | 0.0% | 0.0% | -0.1% | -0.7% | 1.0% | 0.0% | -0.2% | -0.6% | 0.0%
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | -0.2% | -0.3% | -0.8% | -0.1% | -0.1% | -0.3% | -0.8% | 0.0% | -0.1% | -0.2% | -0.6% | 0.0%
YCbCr 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | -0.7% | -0.7% | -1.4% | -0.2% | -0.2% | -0.7% | -1.5% | -0.2% | -0.2% | -0.7% | -1.2% | -0.1%
YCbCr 4:4:4 SC (Optional) | -1.2% | -1.2% | -1.5% | -0.6% | -0.7% | -1.2% | -1.8% | -0.5% | -0.5% | -1.2% | -2.0% | -0.4%
Enc Time[%] | 111% |  |  |  | 102% |  |  |  | 102% |  |  | 
Dec Time[%] | 102% |  |  |  | 101% |  |  |  | 100% |  |  | 

## Slide 12: Experimental Results, Lossy
 | All Intra Main-tier |  |  | All Intra High-tier |  |  | All Intra Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.6% | -0.6% | -0.7% | -0.5% | -0.5% | -0.5% | -0.3% | -0.3% | -0.4%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | -0.9% | -0.8% | -1.0% | -0.8% | -0.8% | -0.9% | -0.8% | -0.8% | -0.8%
RGB 4:4:4 Animation | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1%
YCbCr 4:4:4 SC | -0.8% | -1.0% | -0.9% | -0.7% | -0.9% | -0.8% | -0.7% | -0.7% | -0.7%
YCbCr 4:4:4 Animation | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | -3.0% | -3.0% | -3.1% | -3.3% | -3.5% | -3.9% | -3.5% | -3.5% | -3.8%
YCbCr 4:4:4 SC (Optional) | -1.7% | -1.4% | -1.6% | -1.8% | -1.5% | -1.7% | -1.8% | -1.6% | -1.7%
Enc Time[%] | 106% |  |  | 106% |  |  | 105% |  | 
Dec Time[%] | 102% |  |  | 102% |  |  | 102% |  | 
 | Random Access Main-tier |  |  | Random Access High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -0.5% | -0.6% | -0.4% | -0.4% | -0.5% | -0.5%
Class B | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% | -0.1%
RGB 4:4:4 SC | -0.6% | -0.6% | -0.7% | -0.6% | -0.6% | -0.7%
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | -0.6% | -0.6% | -0.7% | -0.6% | -0.7% | -0.7%
YCbCr 4:4:4 Animation | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | 0.0%
RangeExt | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1%
RGB 4:4:4 SC (Optional) | -2.2% | -2.3% | -2.3% | -2.6% | -2.8% | -3.0%
YCbCr 4:4:4 SC (Optional) | -1.5% | -1.5% | -1.6% | -1.6% | -1.5% | -1.8%
Enc Time[%] | 99% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 101% |  | 
 | Low delay B Main-tier |  |  | Low delay B High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -0.4% | -0.7% | -0.5% | -0.3% | -0.4% | -0.3%
Class B | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | 0.0%
RGB 4:4:4 SC | -0.6% | -0.6% | -0.7% | -0.5% | -0.5% | -0.5%
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | -0.6% | -0.5% | -0.5% | -0.4% | -0.4% | -0.4%
YCbCr 4:4:4 Animation | 0.0% | 0.1% | 0.1% | 0.0% | 0.1% | 0.0%
RangeExt | 0.0% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | -2.2% | -2.2% | -2.1% | -1.3% | -1.2% | -1.1%
YCbCr 4:4:4 SC (Optional) | -1.1% | -1.2% | -1.2% | -1.0% | -1.1% | -1.1%
Enc Time[%] | 100% |  |  | 101% |  | 
Dec Time[%] | 101% |  |  | 101% |  | 

## Slide 13: Contents
Introduction
Proposed Algorithms
Experimental Results
Conclusion

## Slide 14: Conclusion
A major color padding algorithm for intra block copy is proposed.
Saving about 0.6%~3% on BD rate for many test sequences.

## Slide 15: Acknowledgement
We thank MediaTek for crosscheck on our proposal

## Slide 16: Thank you for your attention!