## Slide 1: Adaptive MV precision for Screen Content Coding (JCTVC-P0283)
X. Li, J. Sole, and M. Karczewicz (Qualcomm Inc.)

## Slide 2: Proposed Method
Sub-pixel MC is not efficient for screen content
Proposed method
  Signal a flag at CU level to indicate whether integer-precision MV is used for the CU
  If the flag is true
    Round MV predictors to integer precision
    Signal MV difference in integer precision
  Else
    Current process is used

## Slide 3: Simulation Results (Lossy)

## Slide 4: Conclusions
It is proposed to signal a flag at CU level to indicate whether integer MV precision is used for the CU
Simulations show interesting coding gain
  1%-4% luma BD rate reduction for screen content
  1%-2% luma BD rate reduction for animation
  Noticeable gain for camera content
It is proposed to further study the proposed method in a CE