## Slide 1: Description of screen content coding technology proposal by Microsoft (JCTVC-Q0035)
Bin Li, Jizheng Xu, Feng Wu, Xun Guo and Gary. J. Sullivan
Microsoft Corp.

## Slide 2: Design goals
High coding efficiency
  About 30% bit-saving with fixQP coding
Low extra complexity
  All 8-bit design for the current test
  Always faster than the anchor encoder (RA and LB, lossy and lossless)
  An example of 3x faster (RA and LB, lossy and lossless)
Simple extension
  RExt-5.1 based, can be easily moved to Rext-6.0
  Each tool can be turned on/off by macros

## Slide 3: Technologies
Intra BC improvements
1-D dictionary mode
Palette mode
Adaptive color space coding
2-D dictionary search (encoder only)

## Slide 4: Intra BC improvements
Intra BC skip mode
  Intra BC 2Nx2N without residue
Intra BC merge mode
  Merged with above or left block
Intra BC with flipping
  Only vertical flipping is used
No range constrain on BV
  Search within the whole picture using 2-D dictionary
  Causal constrain still applies
  No PU/TU overlapping

## Slide 5: 1-D dictionary mode
String match
  Convert 2-D block into 1-D signal
  (offset, length) to indicate string copy
Reconstruction based 1-D dictionary
  Copy from reconstructed area according to current block’s structure
  (2D-offset, length) to indicate string copy
Applied to both
  Direct mode to code a single pixel
  Horizontal and vertical scanning
  De-blocking disabled

## Slide 6: Palette mode
Based on JCTVC-P0108
+ Color table sharing (JCTVC-P0153)
+ Four-neighbor major color index prediction (JCTVC-P0098)
+ Transition copy mode (JCTVC-P0115)

## Slide 7: Adaptive color space coding
GBR/YCoCg/RGB/BGR adaptation
  Applied to intra CU
  GBR/RGB/BGR adaptation for lossless coding
GBRYCoCg
  No bit-depth increase
  A bug fix presented in JCTVC-Q0213
Applied to RGB sequences only

## Slide 8: 2-D dictionary search
Hash-based block matching
  Encoder-only
  Exact match based on original signals
  Inverted index for every possible position
Intra BC with 2-D dictionary search
  4x4/8x8/16x16 PU
  Intra BC without residue sent
  Handle flipping as well
Inter mode with 2-D dictionary search
  8x8/16x16/32x32/64x64 PU

## Slide 9: Other encoding algorithms
Early terminate if 2-D dictionary hits
  Skip checking other color spaces
  Skip non-2Nx2N lossy intra BC search
  Skip fractional motion estimation
  Skip all the following RDO process if inter 2D match (with a no greater QP) is found for 64x64
Motion estimation start-point refinement
  Non-2Nx2N PU can use the MV found for 2Nx2N PU with same reference picture as ME start point

## Slide 10: Other changes relative to RExt-5.1
Aligned to Rext-6.0
  2NxN/Nx2N/NxN intra BC added
  r3815 - RExt__P0154_ADDITIONAL_CONTEXT_FOR_CCP
  r3841 - Fixed single-component-loop inter search for lossless coding
  r3816 - RExt__PRCE2_A1_GOLOMB_RICE_PARAMETER_ADAPTATION
Marginal encoding changes
  CABAC state fix
  CABAC fractional bit fix
  Disable SAO at slice level if all CTUs do not use SAO
  Fix uninitialized variables

## Slide 11: Objective performance
PSNR difference
  Weird BD-rate indication
  Some points are lossless coded even with lower bit rate than the anchor
  PSNR difference to the anchor can be used since bit rate has been matched
PSNR clipping
  Visual differences observed even around 63dB
  Suggest to use 114.31dB, instead of 58.92dB
See JCT-Q0053 for more details.

## Slide 12: Simulation
QP adjustment according to lambda on (lossy)
Exactly the same reference structure as the anchor
Matched bit rate coding
  Input QP increased by 1 in encoding order once per sequence if necessary
  Lower bit rate guaranteed (much lower sometimes)
Fixed QP coding
  Same input QPs as the anchor

## Slide 13: PSNR diff. (clipped w/ 58.92dB) Matched bit rate

## Slide 14: Lossless coding results

## Slide 15: Improvement with bug fix (JCTVC-Q0213) Fixed QP

## Slide 16: Faster encoders (JCTVC-Q0052)
Fixed QP coding

## Slide 17: Faster encoders (JCTVC-Q0052)
Lossless coding

## Slide 18: Software
Based on HM-12.1+RExt-5.1
  HM-13.0+Rext-6.0 based version is also available
Compiled with Visual Studio 2013
  Can also be compiled with Visual Studio 2010 or GCC 4.6.3
Separate macros to turn on/off tools

## Slide 19: Summary
HEVC-based simple extension
  High efficiency
  Low extra complexity
Text available
Easy to test individual tool
Bug-fixed version available
  JCTVC-Q0213
Faster encoders available
  JCTVC-Q0052

## Slide 20
Thanks.