## Slide 1
: Comments on IRAP picture alignment and POC value derivation (JCTVC-Q0057/JCT3V-H0039)
Yongjin Cho
Samsung Electronics Co., Ltd.
March. 2014
Notes: <number>

## Slide 2: Proposals on IRAP alignment and POC value
Proposal 1:
  A flag layerwise_start_up_disable_flag disabling a layer-wise start-up is proposed.
Proposal 2:
  When all_layers_idr_aligned_flag is equal to 1, vps_poc_lsb_aligned_flag shall be equal to 1 and poc_reset_info_present_flag shall be equal to 0.
Proposal 3:
  Replacing the restriction that “the value of poc_reset_idc of all pictures in an access unit shall be the same” with “the value of poc_reset_idc of all slices in a layer shall be the same” is proposed.
Proposal 4:
  In MV-HEVC profile (stereo main profile), cross_layer_pic_type_aligned_flag and cross_layer_irap_aligned_flag are equal to 1 by default.
<number>

## Slide 3: Proposal 1: layerwise_startup_disable_flag
Proposal : To notify a layerwise start-up is disabled in some bitstreams, a flag layerwise_startup_disable_flag in VPS extension is proposed.
Reason: When a layer-wise start up is not useful in some bitstreams, e.g. stereo video streams, the proposed flag will be helpful for simplifying the the POC value derivation. Moreover, this is helpful for session negotiation because some simple systems may not be compatible with a layerwise start-up.
<number>
layerwise_startup_disable_flag equal to 1 indicates a layerwise start-up is disallowed in the current bitstream. When layerwise_startup_disable_flag is equal to 1, cross_layer_irap_aligned_flag, and vps_poc_lsb_aligned_flag shall be equal to 1, and poc_reset_info_present_flag shall be equal to 0. layer_wise_startup_disable_flag equal to 0 specifies that the above restriction may or may not apply. When layerwise_startup_disable_flag is equal to 1, the variables LayerInitializedFlag[ i ] and FirstPicInLayerDecodedFlag[ i ] shall have the same value for all values of i from 0 to vps_max_layer_id.

## Slide 4: Proposal 2 : all_layers_idr_aligned_flag
Proposal: direct_dep_type_len_minus2 is fixed-length coded with u(3) in VPS extension. The fixed-length coding is easy accessible.
Purpose: The proposed restriction will be helpful for checking errors in conformance bitstreams, and simplifying the POC value derivation in decoders.
<number>

## Slide 5: Proposal 3 : poc_reset_idc
Proposal: It is proposed to replace the restriction that “the value of poc_reset_idc of all pictures in an access unit shall be the same” with “the value of poc_reset_idc of all slices having the same value of nal_unit_type in an access unit shall be the same”.
Purpose: This relaxation can avoid unnecessary POC value reset of decoded pictures in DPB.
When a POC value of a layer is equal to a POC value of a base layer without POC reset, the redundant POC reset process can be skipped even if the POC values of other layers are reset.
<number>

## Slide 6: Proposal 4 : Restrictions for MV-HEVC
Proposal: In MV-HEVC profile (stereo main profile), cross_layer_pic_type_aligned_flag and cross_layer_irap_aligned_flag are equal to 1 by default.
<number>

## Slide 7
Thank you !
<number>