## Slide 1: MV-HEVC/SHVC HLS: On inter-layer RPS signalling and derivation
JCTVC-Q0060 / JCT3V-H0024
Hahyun Lee

## Slide 2: Summary
The following aspects are asserted
  Proposal 1
    In the slice segment header, Inter-layer RPS signalling should take into account the number of direct reference layer presented in the same access unit as the current picture in order to remove the redundant signal bits
    It is derived by considering two syntax elements
      ‘max_tid_il_ref_pics_plus1’ and ‘sub_layers_vps_max_minus1’.
  Proposal 2
    When ‘max_tid_il_ref_pics_plus1[i][j]’ is equal to 0 (i.e., when only the IRAP pictures of the reference layer may be used as reference for inter-layer prediction for lightweight option), the IRAP pictures is not included in the reference pictures for inter-layer prediction, even though it should be included in the reference pictures for inter-layer prediction.
    It should be fixed.

## Slide 3: Proposal 1
Inter-layer RPS signalling
  In the slice segment header, the number of direct reference layer is only considered for inter-layer RPS signalling.

## Slide 4: Proposal 1
Shortcomings (Example)
The syntax ‘inter_layer_pred_layer_idc[0] = 2’ is signalled.
Assuming ‘all_ref_layers_active_flag == 0’,
‘max_one_active_ref_layer_flag == 1’,
‘inter_layer_pred_enabled_flag == 1’
The syntax element ‘inter_layer_pred_layer_idc[i]’ can skipped, when (NumActiveRefLayerPics == numRefLayerPics)
In this case, there is only one picture that is used in decoding of the current picture for inter-layer prediction ( numRefLayerPics == 1)
(NumActiveRefLayerPics == 1) != (NumDirectRefLayers[3] == 3),

## Slide 5: Proposal 1
Changes
  The number of direct reference layer presented in the same access unit as the current picture, indicated by the variable ‘numRefLayerPics’, should be considered for inter-layer RPS signalling

## Slide 6: Proposal 2
MV-HEVC WD7 and SHVC WD5
  When ‘max_tid_il_ref_pics_plus1[i][j]’ is equal to 0 (i.e., when only the IRAP pictures of the reference layer may be used as reference for inter-layer prediction for lightweight option), the IRAP pictures is not included in the reference pictures for inter-layer prediction, even though it should be included in the reference pictures for inter-layer prediction.
Changes

## Slide 7: Comments on JCTVC-Q0079(JCT3V-H0027)
The following modifications are necessary
  The variables NumDirectRefLayersForTid[lId][tId] and RefLayerIdListForTid[lId][tId][k] are derived as follows by taking into account either vps_max_sub_layers_minus1 or sub_layers_vps_max_minus1[]

## Slide 8: Comments on JCTVC-Q0079(JCT3V-H0027)
The following modifications are necessary
  The variables NumActiveRefLayerPics is derived as follows
  When ‘inter_layer_pred_layer_idc[i]’ is not present, the value is inferred to be equal to i