## Slide 1: On the displacement vector prediction scheme for Intra Block Copy JCTVC-Q0062
C. Gisquet, G. Laroche, P. Onno
17th JCT-VC Meeting, Valencia, March/April 2014

## Slide 2: Context
Intra Block Copy prediction principle
  The block displacement prediction is performed by using, as predictor, the displacement motion of the last CU coded with IBC.
  The predictor is initialized by (-N,0) at CTB level.
In RExt 6.0, the new NxN, 2NxN and Nx2N partition has been adopted, the prediction can be still improved to better math this new partition.

## Slide 3: Proposal
Use the last displacement vectors of the 3 last CUs encoded with IBC.
  Build a list containing these 3 displacement vectors
  Initialized as follows
    mvp2= (-3.N,0), mvp1= (-2.N,0), mvp0=(-.N,0).
Indicate though a syntax element the predictor index from the list
  Truncated binary code.
Memory consideration
  Need just to store 3 displacement vectors instead of 1 in the current design of Range Extension.

## Slide 4: Results
Lossy:
  Rext 6.0 anchors
Summary
  AI:-0.4%
  RA:-0.3%
  LD:-0.2%
  Same runtime

## Slide 5: Results
Lossless:
  RExt 6.0 anchors
Summary
  AI:-0.4%
  RA:-0.3%
  LD:-0.2%

## Slide 6: Conclusion
This proposal introduces a simple modification of the IBC prediction scheme.
  To better take into account the newly adopted partition of IBC (2NxN, Nx2N and NxN).
Results
  Lossy:
    AI:-0.4%
    RA:-0.3%
    LD:-0.2%
    No change in the encoder/decoder runtime
Consider this simple modification and improvement of IBC in the final specifications of Range Extension.