## Slide 1: AhG10: Palette index coding JCTVC-Q0064
C. Gisquet, G. Laroche, P. Onno
17th JCT-VC Meeting, Valencia, March/April 2014

## Slide 2: Current index coding and problem identified in AhG10 software
Palette index is coded using FLC
  For a given palette size P, uses N = log2(P) bits
  Coding e.g. P=17 elements on 5bits or P=3 on 2bits is inefficient
Using Huffman seems a complex task:
  Ideally, the prediction methods should try to decorrelate indexes and make them equiprobable
  There are many cases where it would need to be adaptive, causing excessive complexity at the decoder
Proposal 1: truncated binary coding:
  Let N=log2(P) be the FLC length, so that P = 2N + R
  To code an index idx:
    if idx<R, code idx on N-1 bits
    Otherwise, code idx+R on N bits

## Slide 3: Concept of impossible values
Proposal 2: Take into account impossible values when coding index value
The index value can’t be the one that would have been generated by the previous prediction
  Otherwise the encoder would have increased the runlength
  Pixel "¿" can’t be red: the 3 previous use copy up, so red would have been selected by copy up
  Pixel "?" can’t be blue: the 2 previous use copy left, so blue would have been selected by copy left
A good compromise in terms of complexity

## Slide 4: Signaling escape values
AhG10 uses JCTVC-P0108 signaling
  An index is reserved to signal explicit pixel values
  Known to cause a loss compared to an CABAC-coded escape flag, but seen as a complexity reduction
Proposal 3: escape values can only be signaled if palette has maximal size
  i.e., if transmitted size is 31, assume escaping through index value 31
  Otherwise, no need to make room for it
  Is actually already the behavior of current AhG10 software from JCTVC-P0303

## Slide 5: Results
Lossy
  Anchors:RExt6.0 + P0303
  -1.7% BDR gain for AI

## Slide 6: Results
Lossless

## Slide 7: Conclusion
Multiple elements lead to improved index coding
  Present in JCTVC-Q0037 (InterDigital) / JCTVC-Q0047 (Qualcomm)
The combination is an intermediate complexity increment between FLCs and Huffman-like VLCs
Recommend further study with Palette-related CEs in the scope of Screen Content Coding study.