## Slide 1: AhG10: Combination of Palette coding tools JCTVC-Q0069
C. Gisquet, G. Laroche, P. Onno
17th JCT-VC Meeting, Valencia, March/April 2014

## Slide 2: Tools from other contributions
Palette index coding (JCTVC-Q0064)
  Uses truncated binary codes and knowledge of impossible values
  Present in JCTVC-Q0037 (InterDigital) / JCTVC-Q0047 (Qualcomm)
Transition copy mode (JCTVC-Q0065)
  Knowledge of frequent 2-color patterns are used for prediction
  First presented in JCTVC-P0115
  Similar tool in JCTVC-P0249, JCTVC-Q0033 and JCTVC-Q0037
Run coding for palette mode (JCTVC-Q0066)
  Signal indexes for which no run is coded
  First presented in JCTVC-P0113, similar tool in JCTVC-Q0071
Palette predictor stuffing (JCTVC-Q0063)
  Add unused predictor elements to current palette to build predictor
  Improvement of JCTVC-P0114 / JCTVC-P0303

## Slide 3: Other additions
Bugfixes:
  Invalid evaluation of « copy left » prediction when run is 1
  Invalid evaluation of coding cost
    Palette flag set to 0 coded twice for some mode
    Palette syntax coded twice in inter slices
New palette decision algorithm
  Improvement of JCTVC-P0119 (taking centroid)
  2 iterations instead of 1
  Miscellaneous bugfixes to algorithm
  Essentially, a Kmeans++ algorithm

## Slide 4: Results: vs Rext 6.0
Anchor: RExt 6.0 + P0303 (AhG10 software)
Lossy
Lossless

## Slide 5: Results: vs SCC CfP anchor
Max PSNR=54.462 for lossy, i.e. as if clipped

## Slide 6: Conclusion
Large margin of improvement for the palette mode
Difficult to evaluate palette tools independently of other tools (palette or not)
Recommend continued study of the different elements, in particular in reference to SCC CfP