## Slide 1: AHG18: Worst-Case Escape Code Length Mitigation
JCTVC-Q0073
Broadcast & Professional Research Labs
Sony Europe Ltd.
Karl Sharman
Sony Corp.

## Slide 2: Background
In HEVC, escape codes are used to signal any part of a coefficient’s magnitude that is not described by a CABAC syntax element.
  The escape code syntax element is named “coeff_abs_level_remaining”.
coeff_abs_level_remaining is bypass-coded using a mixed Golomb‑Rice and exponential‑Golomb‑order‑k binarisation.
When using extended‑precision processing to code 16-bit video, the worst-case escape code length is 46:
  The largest possible coefficient magnitude is 222 = 4194304.
    Hence, the largest possible escape code is 4194303 (after deducting 1 for the significance map).
    If the Rice parameter rParam is 0, a further 3 is deducted and the value 4194300 is coded using exponential‑Golomb coding.
    The final code will require 21 prefix bits, 21 suffix bits, 1 separator bit and 3 extra prefix bits to signify that Golomb-Rice coding is not in use. 21 + 21 + 1 + 3 = 46.
  In HEVC version 1, the worst-case escape code length is 32 (see JCTVC-J0142).

## Slide 3: Proposed Scheme
In exponential‑Golomb coding, the suffix length is equal to the prefix length. It is proposed that, instead, when extended‑precision processing is in use:
  Prefix length is limited to a maximum length given by:
    maximumPrefixLength = 32 – (3 + MAX_TR_DYNAMIC_RANGE)
  When a prefix of this length is encountered, the length of the corresponding suffix is given by:
    suffixLength = MAX_TR_DYNAMIC_RANGE – rParam
  Since the prefix has a maximum length, it can be coded using truncated-unary coding.
Using this scheme, the worst-case escape code length would be:
    (32 – (3 + MAX_TR_DYNAMIC_RANGE)) (prefix)
    + (MAX_TR_DYNAMIC_RANGE – rParam) (suffix)
    + rParam (fixed bits)
    + 3 (not-a-Golomb-Rice-code bits)
    = 32
  The worst case has thus been reduced by 14 bits.
  This is the same worst case as in HEVC version 1, which may have to be supported by a Range Extensions codec.

## Slide 4: Results
The proposed scheme was tested under AHG18 lossy and lossless common test conditions.
  Since the proposed scheme is only in use when extended-precision processing is enabled, no change in BD-rate can occur for other test conditions.
  The results for AHG18-lossless are shown to the right, and for AHG18‑lossy are shown below:

## Slide 5: Conclusion
A modification to the current HEVC escape coding scheme for use with extended‑precision processing has been presented.
  Through use of this scheme, the worst-case escape code length can be reduced from 46 to 32, bringing it in line with that of HEVC version 1.
    Therefore, an entropy decoder in a Range Extensions codec designed to operate at a specified number of pixels per second can be designed for a 30% smaller worst case escape code.
The proposed scheme has been shown not to have significant impact on coding efficiency or run-time.
  BD-rate changes of 0.0% are observed for AHG18 test conditions.
  Coefficients that require the worst-case escape codes are very rare (hence they are assigned the largest codes – larger than the coefficients themselves), though a decoder must nonetheless be designed to accommodate them.