## Slide 1: AHG5: Intra-block-copy in Non-4:4:4 Formats
JCTVC-Q0075
Broadcast & Professional Research Labs
Sony Europe Ltd.
Karl Sharman
Sony Corp.

## Slide 2: Background
At the 16th JCTVC meeting, Intra-Block Copy (IBC) was extended to include NxN, 2NxN and Nx2N splitting.
Special rules were generated to handle 4:2:0 and 4:2:2 chroma processing
  The chroma PUs were merged to cover an area of at least 4x4 samples.
  The IBC displacement vector that they used was taken from the bottom-right luma PU of the corresponding luma area.
  Chroma was still processed using sub-PUs down to 2x2 samples in size.
  If the chosen motion vector is out-of-bounds for any of the chroma sub-PUs, it is clipped when processing that sub-PU.
    This requires the motion vector’s legality to be verified at the decoder side (and encoder side).
    The chroma PU is therefore not completely merged.
      The source regions may overlap due to the clipping on each sub-PU.

## Slide 3: Background (continued)
Example NxN split with IBC displacement.
The yellow chroma-sub-PU is correctly displaced.
The red, blue and green chroma-sub-PUs are not fully displaced due to clipping to the valid IBC search area.
Units in pixels

## Slide 4: Background (continued)
The yellow chroma-sub-PU is correctly displaced.
The red, blue and green chroma-sub-PUs are not fully displaced due to clipping to the valid IBC search area.
Without clipping
With clipping
Units in pixels

## Slide 5: Background (continued)
The Range Extensions encoder, as currently defined does not take into account problems regarding constrained intra prediction.
  It does not consider the extended region for which a luma vector is used.

## Slide 6: Proposed Scheme
It is proposed that the motion vector for luma be constrained:
  The luma-based motion vector of the bottom-right PU of a merged chroma set must be valid for every chroma PU in that set.
This simplifies the decoder by removing the checking in the decoder (although the encoder still must check)
It removes the unusual overlapping behaviour
It fully joins the chroma PUs into a block so that at least blocks of 4x4 samples are all subjected to the same displacement.

## Slide 7: Results – AHG5

## Slide 8: Results – AHG8 Lossless

## Slide 9: Results – AHG8 Lossy
  SlideShow and SlideEditing prefer the original overlapping algorithm.
    These sequences occasionally wanted to use the slightly longer motion vector for luma and due to the 480:1 compression ratio, a slight increase in data produces a large BD-rate change.

## Slide 10: Conclusion
A modification to the rules regarding merged chroma PUs for 4:2:0 and 4:2:2 processing of intra-block-copy is proposed.
The modification fully merges the chroma PUs so that the smallest PU is at least effectively 4x4 for chroma.
  The modification simplifies the decoder design by placing a restriction on the bit-stream.