## Slide 1: EXR & TIFF to .YUV
JCTVC -Q0085
MPEG m32804

## Slide 2: Terms
IDT: Input Device Transform
ICES: Input Color Encoding Specification
ACES: Academy Color Encoding Spec.
RRT: Reference Rendering Transform
ODT: Output Display Transform
OCES: Output Color Encoding Spec.
AMPAS: Academy Science & Technology Council
CTL: Control Transform Language

## Slide 3: ...similar to Giorgianni, Madden (2008) description (page 314)

## Slide 4: Stages

## Slide 5: Workflow
ICES to ACES
Apply RRT
(AMPAS ctlrender)
RRT  PQ ODT
(ctlrender)
.EXR (linear EOTF 16-bit half-float ACES RGB with RRT rolloff)
.EXR (16-bit half-float linear RGB )
HEVC encoder
PQ ODT  YDzDx
4:4:4  4:2:0
.yuv
.TIFF (PQ 16-bit float )
S-gamut to ACES primaries (RGB)( S-gamut_to_ACES.ctl )
Apply RRT rolloff (rrt.ctl)
Target 10k nits, D65 (e.g. HDR display)
(odt_PQ10k-D65.ctl )
.bin
HDR chroma subsampling
16-bit to 12-bit right shift

## Slide 6: ICES  ACES
Convert RGB S-Gamut (ICES) to ACES primaries
Applies very wide dynamic range tone curve to some roll-off. (small changes).
This example pre-converts the FruitStall S-log into ACES before applying RRT.
  ctlrender -verbose -force –ctl S-gamut_to_ACES.ctl –ctl transforms/ctl/forward/rrt/rrt.ctl input.tiff –format tiff16 rrt_output.tif

## Slide 7: RRT (TIFF) to PQ ODT (XYZ)
Convert RRT to PQ ODT (4:4:4 XYZ master for compression)
  ctlrender -ctl odt_PQ10k-D65.ctl rrt_output.tif -format tiff16 odt_output.tif

## Slide 8: 4:4:4 PQ XYZ to 4:2:0 YDzDx
Tiff2ydzdx:
  Chroma subsampling: 4:4:4 to 4:2:0
  TIFF  “.yuv” (concatenated)

## Slide 9: Other steps in Q0085
Where to find tools and how to install them
Example use cases
Conversion of decoded output to .TIFF
Conversion to JPG, PNG, etc. for viewing on a 100+ nit display.