## Slide 1: Redundant picture SEI message
Sychev Maxim

## Slide 2: Abstract
This contribution presents the support for redundant pictures in HEVC/SHVC/MV-HEVC due SEI messages for protection of video from loss in bad channels or unmanaged networks.
The proposed solution describes the syntax and semantics of how to support redundant pictures in HEVC.
This contribution propose two SEI messages to point the position of redundant and primary picture in the CVS.

## Slide 3: Introduction
The current specification of SHVC/MV-HEVC and HEVC does not allow having redundant pictures in bitstream. This proposal describes redundant pictures for SHVC/MV-HEVC/HEVC and several applications and examples of how they can be used. Usage of redundant pictures makes no sense for non-reference pictures.
Proposed solutions allow to separate the primary coded picture and the redundant coded pictures, which can increase the error resilience of bitstream in case of burst (grouped) packet loss.

## Slide 4: Description
primary coded picture: The coded representation of a picture to be used by the decoding process for a bitstream conforming to this Recommendation | International Standard. The primary coded picture contains all coding tree units of the picture. The only pictures that have a normative effect on the decoding process are primary coded pictures. See also redundant coded picture.
redundant coded picture: A coded representation of a picture or a part of a picture. The content of a redundant coded picture shall not be used by the decoding process for a bitstream conforming to this Recommendation | International Standard. A redundant coded picture is not required to contain all coding tree units in the primary coded picture. Redundant coded pictures have no normative effect on the decoding process. See also primary coded picture.

## Slide 5: Redundant picture SEI syntax

## Slide 6: Redundant picture SEI semantics
rpi_pic_order_cnt_delta_sign_flag equal to 0 specifies that the picture order count delta indicated by rpi_pic_order_cnt_delta_minus1 is positive. rpi_pic_order_cnt_delta_sign_flag equal to 1 specifies that the picture order count delta indicated by rpi_pic_order_cnt_delta_minus1 is negative.
rpi_pic_order_cnt_delta_minus1 plus 1 specifies the absolute difference between the PicOrderCntVal of the associated primary coded picture (as specified below) and the PicOrderCntVal of the current picture.
The associated primary coded picture is the picture that has PicOrderCntVal equal to prmPicOrderCntVal, which is derived as follows, where currPicOrderCntVal is the PicOrderCntVal of the current picture:
prmPicOrderCntDelta = ( 1 – 2 * rpi_pic_order_cnt_delta_sign ) * ( rpi_pic_order_cnt_delta_minus1 + 1 )
prmPicOrderCntVal = currPicOrderCntVal – prmPicOrderCntDelta
The value of rpi_pic_order_cnt_delta_minus1 shall be in the range of 0 to 255, inclusive.
prm_poc_reset_flag equal to 1 indicates that the associated primary coded picture is an IRAP picture with NoRaslOutputFlag equal to 1 and the PicOrderCntVal of the associated primary coded picture is equal to 0. prm_poc_reset_flag equal to 0 indicates that the associated primary coded picture is not an IRAP picture with NoRaslOutputFlag equal to 1 and the PicOrderCntVal of the associated primary coded picture may or may not be equal to 0.
NOTE – The following two approaches may be applied for decoder state recovering after a primary coded picture loss:
 When some delay is allowed, the decoder may wait for the arrival of a redundant coded picture, and then take the redundant coded picture as the primary coded picture.
 For real-time, low-delay applications after decoding redundant picture replace the primary picture with redundant picture.

## Slide 7: Primary picture SEI semantics
The primary picture SEI message indicates that the current picture is a primary coded picture and provides information on the redundant coded pictures associated with the current picture.
num_redundant_pics_minus1 plus 1 specifies the number of redundant coded pictures associated with the current picture that is a primary coded picture. The value of num_redundant_pics_minus1 shall be in the range of 0 to 15, inclusive.
ppi_pic_order_cnt_delta_sign_flag[ i ] equal to 0 specifies that the picture order count delta indicated by ppi_pic_order_cnt_delta_minus1[ i ] is positive. ppi_pic_order_cnt_delta_sign_flag[ i] equal to 1 specifies that the picture order count delta indicated by ppi_pic_order_cnt_delta_minus1[ i ] is negative.
ppi_pic_order_cnt_delta_minus1[ i ] plus 1 specifies the absolute difference between the PicOrderCntVal of the current picture and and the PicOrderCntVal of i-th redundant coded picture associated with the current picture.
The i-th redundant coded picture associated with the current picture is the picture that has PicOrderCntVal equal to rdtPicOrderCntVal, which is derived as follows, where currPicOrderCntVal is the PicOrderCntVal of the current picture:
rdtPocDelta[ i ] = ( 1 – 2 * ppi_pic_order_cnt_delta_sign[ i ] ) * ( ppi_pic_order_cnt_delta_minus1[ i ] + 1 )
rdtPicOrderCntVal[ i ] = currPicOrderCntVal[ i ] + rdtPocDelta[ i ]
The value of ppi_pic_order_cnt_delta_minus1[ i ] shall be in the range of 0 to 255, inclusive.

## Slide 8: Constraints
A redundant picture SEI messages shall not be associated with any picture that satisfy any of the following conditions:
– The picture has PicOutputFlag equal to 1.
– The picture is used as a reference picture by any other picture.
– The picture has sps_temporal_mvp_enabled_flag equal to 1 and uses a primary coded picture as a reference picture.
– The vps_poc_proportional_to_timing_flag in the VPS referred to by the picture or vui_poc_proportional_to_timing_flag in the SPS referred to by the picture is equal to 1.

## Slide 9: Benefits
Increases the error robustness in error prone channels
Auto recovering features in combination with MDC
Provide much more dynamic quality in case of high loss and bursts
Allows to discard the redundant picture from decoding order if the primary picture is successfully decoded
Do not provide the delay for decoder state recovering
Uses an existing apparatus for protecting video from packet loss
Uses an existing memory
Just HLS to provide such functionality
Simple for implementation

## Slide 10: Network impairment ranges for different service level agreements

## Slide 11: Different PLC methods comparison

## Slide 12: MDC + redundant pictures
Two description video coding scheme (pink and blue) protected by redundant pictures (with POC 13,19,25,31)
The size of blocks approximately shows the size of coded pictures

## Slide 13: Regular scheme with short intra period

## Slide 14: Golden frames (pyramidal scheme)

## Slide 15: Multi Description Video Coding (MDC)

## Slide 16: MDC + redundant B-pictures

## Slide 17: MDC + redundant P-pictures

## Slide 18: MDC + P&B redundant pictures

## Slide 19: Protecting IRAP picture from loss

## Slide 20: Reduced size redundant frames
Redundant frames make sense especially for error resilience those of frames which marked as “used for reference”.
Proposed to code only those areas of picture which are used for temporal inter prediction. In that case it is need to mark redundant frame PicOutputFlag equal to 0 and use it only for decoder state recovery.

## Slide 21: Simulation results
640x480
30 fps
1% loss

## Slide 22: Robustness to packet loss (Random packet loss, FEC for PIR packet) - PSNR
Random packet loss: 0-5% Total bitrate:
1mbps External protection: unequal FEC Scalability:
temporal
Svc211 – Golden frames
Svc27, 37, 47 – MDC+Redundant pics

## Slide 23: Robustness to packet loss (Random packet loss, FEC for PIR packet) – Frame rate
Random packet loss: 0-5% Total bitrate:
1mbps External protection: unequal FEC Scalability:
temporal
Svc211 – Golden frames
Svc27, 37, 47 – MDC+Redundant pics

## Slide 24: Robustness to packet loss (Random packet loss, FEC for PIR packet) - Freezing time
Random packet loss: 0-5% Total bitrate:
1mbps External protection: unequal FEC Scalability:
temporal
Svc211 – Golden frames
Svc27, 37, 47 – MDC+Redundant pics

## Slide 25: Robustness to packet loss (Random packet loss, FEC + NACK)
Random packet loss: 0-10% Total bitrate:
1mbps External protection:
unequal FEC +NACK Scalability:
temporal
Svc211 – Golden frames
Svc27, 47 – MDC+Redundant pics

## Slide 26: Robustness to packet loss (Random packet loss, FEC + NACK)
.
Random packet loss: 0-10% Total bitrate:
1mbps External protection:
unequal FEC +NACK Scalability:
temporal
Svc211 – Golden frames
Svc27, 47 – MDC+Redundant pics

## Slide 27: Robustness to packet loss (Random packet loss, FEC + NACK)
Random packet loss: 0-10% Total bitrate:
1mbps External protection:
unequal FEC +NACK Scalability:
temporal
Svc211 – Golden frames
Svc27, 47 – MDC+Redundant pics

## Slide 28: Simulation results
Test conditions:
Packet loss 4%
Resolution is 640x480, 30fps
Proposed technology
(MDC + redundant B pictures + NACK)
Industry competitors approach (Golden frame technologies + NACK)
Traditional approach
(NACK only)
Applicable for H264 (AVC), H264(SVC), H.265(HEVC), H.265(SHVC)
No Algorithmic delay
Can be implemented over standard HW encoder/decoder

## Slide 29: Conclusion
Redundant frames are very useful in different error protection scenarios such as the interactive scenario using the feedback channel to signal lost data and non-interactive scenarios based on forward error correction approach.
The proposed technique allows to separate the protected primary coded picture and the associated redundant picture for better error resilience in case of bursts.
The proposed solution allows to protect the large sized IRAP frames which are more sensitive to transmission errors.
The new redundant pictures are constructed in a manner which allows to add such functionality to HEVC version 1 because the redundant pictures are regular pictures and not marked for output and will be discarded by already implemented decoders and can be used in future versions with small modifications.
We suggest the committee adopts the redundant picture SEI message to the standard.

## Slide 30
Thank You
www.huawei.com