## Slide 1: Fix for the computation of scaling factors used in inter-layer prediction JCTVC-Q0104
Kenneth Andersson, Jonatan Samuelsson
Notes: 2014-03-25
© Ericsson AB 2014
<number>

## Slide 2: Summary
The proposal enhances the current derivation of the relevant region in the reference layer to match the resolution of the enhancement layer.
As an example the proposal can fix a performance drop for 540p->720p scalability by the use of reference scaling offsets with higher accuracy.
One SPS syntax element is added which determines the accuracy of the reference scaling offsets used for scale factor derivation. The accuracy for locating the corners of the resampled base layer picture is kept to a multiple of two luma samples.
No BDR performance change for common conditions.
Thanks to Qualcomm for cross-check (JCTVC-Q0215).
Notes: 2014-03-25
<number>
© Ericsson AB 2014

## Slide 3: Performance vs SHM-5.0 for 540p->720p scalability
 | AI HEVC 4/3x |  | 
 | Y | U | V
Class A |  |  | 
Class B | -12,1% | -13,0% | -13,1%
Overall (Test vs Ref) | -12,1% | -13,0% | -13,1%
Overall (Test vs single layer) | 12,1% | 8,3% | 7,5%
Overall (Ref vs single layer) | 27,7% | 24,5% | 23,7%
EL only (Test vs Ref) | -38,5% | -38,9% | -39,0%
Enc Time[%] | 98,5% |  | 
Dec Time[%] | 93,8% |  | 
 | RA HEVC 4/3x |  | 
 | Y | U | V
Class A |  |  | 
Class B | -9,6% | -9,1% | -9,3%
Overall (Test vs Ref) | -9,6% | -9,1% | -9,3%
Overall (Test vs single layer) | 22,8% | 26,8% | 27,1%
Overall (Ref vs single layer) | 35,8% | 39,7% | 40,4%
EL only (Test vs Ref) | -29,1% | -28,5% | -28,6%
Enc Time[%] | 95,7% |  | 
Dec Time[%] | 94,2% |  | 
 | LD-B HEVC 4/3x |  | 
 | Y | U | V
Class A |  |  | 
Class B | -8,8% | -8,0% | -8,2%
Overall (Test vs Ref) | -8,8% | -8,0% | -8,2%
Overall (Test vs single layer) | 31,1% | 35,2% | 36,4%
Overall (Ref vs single layer) | 43,7% | 46,9% | 48,7%
EL only (Test vs Ref) | -26,4% | -25,5% | -25,6%
Enc Time[%] | 97,3% |  | 
Dec Time[%] | 96,1% |  | 
Notes: 2014-03-25
<number>
© Ericsson AB 2014

## Slide 4: Background
Reference scaling offsets are used to determine the relevant region of the reference layer to match the resolution of the enhancement layer.
Together with the encoded reference and enhancement layer resolutions they determines scale factors both for sample and motion based inter-layer prediction.
Scale factors are used as part of the alignment of the sample positions in the reference and enhancement layer and corresponds to the ratio between reference and enhancement layer with respect to width or height.
Notes: 2014-03-25
<number>
© Ericsson AB 2014

## Slide 5: Problem
When the reference layer resolution is 540p and the enhancement layer resolution is 720p it is not possible to obtain the desired scaling factor in the vertical direction (540/720).
The reason is that the optimal reference scaling offset to achieve the desired scale factor is equal to:
  720-544*(720/540) = -5-1/3 -> 544/(725+1/3) = 540/720
Currently the accuracy of the reference scaling offset is a multiple of 2 luma samples.
This results in a performance drop for 540p->720p scalability.
Notes: 2014-03-25
<number>
© Ericsson AB 2014

## Slide 6: Proposal
Introduce a fractional scaling factor in SPS extension
  Factor equal to 1 performs identical with SHM-5.0.
  Factor larger than 1 enables fractional accuracy of the reference scaling offsets to derive ScaleFactorX, ScaleFactorY, ScaleFactorMVX, ScaleFactorMVY.
  The accuracy of ScaledRefLayerLeftOffset, ScaledRefLayerTopOffset, ScaledRefLayerRightOffset and ScaledRefLayerBottomOffset is kept as a multiple of two luma samples
Notes: 2014-03-25
<number>
© Ericsson AB 2014

## Slide 7: Proposal
Notes: 2014-03-25
<number>
© Ericsson AB 2014

## Slide 8: Results
For common conditions there is no difference in performance.
For 540p to 720p scalability we compare the proposal with SHM-5.0 using following configuration parameters:
  SHM-5.0:
    NumScaledRefLayerOffsets1 : 1 # Number of scaled entry offsets for this layer
    ScaledRefLayerId1 : 0 # Scaled reference layer ID
    ScaledRefLayerBottomOffset1 : -3 # offset for spatial alignment of BL and EL
  JCTVC-Q0104:
    NumScaledRefLayerOffsets1 : 1 # Number of scaled entry offsets for this layer
    ScaledRefLayerId1 : 0 # Scaled reference layer ID
    ScaledRefLayerBottomOffset1 : -8 # offset for spatial alignment of BL and EL
    ScaledRefLayerFracFactor1 : 2 # Fractional scaling factor. A value larger than 0 corresponds to use of fractional reference layer scaling offsets
Notes: 2014-03-25
<number>
© Ericsson AB 2014

## Slide 9: Performance vs SHM-5.0 for 540p->720p scalability
 | AI HEVC 4/3x |  | 
 | Y | U | V
Class A |  |  | 
Class B | -12,1% | -13,0% | -13,1%
Overall (Test vs Ref) | -12,1% | -13,0% | -13,1%
Overall (Test vs single layer) | 12,1% | 8,3% | 7,5%
Overall (Ref vs single layer) | 27,7% | 24,5% | 23,7%
EL only (Test vs Ref) | -38,5% | -38,9% | -39,0%
Enc Time[%] | 98,5% |  | 
Dec Time[%] | 93,8% |  | 
 | RA HEVC 4/3x |  | 
 | Y | U | V
Class A |  |  | 
Class B | -9,6% | -9,1% | -9,3%
Overall (Test vs Ref) | -9,6% | -9,1% | -9,3%
Overall (Test vs single layer) | 22,8% | 26,8% | 27,1%
Overall (Ref vs single layer) | 35,8% | 39,7% | 40,4%
EL only (Test vs Ref) | -29,1% | -28,5% | -28,6%
Enc Time[%] | 95,7% |  | 
Dec Time[%] | 94,2% |  | 
 | LD-B HEVC 4/3x |  | 
 | Y | U | V
Class A |  |  | 
Class B | -8,8% | -8,0% | -8,2%
Overall (Test vs Ref) | -8,8% | -8,0% | -8,2%
Overall (Test vs single layer) | 31,1% | 35,2% | 36,4%
Overall (Ref vs single layer) | 43,7% | 46,9% | 48,7%
EL only (Test vs Ref) | -26,4% | -25,5% | -25,6%
Enc Time[%] | 97,3% |  | 
Dec Time[%] | 96,1% |  | 
Notes: 2014-03-25
<number>
© Ericsson AB 2014

## Slide 10: Conclusion
The proposal enhances the current derivation of the relevant region in the reference layer to match the resolution of the enhancement layer.
The proposal can fix a performance drop for 540p->720p scalability by use of reference scaling offsets with higher accuracy.
We propose that this fix is included in the next version of the HEVC scalable extension draft.
Notes: 2014-03-25
<number>
© Ericsson AB 2014

## Slide 11
Notes: 2014-03-25
<number>
© Ericsson AB 2014