## Slide 1
JCTVC-Q0128
Fix for Strong Intra Smoothing in RExt
Copyright 2014 Sony Corporation
Jun Xu, Ali Tabatabai, Ohji Nakagami, Teruhiko Suzuki
Sony Electronics Inc. Sony Corporation

## Slide 2: Introduction
Mismatch between RExt text and software on Strong Intra Smoothing (SIS).
  Text draft: SIS is allowed for all color components in JCTVC-P1005_v1
    8.4.5.2.1: Conditions to call the neighboring pixel filtering process for intra pred.
    When intra_smoothing_disabled_flag is equal to 0 and either cIdx is equal to 0 or ChromaArrayType is equal to 3, the filtering process of neighbouring samples specified in subclause 8.4.5.2.3 is invoked…
    8.4.5.2.3 : Conditions to apply SIS
    – filterFlag is equal to 1 (predModeIntra is not equal to INTRA_DC and nTbS is not equal 4)
    – strong_intra_smoothing_enabled_flag is equal to 1
    – nTbS is equal to 32
    – Abs( p[ −1 ][ −1 ] + p[ nTbS * 2 − 1 ][ −1 ] – 2 * p[ nTbS − 1 ][ −1 ] ) < ( 1 << ( BitDepthY − 5 ) )
    – Abs( p[ −1 ][ −1 ] + p[ −1 ][ nTbS * 2 − 1 ] – 2 * p[ −1 ][ nTbS − 1 ] ) < ( 1 << ( BitDepthY − 5 ) )
  Software: SIS is allowed only for luma in HM13.0+RExt6.0
    @ initAdiPatternChType() of TComPattern.cpp
    Bool useStrongIntraSmoothing = isLuma(chType) && pcCU->getSlice()->getSPS()->getUseStrongIntraSmoothing();

## Slide 3: Proposal
Proposed to align the text to the software.
  SIS is allowed for luma ONLY.
Pros
  Maintain coding efficiency under CTC.
Proposed text: add the condition in 8.4.5.2.3
  – filterFlag is equal to 1 (predModeIntra is not equal to INTRA_DC and nTbS is not equal 4)
  – strong_intra_smoothing_enabled_flag is equal to 1
  – nTbS is equal to 32
  – cIdx is equal to 0
  – Abs( p[ −1 ][ −1 ] + p[ nTbS * 2 − 1 ][ −1 ] – 2 * p[ nTbS − 1 ][ −1 ] ) < ( 1 << ( BitDepthY − 5 ) )
  – Abs( p[ −1 ][ −1 ] + p[ −1 ][ nTbS * 2 − 1 ] – 2 * p[ −1 ][ nTbS − 1 ] ) < ( 1 << ( BitDepthY − 5 ) )

## Slide 4: Simulation results on AHG5
Anchor: HM13.0+RExt6.0
Tested: SIS is allowed for all color components.

## Slide 5: Simulation results on AHG8
Anchor: HM13.0+RExt6.0
Tested: SIS is allowed for all color components.
 | All Intra Main-tier |  |  | All Intra High-tier |  |  | All Intra Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 Animation | 0.2% | 0.2% | 0.2% | 0.1% | 0.1% | 0.1% | 0.1% | 0.0% | 0.0%
RangeExt | 0.2% | 0.2% | 0.1% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC (Optional) | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | Random Access Main-tier |  |  | Random Access High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RGB 4:4:4 SC | 0.0% | 0.1% | 0.0% | 0.1% | 0.1% | 0.1% |  |  | 
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
YCbCr 4:4:4 SC | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.0% |  |  | 
YCbCr 4:4:4 Animation | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% |  |  | 
RangeExt | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RGB 4:4:4 SC (Optional) | 0.1% | 0.1% | 0.2% | 0.0% | 0.0% | 0.0% |  |  | 
YCbCr 4:4:4 SC (Optional) | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% |  |  | 
 | Low delay B Main-tier |  |  | Low delay B High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RGB 4:4:4 SC | 0.1% | 0.0% | 0.1% | 0.1% | 0.0% | 0.1% |  |  | 
RGB 4:4:4 Animation | -0.1% | -0.1% | 0.0% | -0.1% | 0.0% | 0.0% |  |  | 
YCbCr 4:4:4 SC | -0.1% | 0.0% | -0.1% | -0.1% | 0.0% | -0.2% |  |  | 
YCbCr 4:4:4 Animation | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% |  |  | 
RangeExt | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RGB 4:4:4 SC (Optional) | -0.7% | -0.8% | -0.7% | -0.2% | -0.3% | -0.3% |  |  | 
YCbCr 4:4:4 SC (Optional) | -0.6% | -0.7% | -0.5% | -0.7% | -0.8% | -0.7% |  |  | 

## Slide 6: Conclusion
Identified mismatch on SIS.
Proposed fix for mismatch on SIS.
  Coding efficiency is maintained for CTC.
Recommend to adopt proposed fix.