## Slide 1: Performance of encoder and parameter only changes for Screen Content Coding JCTVC-Q0140
Joel Sole, Chao Pang, Li Zhang, Krishna Rapaka, Marta Karczewicz

## Slide 2: Proposal
No new tools are introduced in the HEVC Range Extensions design;
Encoder-only improvements and changing parameters
  Increased transform skip size to 8×8
  Increased search area for Intra BC to full frame (JCTVC-Q0139)
  Inter frame motion estimation refinement (JCTVC-Q0147)
  Uniform quantization for RDPCM (JCTVC-Q0148)
  Intra BC refinement with chroma component (JCTVC-Q0175)

## Slide 3: Experimental results
Test 1: anchor is HM-13.0+RExt-6.0 with CfP sequences
Test 2: anchor is the CfP anchor
Test 3: anchor is AVC High 4:4:4 with AHG8 sequences

## Slide 4: RExt 6.1 as anchor with CfP sequences
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | Y | U | V | Y | U | V | Y | U | V
RGB, text & graphics with motion, 1080p | -31.3% | -27.6% | -27.7% | -30.8% | -26.2% | -26.0% | -29.1% | -22.9% | -21.8%
RGB, text & graphics with motion,720p | -22.9% | -16.9% | -17.4% | -29.3% | -22.1% | -23.9% | -31.8% | -21.3% | -23.3%
RGB, mixed content, 1440p | -19.6% | -14.2% | -14.4% | -28.6% | -22.0% | -22.4% | -41.2% | -32.0% | -32.2%
RGB, mixed content, 1080p | -17.1% | -11.9% | -11.8% | -25.6% | -15.1% | -14.5% | -30.6% | -18.2% | -17.0%
RGB, Animation, 720p | -8.8% | 0.5% | 1.2% | -14.2% | -6.0% | -2.3% | -22.6% | -5.2% | -3.1%
YUV, text & graphics with motion, 1080p | -26.7% | -27.0% | -26.7% | -25.9% | -28.8% | -28.7% | -23.8% | -27.8% | -27.3%
YUV, text & graphics with motion,720p | -15.4% | -15.8% | -16.2% | -20.8% | -22.4% | -25.1% | -19.8% | -22.9% | -27.6%
YUV, mixed content, 1440p | -14.7% | -14.8% | -14.8% | -19.7% | -23.2% | -23.1% | -29.4% | -36.8% | -37.0%
YUV, mixed content, 1080p | -12.5% | -13.0% | -12.7% | -15.6% | -20.6% | -19.7% | -18.5% | -23.9% | -23.3%
YUV, Animation, 720p | -0.1% | -0.8% | -0.6% | -1.5% | -10.9% | -13.1% | -7.0% | -14.2% | -18.0%
Enc Time[%] | 117% |  |  | 102% |  |  | 97% |  | 
Dec Time[%] | 93% |  |  | 96% |  |  | 90% |  | 

## Slide 5: The CfP anchor as anchor
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | Y | U | V | Y | U | V | Y | U | V
RGB, text & graphics with motion, 1080p | -41.0% | -37.6% | -37.6% | -36.0% | -31.4% | -31.1% | -31.9% | -25.5% | -24.4%
RGB, text & graphics with motion,720p | -29.2% | -23.5% | -24.0% | -33.8% | -26.7% | -28.4% | -34.4% | -23.6% | -25.9%
RGB, mixed content, 1440p | -24.6% | -19.4% | -19.6% | -31.3% | -25.0% | -25.4% | -42.7% | -33.6% | -33.8%
RGB, mixed content, 1080p | -23.8% | -19.2% | -19.1% | -29.0% | -18.8% | -18.2% | -32.5% | -20.1% | -19.0%
RGB, Animation, 720p | -9.5% | -0.4% | 0.3% | -14.9% | -6.7% | -2.9% | -23.2% | -5.6% | -3.5%
YUV, text & graphics with motion, 1080p | -36.5% | -36.7% | -36.4% | -30.6% | -33.5% | -33.3% | -26.1% | -30.2% | -29.7%
YUV, text & graphics with motion,720p | -21.6% | -22.2% | -22.3% | -25.3% | -27.0% | -29.6% | -22.0% | -25.2% | -29.6%
YUV, mixed content, 1440p | -19.8% | -20.1% | -20.1% | -22.8% | -26.7% | -26.8% | -31.0% | -38.5% | -38.9%
YUV, mixed content, 1080p | -19.1% | -19.9% | -19.6% | -19.2% | -24.2% | -23.4% | -20.5% | -25.9% | -25.2%
YUV, Animation, 720p | -0.8% | -1.5% | -1.2% | -1.9% | -11.3% | -13.3% | -7.2% | -14.1% | -17.8%
Enc Time[%] | 169% |  |  | 109% |  |  | 101% |  | 
Dec Time[%] | 73% |  |  | 92% |  |  | 86% |  | 

## Slide 6: AVC High 4:4:4 as anchor with AHG8 sequences
 | All Intra Main-tier |  |  | All Intra High-tier |  |  | All Intra Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F 4:2:0 SC | -43.2% | -40.6% | -41.7% | -44.7% | -37.8% | -38.3% | -43.8% | -35.5% | -36.2%
Class B 4:2:0 Natural | -22.7% | -19.2% | -17.9% | -19.5% | -19.4% | -19.4% | -13.5% | -17.6% | -19.6%
RGB 4:4:4 SC | -78.4% | -75.2% | -75.5% | -79.2% | -77.1% | -77.4% | -77.6% | -75.9% | -75.9%
RGB 4:4:4 Animation | -47.8% | -38.8% | -37.3% | -43.8% | -37.2% | -36.4% | -38.8% | -32.3% | -31.9%
YCbCr 4:4:4 SC | -64.0% | -61.7% | -63.2% | -65.5% | -61.8% | -63.2% | -64.9% | -61.3% | -62.1%
YCbCr 4:4:4 Animation | -25.4% | -30.1% | -25.8% | -23.2% | -28.4% | -25.4% | -20.8% | -24.3% | -22.3%
RangeExt 4:4:4 Natural | -20.9% | -14.4% | -17.8% | -17.1% | -14.8% | -18.6% | -12.0% | -12.7% | -14.8%
RGB 4:4:4 SC (Optional) | -93.1% | -92.9% | -93.1% | -92.7% | -92.7% | -92.8% | -91.7% | -91.3% | -91.3%
YCbCr 4:4:4 SC (Optional) | -87.6% | -83.6% | -83.6% | -87.9% | -84.4% | -84.1% | -86.6% | -85.3% | -85.1%
 | Random Access Main-tier |  |  | Random Access High-tier |  | 
 | Y | U | V | Y | U | V
Class F 4:2:0 SC | -44.8% | -51.9% | -52.5% | -43.8% | -47.9% | -47.8%
Class B 4:2:0 Natural | -38.0% | -40.9% | -44.8% | -32.2% | -35.4% | -43.5%
RGB 4:4:4 SC | -76.3% | -71.7% | -72.9% | -75.0% | -71.5% | -72.3%
RGB 4:4:4 Animation | -50.6% | -45.0% | -41.4% | -45.6% | -41.0% | -36.8%
YCbCr 4:4:4 SC | -63.1% | -63.1% | -65.9% | -63.4% | -62.6% | -65.1%
YCbCr 4:4:4 Animation | -38.3% | -49.5% | -44.8% | -30.4% | -45.7% | -40.9%
RangeExt 4:4:4 Natural | -29.0% | -23.3% | -19.1% | -24.7% | -31.4% | -26.2%
RGB 4:4:4 SC (Optional) | -90.0% | -89.8% | -90.0% | -91.0% | -90.9% | -91.0%
YCbCr 4:4:4 SC (Optional) | -81.9% | -82.6% | -82.6% | -84.0% | -83.4% | -83.1%
 | Low delay B Main-tier |  |  | Low delay B High-tier |  | 
 | Y | U | V | Y | U | V
Class F 4:2:0 SC | -46.1% | -61.3% | -62.3% | -44.2% | -53.7% | -53.5%
Class B 4:2:0 Natural | -44.4% | -36.5% | -44.8% | -35.6% | -25.9% | -32.7%
RGB 4:4:4 SC | -72.2% | -65.4% | -67.1% | -70.5% | -65.5% | -66.5%
RGB 4:4:4 Animation | -55.9% | -48.2% | -44.6% | -50.0% | -42.8% | -38.3%
YCbCr 4:4:4 SC | -60.3% | -61.2% | -64.7% | -60.2% | -59.6% | -62.8%
YCbCr 4:4:4 Animation | -46.0% | -60.5% | -58.8% | -35.6% | -56.0% | -53.5%
RangeExt 4:4:4 Natural | -36.8% | -38.0% | -34.2% | -32.2% | -38.0% | -40.5%
RGB 4:4:4 SC (Optional) | -87.7% | -87.1% | -87.2% | -89.9% | -89.5% | -89.6%
YCbCr 4:4:4 SC (Optional) | -78.3% | -80.4% | -80.2% | -81.6% | -81.7% | -80.9%

## Slide 7: Conclusions
Performance of encoder and parameter only changes for Screen Content Coding is reported
Significant gains can be obtained from current HEVC Range Extensions design without new tools
Very large gains of the HEVC RExt with respect to AVC High 4:4:4

## Slide 8: Performance of encoder and parameter only changes for Screen Content Coding JCTVC-Q0140
Joel Sole, Chao Pang, Li Zhang, Krishna Rapaka, Marta Karczewicz