## Slide 1: AHG 13: Sub-region extraction – position calculation and comparison of different approaches (JCTVC-Q0159)
JCT-VC 16th Meeting: San José, US, 9–17 Jan. 2014
Tomoyuki Yamamoto, Tomohiro Ikai, Takeshi Tsukuba (SHARP)

## Slide 2: Summary
Proposal:
  modifications on scale and reference position derivation to help sub-region extraction
    SPS syntax to signal “reference layer offsets”
    scale and reference position derivation using “reference layer offsets” and “scaled reference layer offsets”
Benefits:
  It enables support of BL sub-region extraction without any drift in SHVC
  Additionally, it is helpful to support “540p to 720p” scalability.

## Slide 3: Introduction
sub-region extraction in SHVC
  create bitstream corresponding to sub-region (ROI) by
    extracting VCL NAL Unit relating the sub-region for both EL/BL
    rewriting PS and header information
Problem
  cannot keep the same pixel value before and after extraction
    derived scale value could be different
    derived phase between EL and BL pixels could be different
Discussion at the last meeting
  It is commented that there are several other approaches to achieve sub-region extraction in SHVC
   This time, comaprison of different approaches is studied

## Slide 4: Alternative approaches
(B) Drop EL tiles, Empty BL tiles
(C) Drop EL tiles
(D) Re-encoding
(A) Drop EL/BL tiles
(A-1) phase/scale align
(A-2) no phase/scale align
drop slice data
rewrite slice data with empty CTU
decoding and
encoding

## Slide 5: Comparison
 |  | Bitrate (full-region, EL+BL) | Rewriting complexity | Bitrate (sub-region, EL+BL) | Decoding comlexity
A | Drop EL/BL tiles | 105% (*), tiling | easy (drop slice data) | 35% (*) | less complex, need alternative scale support
B | Drop EL tiles Empty BL tiles | 105% (*), tiling | not so difficult (empty slice data) | 35% + α (*) | relatively complex (need BL empty CTUs)
C | Drop EL tiles No BL change | 102% (*), tiling | easy (drop slice data) | 56% (*) | complex (need full BL decode)
D | Re-encoding | 100% | Very Difficult (need dec & enc) | 33% (*) | low complex
Ref | No extraction | 100% | no rewriting | 100% | very complex (need full EL/BL decode)
negative
positive
* assumptions:
1) EL bitrate is 200% of corresponding BL
2) bitrate increase by tiling: 3% for EL, 9% for BL
3) sub-region area is 1/3 of full-region

## Slide 6: Sub region extraction example
extraction
EL
BL
ELW0 = SRLW0
BLW0
EL
BL
ELW1
SRLW1
BLW1
A
B
C
D
Phase could be different from “A and B” to “C and D”
Scale could be different (cf. “BLW0 / SRLW0” and “BLW1 / SRLW1”)

## Slide 7: Reference layer offsets
extraction
EL
BL
ELW0 = SRLW0
BLW0
EL
BL
ELW1
AltBLW1
SRLW1
BLW1
RefLayerLeft/TopOffset (negative value)
RefLayerRight/BottomOffset (negative value)
ScaledRefLayerTop/LeftOffset
ScaledRefLayerBottom/RightOffset
EL picture
SRL picture
BL picture
Alt BL picture

## Slide 8: RefLayerOffset syntax in SPS extension
sps_multilayer_extension( ) { | Descriptor
inter_view_mv_vert_constraint_flag | u(1)
num_scaled_ref_layer_offsets | ue(v)
for( i = 0; i < num_scaled_ref_layer_offsets; i++) { | 
scaled_ref_layer_id[ i ] | u(6)
scaled_ref_layer_left_offset[ scaled_ref_layer_id[ i ] ] | se(v)
scaled_ref_layer_top_offset[ scaled_ref_layer_id[ i ] ] | se(v)
scaled_ref_layer_right_offset[ scaled_ref_layer_id[ i ] ] | se(v)
scaled_ref_layer_bottom_offset[ scaled_ref_layer_id[ i ] ] | se(v)
} | 
num_ref_layer_offsets | ue(v)
for( i = 0; i < num_ref_layer_offsets; i++) { | 
ref_layer_id[ i ] | u(6)
ref_layer_left_offset[ ref_layer_id[ i ] ] | se(v)
ref_layer_top_offset[ ref_layer_id[ i ] ] | se(v)
ref_layer_right_offset[ ref_layer_id[ i ] ] | se(v)
ref_layer_bottom_offset[ ref_layer_id[ i ] ] | se(v)
} | 
} | 
reference layer offset variables are derived as follows
RefLayerLeftOffset = (ref_layer_left_offset [ref_layer_id[i]] << 1)
ref_layer_left_offset[ ref_layer_id[ i ] ] specifies the horizontal offset between the top-left luma sample of the alternative inter-layer reference picture with nuh_layer_id equal to ref_layer_id[ i ] and the top-left luma sample of the inter-layer reference picture with nuh_layer_id equal to ref_layer_id[ I ] in units of two luma samples. When not present, the value of ref_layer_left_offset[ ref_layer_id[ i ] ] is inferred to be equal to 0.

## Slide 9: Scale and reference position derivation
AltRefLayerPicWidthInSamplesY = RefLayerPicWidthInSamplesY – RefLayerLeftOffset – RefLayerRightOffset
ScaleFactorX = ( ( AltRefLayerPicWidthInSamplesY << 16 ) + ( ScaledRefLayerPicWidthInSamplesY >> 1 ) ) / ScaledRefLayerPicWidthInSamplesY
BL
ELW1
AltBLW1
SRLW1
BLW1
(RefLayerLeftOffset, RefLayerTopOffset)
(RefLayerRightOffset, RefLayerBottomOffset)
ScaledRefLayerTop/LeftOffset
ScaledRefLayerBottom/RightOffset
offsetXRef = ( RefLayerLeftOffset << 4 )/ ( ( cIdx = = 0) ? 1 : SubWidthC)
xRef16 = ( ( ( xP – offsetX ) * ScaleFactorX + addX + ( 1 << 11 ) ) >> 12 ) – ( phaseX << 2 ) + offsetXRef
Scale
Reference position
xRef = ( ( xP − ScaledRefLayerLeftOffset ) * ScaleFactorX + ( 1 << 15 ) ) >> 16 + RefLayerLeftOffset

## Slide 10: On 520p to 720p scalability
Ericsson pointed out the problem of 520p to 720p spatial scalability in JCTVC-Q0104.
520p to 720p scalability can be seen as extraction from base-layer
With proposed method, correct correspondence between EL and BL pixel can be configured.
EL
BL
540
RefLayerBottomOffset = -4
544
720

## Slide 11: Results for 540p to 720p scalability
 | AI HEVC 4/3x |  |  | RA HEVC 4/3x |  |  | LD HEVC 4/3x |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A |  |  |  |  |  |  |  |  | 
Class B | -12.1% | -13.0% | -13.1% | -9.6% | -9.1% | -9.3% | -8.8% | -8.0% | -8.2%
Overall (Test vs Ref) | -12.1% | -13.0% | -13.1% | -9.6% | -9.1% | -9.3% | -8.8% | -8.0% | -8.2%
Overall (Test vs single layer) | 12.1% | 8.3% | 7.5% | 22.8% | 26.8% | 27.1% | 31.1% | 35.2% | 36.4%
Overall (Ref vs single layer) | 27.7% | 24.5% | 23.7% | 35.8% | 39.7% | 40.4% | 43.7% | 46.9% | 48.7%
EL only (Test vs Ref) | -38.5% | -38.9% | -39.0% | -29.1% | -28.5% | -28.6% | -26.4% | -25.5% | -25.6%
Enc Time[%] | 99.1% |  |  | 97.6% |  |  | 98.7% |  | 
Dec Time[%] | 93.0% |  |  | 96.4% |  |  | 97.0% |  | 
BL Match | Matched |  |  | Matched |  |  | Matched |  | 
Proposed method achieves almost the same gain compared to those reported in Q0104
Small difference may be due to difference in signalling additional parameters in parameter set
Anchor: SHM-5.0 with scalad_reference_layer_bottom_offset = -3
Test: Proposed method with reference_layer_bottom_offset = -2

## Slide 12: Conclusion
This contribution proposes:
  new “reference layer offset” syntax
  modified scale and reference position derivation
The proposed changes helps to keep reconstructed pixel values after sub-region extraction  light sub-region extraction process can be supported
In addition, 540p to 720p scalability can be handled
It is recommended to adopt the proposed changes in SHVC