## Slide 1: Layer association of auxiliary pictures (JCTVC-Q0161, JCT3V-H0049)
JCT-VC 17th Meeting: Valencia, ES, 27 Mar. – 4 Apr. 2014
JCT-3V 8th Meeting: Valencia, ES, 29 Mar. – 4 Apr. 2014
Tomohiro Ikai
SHARP Corporation

## Slide 2: Summary
Motivation
  Non-intentional association in multiple dependent tree case
  When ScalabilityId is different, the auxiliary picture sharing cannot be achieved
  Proposal
  Proposal 1
    Add new scalability dimension, named “UserId”, to distinguish a layer among layers which have the same ScalabilityId[ i ][ j ].
  Proposal 2
    Add a flag, called aux_mask_flag [j], for each ScalabilityId[ ][ j ] to control association.

## Slide 3: BackGround
Auxiliary picture / Primary picture association
For an auxiliary picture with nuh_layer_id equal to nuhLayerIdA, an associated primary pictures, if any, is the picture in the same access unit having AuxId[ nuhLayerIdB ] equal to 0 such that ScalabilityId[ LayerIdxInVps[ nuhLayerIdA ] ][ j ] is equal to ScalabilityId[ LayerIdxInVps[ nuhLayerIdB ] ][ j ] for all values of j in the range of 0 to 2, inclusive, and 4 to 15, inclusive.
ScalabilityId Equaliness is used for association

## Slide 4: Problem: duplicate sending
Auxiliary picture sharing in not possible in main use case (Duplicate sending is inevitable)
  EL and BL utilizes the same alpha
  Left view and right view associate with the center depth
Auxiliary picture
(AuxId=1)
Primary picture
(AuxId=0)
Enhancement layer
(ScalabilityId[2]=1)
Base layer
(ScalabilityId[2]=0)
Alpha picture
(ScalabilityId[2]=0)
NG

## Slide 5: Proposal2 (1)
    Add a flag, called aux_mask_flag [j], for each ScalabilityId[ ][ j ] to control association
vps_extension( ) { | Descriptor
avc_base_layer_flag | u(1)
splitting_flag | u(1)
for( i = 0, NumScalabilityTypes = 0; i < 16; i++ ) { | 
scalability_mask_flag[ i ] | u(1)
NumScalabilityTypes += scalability_mask_flag[ i ] | 
} | 
for( j = 0; j < ( NumScalabilityTypes − splitting_flag ); j++ ) | 
dimension_id_len_minus1[ j ] | u(3)
if (scalability_mask_flag[ 3]) | 
for( j= 0; j < 16 ; i++ ) | 
if (scalability_mask_flag [j] && i != 3) | 
aux_mask_flag[ j ] | u(1)

## Slide 6: Proposal2 (2)
For an auxiliary picture with nuh_layer_id equal to nuhLayerIdA, one or morean associated primary pictures, if any, isare the pictures in the same access unit having AuxId[ nuhLayerIdB ] equal to 0 such that ScalabilityId[ LayerIdxInVps[ nuhLayerIdA ] ][ j ] is equal to ScalabilityId[ LayerIdxInVps[ nuhLayerIdB ] ][ j ] and aux_mask_flag[j] is equal to 1 for all values of j in the range of 0 to 2, inclusive, and 4 to 15, inclusive.
aux_mask_flag[ j ] equal to 1 specify that the primary picture association with nuh_layer_id is specified by the equality of ScalabilityId[ ][ j ]. aux_mask_flag[ j ] equal to 0 specify that auxiliary picture association is not specified by the equality of ScalabilityId[ ][ j ]. When not present, aux_mask_flag[ j ] is inferred to be 0.

## Slide 7: Proposal2 (3)
Allow plural association
It is a requirement of bitstream conformance that there shall be one or more an associated primary pictures for each auxiliary picture with AuxId[ nuh_layer_id ] equal to AUX_ALPHA.

## Slide 8: Problem (non-intentional association)
  Non-intentional association in multiple dependent tree case.
Auxiliary picture
(AuxId=1)
DependencyId=0
Primary picture
(AuxId=0)
DependencyId=0
DependencyId=0
DependencyId=0
Dependent tree A
Dependent tree B
?
?

## Slide 9: Problem (non-intentional association)
Auxiliary picture
(AuxId=1)
DependencyId=0
Primary picture
(AuxId=0)
DependencyId=0
DependencyId=0
DependencyId=0
DependencyId=0

## Slide 10: Proposal1
UserId (Unspecified scalability dimension)
scalability mask index | Scalability dimension | ScalabilityId mapping
0 | Reserved | 
1 | Multiview | View Order Index
2 | Spatial/quality scalability | DependencyId
3 | Auxiliary | AuxId
4-14 | Reserved | 
15 | User | UserId
Note: Unspecified (free) scalability id can be useful in several ways
User specific identifications such as Person Id, City Id, Ray Id, Latitude Id, Language Id ...
Free NAL unit header indication (with splitting flag)

## Slide 11: Proposal1 (2)
Relax ScalabilityId usage restriction for proposed UserId
H.11.1.2 Scalable Main and Scalable Main 10 profiles
The derived sub-bitstream for an output layer set conforming to the Scalable Main or Scalable Main 10 profiles shall obey the following constraints:
…
ScalabilityId[ j ][ smIdx ] shall be equal to 0 for any smIdx value not equal to 2 or 15 and for any value of j for which layer_id_included_flag[ layerSetIdx ][ j ] is equal to 1.
G.11.1.2 Stereo Main profile
The bitstream shall contain a sub-bitstream consisting of two layers having nuh_layer_id equal to 0 and nuhLayerIdA for which ScalabilityId[ LayerIdxInVps[ nuhLayerIdA ] ][ smIdx ] shall be equal to 0 for any smIdx from 0 to 15, inclusive that is not equal to 1 or 15.

## Slide 12: Benefit by proposal2
One auxiliary picture can serve BL and EL
Auxiliary picture
(AuxId=1)
Primary picture
(AuxId=0)
Enhancement layer
(ScalabilityId[2]=1)
Base layer
(ScalabilityId[2]=0)
Alpha picture
(ScalabilityId[2]=0)
OK
aux_mask_flag[2] = 0

## Slide 13: Benefit by proposal1
Auxiliary picture
(AuxId=1)
DependencyId=0
UserId=0
Primary picture
(AuxId=0)
DependencyId=0
UserId=0
DependencyId=0
UserId=0
DependencyId=0
UserId=1
Dependent tree A
Dependent tree B

## Slide 14: Benefit by proposal1
Intentional association
Auxiliary picture
(AuxId=1)
DependencyId=0
UserId=0
Primary picture
(AuxId=0)
DependencyId=0
UserId=0
DependencyId=0
UserId=1
DependencyId=0
UserId=0
DependencyId=0
UserId=1

## Slide 15
Thank you!