## Slide 1: SHVC/MV-HEVC HLS: Scaled offset information of auxiliary pictures (JCTVC-Q0162, JCT3V-H0050)
JCT-VC 17th Meeting: Valencia, ES, 27 Mar. – 4 Apr. 2014
JCT-3V 8th Meeting: Valencia, ES, 29 Mar. – 4 Apr. 2014
Tomohiro Ikai
SHARP Corporation

## Slide 2: Summary
Motivation
    Two ways for scaled offset information for auxiliary picture are confusing and bring decoder implementation more complex.
  - Case A: SPS of auxiliary pictures carries scaled reference layer offset information
  - Case B: SPS of primary pictures carries scaled reference layer offset information
  Proposal
- SPSs referred from primary pictures shall not have scaled reference layer offset information for auxiliary pictures

## Slide 3: Problem (1)
Two ways of scaled offset information
Primary picture
Auxiliary picture
SRLOffsetTL
SRLOffsetBR
ScaledRefLayerPicWidthInSamplesY
RefLayerPicWidthInSamplesY
PicWidthInSamplesY
(xP, yP)
Primary picture
Auxiliary picture
(xRef, yRef)
(xP, yP)
SRLOffsetBR
ScaledRefLayerPicWidthInSamplesY
(xRef, yRef)
RefLayerPicWidthInSamplesY
SRLOffsetTL
PicWidthInSamplesY
Case A
Case B

## Slide 4: Problem (2)
Decoder confusion
  Some decoder could mistakenly conclude scaled reference layer offset is not applied by just interpreting no scaled offset in SPS of auxiliary picture (but SPS of primary picture may have).
Encoder confusion
  Encoder designer is confused on which SPS should carry that information and may consider scaled reference layer offset should be defined in both SPS of auxiliary picture and SPS of primary picture
Implementation complexity
  Implementation of two ways of coordinate calculations between auxiliary picture and primary picture are needed and the switch of calculation depends on which layer has the scaled offset information.

## Slide 5: Two ways of coordinate calculations
Case A
Case B
The coordinate of (xAux, yAux) on auxiliary picture is corresponds to the coordinate of (xRef, yRef) on primary picture as follows.
xRef = ((xAux - SRLLOffset) * scaleX) + ( 1 << 15 ) ) >> 16
yRef = ((yAux - SRLTOffset) * scaleY) + ( 1 << 15 ) ) >> 16
xAux = ((xRef * invScaleX) + ( 1 << 15 ) ) >> 16) + SRLLOffset
yAux = ((yRef * invScaleY) + ( 1 << 15 ) ) >> 16) + SRLTOffset
The coordinate of (xAux, yAux) on auxiliary picture is corresponds to the coordinate of (xP, yP) on primary picture as follows.
xAux = ((xP - SRLLOffset) * scaleX’) + ( 1 << 15 ) ) >> 16
yAux = ((yP - SRLTOffset) * scaleY’) + ( 1 << 15 ) ) >> 16
xP = ((xAux * invScaleX’) + ( 1 << 15 ) ) >> 16) + SRLLOffset
yP = ((yAux * invScaleY’) + ( 1 << 15 ) ) >> 16) + SRLTOffset

## Slide 6: Proposal
Allow only Case A (by disablling Case B)
It is bitstream conformance that SPSs referred from primary pictures shall not have scaled reference layer offset information for auxiliary pictures

## Slide 7
Thank you!