## Slide 1: JCTVC-Q0204r4 - HEVC verification test results
TK Tan, M. Mrak, V. Baroncini and N. Ramzan
Ahg 19: Verification test preparation and testing
28 March 2014

## Slide 2: Executive Summary
Purpose of the HEVC verification test
  To confirm that the objective of achieving a substantially greater bit-rate reduction over the AVC High Profile has been met by the HEVC standard.
What was done
  A subjective evaluation was conducted comparing the HEVC Main profile to the AVC High profile.
  20 video sequences with resolutions ranging from 480p to UHD were tested (at 4 different bit-rates / quality levels) .
Results
  Analysis of the subjective test results show that in 86% of the test points, HEVC and AVC have the same quality, even though the bit-rates of AVC are greater than or equal to approximately double the HEVC bit-rates.
  The bit-rate savings are similar for the different resolutions tested, with slightly more savings for sequences with higher resolutions. The average bit-rate savings for UHD, 1080p, 720p and 480p are estimated at approximately 64%, 62%, 56% and 52%, respectively.

## Slide 3: Conclusion
The results confirmed that the HEVC Main profile achieves the same subjective quality as AVC High profile while requiring on average approximately 59% less bit-rate.

## Slide 4: Test Logistics
Test sequences were donated by 8 organizations.
  4EVER, BBC, Kamerawerk, NTIA, Plannet, Inc., SVT, Technicolor, Vidyo
Test bitstreams were encoded by NTT DOCOMO, Inc. using the HM12.1 and JM18.5 reference software.
The subjective test was carried out at the following test sites coordinated by Vittorio Baroncini (MPEG Test Chair).
  British Broadcasting Corporation (BBC) R&D
  School of Computing, University of West of Scotland
Thank you to all the organizations and individuals who contributed to the HEVC verification test.

## Slide 5: Summary of the MOS vs. bit-rate plots
The complete set of plots for the 20 sequences tested can be found at the end of the slides.
All the plots with the exception of the WheelAndCalender sequence, show that the rate distortion (RD) curves of the HEVC test points are located substantially to the left of the RD-curves of the AVC test points.
The MOS scores of HECV test points were compared to the MOS scores of AVC test points.
The number test points was counted and tabulated for the cases where the MOS confidence intervals (CI) of the HEVC test points overlap with the MOS CI of the AVC test points having bit-rates where the bit-rates of AVC are
  greater than approximately double the bit-rates of HEVC.
  equal to approximately double the bit-rates of HEVC.
  less than approximately double the bit-rates of HEVC.

## Slide 6: Statistics of HEVC test points
The table shows that
  45% of the HEVC test points have the same quality as AVC at approximately double the bit-rates of the HEVC test points.
  41% of the HEVC test points have the same quality as AVC at greater than approximately double the bit-rates of the HEVC test points.
  only 14% of the HEVC test points have the same quality as AVC at less than approximately double the bit-rates of the HEVC test points.
Statistically, 86% of the data show that the quality of HEVC is indistinguishable from the quality of AVC at bit-rates that are greater than or equal to approximately double the HEVC bit-rates.

## Slide 7: Summary of MOS BD-rate
* In order for the BD-rate interpolation to work correctly, the MOS values should exhibit a smooth curve, and the range of the averaging (shown as solid lines in the plots) should be interpolated from at least three MOS scores that are monotonically increasing with bit-rate. The sequences HomelessSleeping and WheelAndCalender did not satisfy this requirement and hence was not included in these results.
In order to get a quantitative bit-rate savings, the following is done:
  Average bit-rate savings of HEVC compared to AVC for each sequence were computed from the MOS vs. bit-rate plots using the BD-rate method
  Two averaging intervals were used:
    Full MOS scale (maximum range)
    MOS >= 7 (range where the picture quality is considered suitable for services)
  Two sequences were excluded (see * below)
Overall average show that HEVC gives:
  59% (full MOS range) and
  57% (MOS >=7)
  bit-rate savings over AVC while having the same subjective quality.

## Slide 8: Graphical representation of MOS BD-rate
Overall Average show that HEVC gives:
  59% (full MOS range) and
  57% (MOS >=7)
  bit-rate savings over AVC while having the same subjective quality.

## Slide 9: Example of MOS vs. bit-rate plots
4 examples of the MOS vs. bit-rate plots are shown in the subsequent slides.
The eleven-grade MOS scale from 0 to 10 as shown in the plots may be interpreted as follows

## Slide 10
R1
R1
R2
R2
R3
R3
R4
R4
MOS BD-rate = -75% MOS (>= 7) BD-rate = -70%
MOS vs. bit-rate plot (example with bit-rate savings > 50%)
Most plots are similar to this

## Slide 11
R1
R1
R2
R2
R3
R3
R4
R4
MOS vs. bit-rate plot (example with bit-rate savings ~ 50%)
Large number of plots are similar to this
MOS BD-rate = -49% MOS (>= 7) BD-rate = -50%

## Slide 12
R1
R1
R2
R2
R3
R3
R4
R4
MOS vs. bit-rate plot (example with bit-rate savings < 50%)
A few plots are similar to this
MOS BD-rate = -36% MOS (>= 7) BD-rate = -35%

## Slide 13: MOS vs. bit-rate plot (unclear) This is an isolated case that was excluded
R1
R1
R2
R2
R3
R3
R4
R4
Sequence was excluded from the BD-rate calculations

## Slide 14: Comparison of MOS BD-rate and PSNR BD-rate
MOS BD-rate is consistently higher than the PSNR BD-Rate by approximately 14% on average. (-1% min, 35% max)
  HEVC is better than AVC by 59% subjectively compared to 45% objectively.

## Slide 15: Conclusions
Conclusions
  Analysis of the subjective test results show that in 86% of the test points, HEVC and AVC have the same quality, even though the bit-rates of AVC are greater than or equal to approximately double the HEVC bit-rates.
  By applying the MOS BD-rate measurement on the results of the subjective test, it is estimated that the HEVC Main profile achieves the same subjective quality as AVC High profile while requiring on average approximately 59% less bit-rate.
  The objective of achieving a substantially greater bit-rate reduction over the AVC High Profile has been met by the HEVC standard.

## Slide 16: MOS vs. bit-rate plots

## Slide 17
R1
R1
R2
R2
R3
R3
R4
R4
MOS BD-rate = -75% MOS (>= 7) BD-rate = -70%
MOS vs. bit-rate plot (>50%)

## Slide 18
R1
R1
R2
R2
R3
R3
R4
R4
MOS BD-rate = -66% MOS (>= 7) BD-rate = -65%
MOS vs. bit-rate plot (>50%)

## Slide 19
R1
R1
R2
R2
R3
R3
R4
R4
MOS vs. bit-rate plot (>50%)
Sequence was excluded from the BD-rate calculations

## Slide 20
R1
R2
R2
R3
R3
R4
R4
R1
MOS BD-rate = -56% MOS (>= 7) BD-rate = -56%
MOS vs. bit-rate plot (~50%)

## Slide 21
R1
R2
R2
R3
R3
R4
R4
R1
MOS BD-rate = -58% MOS (>= 7) BD-rate = -50%
MOS vs. bit-rate plot (>50%)

## Slide 22
R1
R2
R2
R3
R3
R4
R4
R1
MOS BD-rate = -70% MOS (>= 7) BD-rate = -73%
MOS vs. bit-rate plot (>50%)

## Slide 23
R1
R2
R2
R3
R3
R4
R4
R1
MOS BD-rate = -52% MOS (>= 7) BD-rate = -46%
MOS vs. bit-rate plot (~50%)

## Slide 24
R1
R2
R2
R3
R3
R4
R4
R1
MOS BD-rate = -69% MOS (>= 7) BD-rate = -60%
MOS vs. bit-rate plot (>50%)

## Slide 25
R1
R2
R2
R3
R3
R4
R4
R1
MOS BD-rate = -53% MOS (>= 7) BD-rate = -56%
MOS vs. bit-rate plot (~50%)

## Slide 26
R1
R1
R2
R2
R3
R3
R4
R4
MOS BD-rate = -68% MOS (>= 7) BD-rate = -52%
MOS vs. bit-rate plot (>50%)

## Slide 27
R1
R1
R2
R2
R3
R3
R4
R4
MOS BD-rate = -48% MOS (>= 7) BD-rate = -53%
MOS vs. bit-rate plot (~50%)

## Slide 28
R1
R1
R2
R2
R3
R3
R4
R4
MOS BD-rate = -66% MOS (>= 7) BD-rate = -65%
MOS vs. bit-rate plot (>50%)

## Slide 29
R1
R1
R2
R2
R3
R3
R4
R4
MOS BD-rate = -58% MOS (>= 7) BD-rate = -58%
MOS vs. bit-rate plot (>50%)

## Slide 30
R1
R1
R2
R2
R3
R3
R4
R4
MOS BD-rate = -73% MOS (>= 7) BD-rate = -73%
MOS vs. bit-rate plot (>50%)

## Slide 31
R1
R1
R2
R2
R3
R3
R4
R4
MOS BD-rate = -36% MOS (>= 7) BD-rate = -35%
MOS vs. bit-rate plot (<50%)

## Slide 32
R1
R1
R2
R2
R3
R3
R4
R4
MOS BD-rate = -45% MOS (>= 7) BD-rate = -45%
MOS vs. bit-rate plot (~50%)

## Slide 33
R1
R1
R2
R2
R3
R3
R4
R4
MOS BD-rate = -42% MOS (>= 7) BD-rate = -40%
MOS vs. bit-rate plot (<50%)

## Slide 34
R1
R1
R2
R2
R3
R3
R4
R4
MOS BD-rate = -49% MOS (>= 7) BD-rate = -50%
MOS vs. bit-rate plot (~50%)

## Slide 35
R1
R1
R2
R2
R3
R3
R4
R4
MOS BD-rate = -72% MOS (>= 7) BD-rate = -74%
MOS vs. bit-rate plot (>50%)

## Slide 36: MOS vs. bit-rate plot (unknown)
R1
R1
R2
R2
R3
R3
R4
R4
Sequence was excluded from the BD-rate calculations