## Slide 1: Proposal to support 12 bit video in SHVC (JCTVC-Q0206)
Teruhiko Suzuki, Cheung Auyeung and Kazushi Sato
teruhikos@jp.sony.com
Notes: 1

## Slide 2: Background
Propose to investigate 4:2:0 12 bit support in SHVC
  Currently bit depth scalability in SHVC is limited up to 10 bit
  However, in UHDTV, for example ITU-R BT.2020, 4K video is defined for both 10 bit and 12 bit
  In addition, 4:2:0 12 bit profile is defined in RExt and the profile is used for consumer application in near future
  Therefore, in SHVC bit depth scalability profile in SHVC, 12 bit video should be allowed for both BL and EL.
  This contribution proposes to allow to use 4:2:0 12 bit video in bit depth scalability profiles in SHVC.

## Slide 3: Proposal
Proposals are,
  To add 4:2:0 12 bit video capability in SHVC (with the tools limited to the tools in 4:2:0 12 bit profile)
  To check the performance of bit depth scalability with 12 bit video, e.g. by SCE
  To consider to include 12 bit video capability in profiles supporting bit depth scalability
4:2:0 12 bit video should be allowed for both BL and EL
Tools for 12 bit in BL and EL should be the same as 4:2:0 12 bit profile

## Slide 4: Initial test
The test sequence
  FruitStall in 4096x2160 at 24fps in YUV 4:2:0
    Generated 10 bit and 12 bit from 16 bit
  BL: 10 bits
  EL: 12 bits
Software
  SHM-5.0-IRAP from JCTVC-Q0130 [2] using the QPs for 1x scalability from SCE1 [1]
  RExt-6.0, HM-13.0 for single layer

## Slide 5: Results

## Slide 6: Results AI
Chart: Y PSNR vs Bitrate
| 126942.65919999999 | 64654.2592 | 36857.743999999999 | 23574.995999999999
SHM-5.0-anchor with bug fixed from JCTVC-Q0130 | 45.7815 | 43.7202 | 42.1057 | 40.534
#REF! | 45.9284 | 43.9164 | 42.3871 | 40.9158
#REF! | 45.9157 | 43.912 | 42.3909 | 40.9125

## Slide 7: Results RA
Chart: Y PSNR vs Bitrate
| 7338.3136000000004 | 3012.4168 | 1579.5272 | 925.98079999999993
SHM-5.0-anchor with bug fixed from JCTVC-Q0130 | 43.4409 | 42.3437 | 41.068 | 39.5555
Rext-6.0 | 43.3467 | 42.2474 | 41.0154 | 39.5034
HM-13.0 | 43.3504 | 42.2538 | 41.0259 | 39.515

## Slide 8: Proposal
Proposals are,
  To add 4:2:0 12 bit video capability in SHVC (with the tools limited to the tools in 4:2:0 12 bit profile)
  To check the performance of bit depth scalability with 12 bit video, e.g. by SCE
  To consider to include 12 bit video capability in profiles supporting bit depth scalability
4:2:0 12 bit video should be allowed for both BL and EL
Tools for 12 bit in BL and EL should be the same as 4:2:0 12 bit profile