## Slide 1
Jill Boyce
JCTVC-R0041: Use of general_profile_space for auxiliary picture profile indication

## Slide 2: Introduction
In HEVC version 1, the base layer must have nuh_layer_id equal to 0
  NAL units with other values of nuh_layer_id are discarded by a decoder
Useful for enhancement layers (auxiliary pictures, simulcast layer) that otherwise conform to an HEVC version 1 single layer profile (Main, Main 10, etc.) to indicate profile conformance
Propose to use an unused value of the general_profile_space syntax element to indicate that a layer with a non-zero value of nuh_layer_id in a multi-layer bitstream is otherwise conforming to a single layer profile

## Slide 3: Details
Initial version proposed defining additional “Extension” profiles to indicate that a non-zero base layer allowed
The v4 version of the document alternatively defines an Independent non base layer decoding (INBLD) process in Annex F
general_profile_space has 2 bits, version 1 requires that it be equal to 0

## Slide 4: Discussion
It is asserted that having an explicit indication of a non-zero base layer decoding requirement in the profile/tier/level syntax elements is advantageous for simple description of bitstream characteristics (and required decoder capability) and systems layer integration
AHG10 discussed alternative solutions
  No explicit indication
  Use one of the general_reserved_zero_44bits