## Slide 1
Jill Boyce
JCTVC-R0041: Use of general_profile_space for auxiliary picture profile indication

## Slide 2: Introduction
In HEVC version 1, the base layer must have nuh_layer_id equal to 0
  NAL units with other values of nuh_layer_id are discarded by a decoder
Useful for enhancement layers (auxiliary pictures, simulcast layer) that otherwise conform to an HEVC version 1 single layer profile (Main, Main 10, etc.) defined in Annex A to indicate profile conformance
Propose to use the profile_tier_level( ) syntax structure to indicate that a layer with a non-zero value of nuh_layer_id in a multi-layer bitstream is otherwise conforming to a single layer profile

## Slide 3: Independent Non Base Layer Decoding (INBLD) capability
Contribution was discussed during several AHG10 conference calls and in JCT-VC track discussion in Sapporo
  Multiple versions of the document have been created, with different alternatives, following discussion
Initial version proposed defining additional “Extension” profiles to indicate that a non-zero base layer allowed
  Main and Extension Main, Main 10 and Extension Main 10, etc.
The v4 version of the document alternatively defines an Independent non base layer decoding (INBLD) process in Annex F, rather than defining a new profile
  Single layer profile decoders could easily add support for INBLD capability, but version 1 decoders would not be required to support

## Slide 4: Bitstream indication
It is asserted that having an explicit indication of a non-zero base layer decoding requirement in the profile/tier/level syntax elements is advantageous for simple description of bitstream characteristics (and required decoder capability) and systems layer integration
AHG10 discussed alternative solutions
  Use one of the general_reserved_zero_44bits
    Preferred option during JCT-VC track discussion
  Use a value of general_profile_space
  No explicit indication