## Slide 1: SCCE4: Results of subtest 3.3
Liping Zhao, Xianyi Chen, Tao Lin
Jing Ye, Shan Liu, Shawmin Lei

## Slide 2
115/07/29
Copyright © MediaTek Inc. All rights reserved.
<number>
Pos (=DV in IBC)
Len = the length of the string
Unmatched sample (=escape color in palette)
Basic Elements of String Matching

## Slide 3: Current options of dictionary size
115/07/29
Copyright © MediaTek Inc. All rights reserved.
<number>
dictionary size option # | dictionary (part of reconstructed pixel buffer) size (KB) | hash table size (KB) encoder only | 
 |  | sample-based | pixel-based
1 | 4 | 10.5 | 5.2
2 | 8 | 19 | 8.4
3 | 16 | 36 | 14.7
4 | 64 | 138 | 52.7
5 | 256 | 1,092 | 308
6 | 1,024 | 4,356 | 1220
7 | 4,096 | 16,644 | 4292

## Slide 4
115/07/29
Copyright © MediaTek Inc. All rights reserved.
<number>
Maximum matching string length: extended from 273 to 12288
Bijective mapping for the whole value range of pos and len
Color quantization (CQ) pre-processing
Enhancements in this subtest

## Slide 5: Bijective mapping for pos and len
Maps more frequently occurred values to smaller values.
115/07/29
Copyright © MediaTek Inc. All rights reserved.
<number>
Mapping of pos for depth = 3 | 
Pre-map value | Post-map value
3 | 0
21, 24, 27 | 1, 2, 3
48 | 4
12, 15, 18 | 5, 6, 7
72, 96 | 8, 9
6, 9 | 10, 11
30, 33, 36, 39 | 12, 13, 14, 15
120, 144, ……, 216, 240 | 16, 17, ……, 20, 21
42, 45, 51, 54, ……, 66, 69, 75 | 22, 23, 24, 25, ……, 29, 30, 31
…… | ……

## Slide 6
115/07/29
Copyright © MediaTek Inc. All rights reserved.
<number>
Mapping of pos for depth = 2 | 
Pre-map value | Post-map value
3 | 0
45, 48, 51 | 1, 2, 3
96 | 4
12, 15, 18 | 5, 6, 7
144, 54 | 8, 9
6, 9 | 10, 11
21, 24, 27, 30 | 12, 13, 14, 15
192,240 | 16,17
87,90,93 | 18,19,20
33,36,39,42 | 21,22,23,24
57,60,……,72,75 | 25,26,……,30,31
288,336,384 | 32,33,34
78,81,84 | 35,36,37
,…… | ……

## Slide 7
115/07/29
Copyright © MediaTek Inc. All rights reserved.
<number>
Mapping of pos for depth = 1 | 
Pre-map value | Post-map value
3 | 0
93, 96, 99 | 1, 2, 3
192 | 4
90, 18, 21 | 5, 6, 7
288,384 | 8, 9
6, 9 | 10, 11
87, 12, 15, 24 | 12, 13, 14, 15
480 | 16
27,30,……,66,69 | 17,18,……,30,31
576,672,768 | 32,33,34
72,75,……,81,84 | 35,36,……,38,39
…… | ……

## Slide 8
115/07/29
Copyright © MediaTek Inc. All rights reserved.
<number>
Mapping of pos for depth = 0 | 
Pre-map value | Post-map value
3 | 0
192,384,189 | 1, 2, 3
576 | 4
12,15,18 | 5, 6, 7
768 | 8
6, 9 | 9 ,10
195 | 11
21,24,27,30 | 12,13,14,15
960,1152 | 16,17
183,186,198 | 18,19,20
33,36,……,60,63 | 21,22,……,30,31
1344,1536 | 32,33
66,69,……,150,153 | 34,35,……,62,63
1728,1920,……,3648,3840 | 64,65,……,74,75
…… | ……

## Slide 9
115/07/29
Copyright © MediaTek Inc. All rights reserved.
<number>
Mapping of length (all depths) | 
Pre-map value | Post-map value
3,6,……,45,48 | 0,1,……, 14,15
2,5……,20,23 | 16,17,……,22,23
51,54,……,69,72 | 24,25,……,30,31
4,7,……,22,25 | 32,33,……,38,39
75,78,……,93,96 | 40,41,……,46,47
26,29,……,44,47 | 48,49,……,54,55
28,31,……,46,49 | 56,57,……,62,63
99,102,……,141,144 | 64,65,……,78,79
50,53,……,68,71 | 80,81,……,86,87
52,55,……70,73 | 88,89,……94,95
…… | ……

## Slide 10: CU level string matching
115/07/29
Copyright © MediaTek Inc. All rights reserved.
<number>
coding_unit( x0, y0, log2CbSize ) { | Descriptor
… | 
else { | 
if( intra_block_copy_enabled_flag ) | 
intra_bc_flag[ x0 ][ y0 ] | ae(v)
if( !intra_bc_flag[ x0 ][ y0 ] ) { | 
if(intra_p2m_enabled_flag ) | 
intra_p2m_flag[ x0 ][ y0 ] | ae(v)
if(intra_p2m_flag[ x0 ][ y0 ] ) | 
p2m_coder( x0, y0, log2CbSize ) | 
} | 
if( !intra_p2m_flag [ x0 ][ y0 ] ){ | 
if( slice_type != I && !intra_bc_flag[ x0 ][ y0 ]) | 
pred_mode_flag | ae(v)
… | 
} | 
} | 
} | 

## Slide 11: Memory bandwidth merit of 1D over 2D
1-D vs 2-D: typically 70%-50% less in DDR case 50%-30% less in SRAM case

## Slide 12: Lossy results (Search range size=64KB)
Anchor: SCM1.0 FullFrame IBC
-13.9%, -8.9%, -4.6% BD-rate savings for TGM YUV 1080p AI, RA, LB

## Slide 13
Anchor: SCM1.0 FullFrame IBC
-14.5%, -9.2%, -4.9% BD-rate savings for TGM YUV 1080p AI, RA, LB
Lossy results (Search range size=1MB)

## Slide 14
Anchor: SCM1.0 2CTU IBC
-15.6%, -10.4%, -5.4% BD-rate savings for TGM YUV 1080p AI, RA, LB
Lossy results (Search range size=16KB)

## Slide 15
Anchor: SCM1.0 FullFrame IBC
26.1%, 17.1%, 13.6% average bit-rate savings for TGM YUV 1080p AI, RA, LB
Lossless results (Search range size=1MB)

## Slide 16
Lossless results (Search range size=64KB)
Anchor: SCM1.0 FullFrame IBC
23.3%, 14.9%, 11.6% average bit-rate savings for TGM YUV 1080p AI, RA, LB

## Slide 17: Search range size 64KB vs 1MB, lossless
 | All Intra |  |  | 
 | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
RGB, text & graphics with motion, 1080p | 3.1% | 2.9% | 1.6% | 4.2%
RGB, text & graphics with motion,720p | 1.0% | 0.9% | 0.1% | 2.2%
RGB, mixed content, 1440p | 0.3% | 0.3% | 0.3% | 0.4%
RGB, mixed content, 1080p | 0.8% | 0.8% | 0.8% | 0.8%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | 3.8% | 3.7% | 3.3% | 4.3%
YUV, text & graphics with motion,720p | 1.1% | 1.1% | 0.1% | 2.4%
YUV, mixed content, 1440p | 0.5% | 0.6% | 0.3% | 0.9%
YUV, mixed content, 1080p | 1.1% | 1.1% | 1.1% | 1.1%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 112% |  |  | 
Dec Time[%] | 94% |  |  | 

## Slide 18
Lossless results (Search range size=16KB)
Anchor: SCM1.0 2CTU IBC
26.4%, 17.2%, 13.0% average bit-rate savings for TGM YUV 1080p AI, RA, LB

## Slide 19
Conclusions
len extended and bijective mapping for pos & len
Color quantization (CQ) pre-processing
64KB search range (5.3 CTUs) captures most gain, 96% in lossy case and 90% in lossless case
1D has significant memory BW advantage over 2D
Still have significant room for improvement
Palette coding is a special case of SM with an additional small dictionary (palette) and coding pos (matching distance) as index map
Suggest further study in CE and TE