## Slide 1: JCTVC-R0061: SCCE1 Test 3.4: IntraBC BV prediction
Xiaozhong Xu, Shan Liu and Shawmin Lei

## Slide 2: Outlines
Introduction
Proposed method
Changes in syntax and semantics
Simulation results
Conclusion

## Slide 3: Introduction
Block Vector Prediction in SCM-1.0
  The last coded IntraBC BV is stored to predict current IntraBC BV
  Updated for each IntraBC coded PU
  Reset at each CTU with (-w, 0)

## Slide 4: Proposed BV prediction method
AMVP-like prediction, no temporal BV predictors
Use default vectors (-2w, 0) and (-w, 0) when spatial candidates are not available
Use one flag to signal which candidate (above or left) to use
Share the context with mvp_l0_flag

## Slide 5: Syntax/semantics changes
In coding_unit()
  IntraBC flag is signaled at CU, IntraBC mvd coding is moved to PU
coding_unit( x0, y0, log2CbSize ) { | Descriptor
if( transquant_bypass_enabled_flag ) | 
cu_transquant_bypass_flag | ae(v)
if( slice_type != I ) | 
cu_skip_flag[ x0 ][ y0 ] | ae(v)
nCbS = ( 1 << log2CbSize ) | 
if( cu_skip_flag[ x0 ][ y0 ] ) | 
prediction_unit( x0, y0, nCbS, nCbS ) | 
else { | 
if( intra_block_copy_enabled_flag ) | 
intra_bc_flag[ x0 ][ y0 ] | ae(v)
if( slice_type != I && !intra_bc_flag[ x0 ][ y0 ] ) | 
pred_mode_flag | ae(v)
if( CuPredMode[ x0 ][ y0 ] != MODE_INTRA ¦ ¦ intra_bc_flag[ x0 ][ y0 ] ¦ ¦ log2CbSize = = MinCbLog2SizeY ) | 
part_mode | ae(v)
if( CuPredMode[ x0 ][ y0 ] = = MODE_INTRA && ! intra_bc_flag[ x0 ][ y0 ] ) { | 
if( PartMode = = PART_2Nx2N && pcm_enabled_flag && !intra_bc_flag[ x0 ][ y0 ] && log2CbSize >= Log2MinIpcmCbSizeY && log2CbSize <= Log2MaxIpcmCbSizeY ) | 
pcm_flag[ x0 ][ y0 ] | ae(v)
…… | 

## Slide 6: Syntax/semantics changes
In prediction_unit()
  Share context modeling of mvp_l0_flag with inter slice
prediction_unit( x0, y0, nPbW, nPbH ) { | Descriptor
if( cu_skip_flag[ x0 ][ y0 ] ) { | 
if( MaxNumMergeCand > 1 ) | 
merge_idx[ x0 ][ y0 ] | ae(v)
} else if (intra_bc_flag[ x0 ][ y0 ]){ /* Intra BC*/ | 
mvd_coding( x0, y0, 2) | 
mvp_l0_flag [ x0 ][ y0 ] | ae(v)
} else { /* MODE_INTER */ | 
…… | 
} | 
} | 

## Slide 7: Simulation results (1)
Anchor: SCM-1.0, lossy coding
 | Test 3.4 release |  | 
 | AI | RA | LD
RGB, text & graphics with motion, 1080p | -3.8% | -1.6% | -0.7%
RGB, text & graphics with motion,720p | -1.9% | -1.2% | -0.3%
RGB, mixed content, 1440p | -1.4% | -0.8% | -0.4%
RGB, mixed content, 1080p | -1.8% | -1.0% | -0.4%
RGB, Animation, 720p | -0.1% | -0.2% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | -4.5% | -1.7% | -0.7%
YUV, text & graphics with motion,720p | -2.4% | -1.5% | -0.4%
YUV, mixed content, 1440p | -1.7% | -0.9% | -0.4%
YUV, mixed content, 1080p | -2.1% | -1.3% | -0.1%
YUV, Animation, 720p | -0.1% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 101% | 99% | 98%
Dec Time[%] | 99% | 102% | 100%

## Slide 8: Simulation results (2)
Anchor: SCM-1.0, lossless coding
 | Test 3.4 release |  | 
 | AI | RA | LD
RGB, text & graphics with motion, 1080p | 1.9% | 0.9% | 0.8%
RGB, text & graphics with motion,720p | 0.2% | 0.1% | 0.1%
RGB, mixed content, 1440p | 0.2% | 0.1% | 0.0%
RGB, mixed content, 1080p | 0.2% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | 2.0% | 0.9% | 0.8%
YUV, text & graphics with motion,720p | 0.3% | 0.1% | 0.1%
YUV, mixed content, 1440p | 0.2% | 0.1% | 0.0%
YUV, mixed content, 1080p | 0.3% | 0.1% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 105% | 98% | 99%
Dec Time[%] | 100% | 99% | 101%

## Slide 9: Conclusion
In this proposal
  AMVP-like prediction, using spatial neighbors to predict the BV of current IntraBC block
  When one or two candidates is not available, preset BV predictor(s) will be used
  BD rate reduction of 3.8%/4.5%, 1.6%/1.7%, 0.7%/0.7% in 1080p TGM class, for AI, RA and LD configurations
Recommend to include in SCM
  Thank Huawei for cross-checking (R0248)!